## Slide 1: Wavefront Skipping using BRAMs for Conditional Algorithms on Vector Processors
Aaron Severance
Joe Edwards
Guy G.F. Lemieux

## Slide 2: VectorBlox MXP Soft Vector Processor (SVP)
Software programmable
1 to 128 parallel ALUs
(4 shown)
Flat scratchpad memory
Vectors at any address,
have any length
2
Notes: Software Compilation Times

## Slide 3: Vectors in Scratchpad Memory
3

## Slide 4: Early Exit Algorithms
Stage 1
Stage 2
Stage 3

## Slide 5: Divergent Control Flow on SVPs
Predication/CMOV
  Process entire vector
Vector Compress
  Load inputs, compress
  Expand outputs, store
Mask Vector:
1’s in corresponding vector are active
0’s are disabled
Wavefronts
(1 per cycle)
Vector
Lanes

## Slide 6: Vector Compress: 5x1 Sliding Window
N*M compress operations (time)
N*M temporary vectors (space)

## Slide 7: Divergent Control Flow on SVPs
Predication/CMOV
  Process entire vector
Vector Compress
  Load inputs, compress
  Expand outputs, store
Compress + Scatter/Gather
  Compress addresses
  Load/store indexed
Density-time
  Scan mask for next valid wavefront
Mask Vector:
1’s in corresponding vector are active
0’s are disabled
Wavefronts
(1 per cycle)
Vector
Lanes

## Slide 8: Wavefront Skipping using BRAMs
Wavefront Number (Offset)
0
1
2
3
4
5
6
7
Mask BRAM
Mask Vector
mask_setup() comparison populates mask BRAM
  Only wavefronts with active elements stored
Masked execution adds offsets from mask BRAM to base

## Slide 9: Code Example
#define STRIDE 5
//Toy functition to double every fifth element in the vector v_a
void double_every_fifth_element( int *v_a, int *v_temp int vector_length ){
int i;
//Initialize every fifth element of v_temp to zero
for( i = 0; i < vector_length; i++ ) {
v_temp[i] = i % STRIDE;
}
//Set the vector length which will be processed
vbx_set_vl( vector_length );
//Set mask for every element equal to zero
vbx_setup_mask( CMOV_Z, v_temp );
//Perform the wavefront skipping operation: multiply all non-masked off
//elements of v_a by 2 and store the result back in v_a
vbx_masked( SVW, MUL, v_a, 2, v_a );
}

## Slide 10: Partial Wavefront Skipping
Notes: Animate, say # of cycles taken

## Slide 11: BRAM Usage for Varying MMVL
Increasing Maximum Masked Vector Length (MMVL):
More wavefronts, more speedup with sparse masks
              Deeper BRAMs needed

## Slide 12: BRAM Usage for Multiple Partitions

## Slide 13: Work Done for Different Strategies

## Slide 14: Different Strategies (Mandelbrot Set)

## Slide 15: Face Detect Results

## Slide 16: Speedup per Area (eALM)

## Slide 17: Varying MMVL (Face Detect)

## Slide 18: Limitations and Future Work
Large area cost for multiple partitions
  Area overhead on V4: 1 partition 4%, 4 partitions 26%
Single mask
  Requires extra instructions to store/restore

## Slide 19: Conclusions
BRAMs used to implement Wavefront Skipping
Wide configurations space
  Full Wavefront Skipping uses <5% more eALMs
  Multiple partitions, longer MMVL can use 100’s of BRAMs
3x higher performance per area on early exit algorithms

## Slide 20: Thank You!