## Slide 1
Rapid Overlay Builder
for Xilinx FPGAs
Michael Yue1, Dirk Koch2, Guy Lemieux1
1University of British Columbia, 2University of Manchester
1

## Slide 2
Motivation
Design productivity barrier: place-and-route (PAR) process
Traditional techniques to accelerate PAR process:
  Parallel compilation
  Netlist preservation
  Trading circuit performance
Speedup obtainable is still limited
2

## Slide 3
Motivation
Design flow using overlay architectures
FPGA Substrate
HDL Code
traditional design flow
LONG PAR PROCESS!
Programmer-friendly Languages
FPGA Substrate
Overlay Architecture
Fast
High-level Synthesis
PAR Process
new design flow
focus of this paper
3

## Slide 4
Contributions
This paper developed a component-based design methodology that:
Obtains scalable speedups in building overlay designs
Achieves high logic utilization level with scalable speedups
Maintains higher and more consistent clock rates compared to ISE
4

## Slide 5
CGRA Architecture – PE
32-bit input/output bus
5-bit personalization bus
Nearest-neighbor communication
Integer operations
  Shifting
  Addition/subtraction
  Comparison
  Multiplication
  Bit manipulation
PE
PE
PE
PE
PE
5

## Slide 6
CGRA Architecture – FPGA Driver
FPGA Driver
HOST
PLATFORM
Communication:
DDR3
Ethernet
PCIe
Purposes:
Streaming application data
Personalization
Partial reconfiguration
6

## Slide 7
ROB Methodology
Step 1 - Resource budgeting
Step 2 - Floorplanning
Step 3 - Building initial PE variants
Step 4 - Extracting PE tiles
Step 5 - Relocating PE tiles
Step 6 - Establishing interconnects
7

## Slide 8
Step 1 - Resource Budgeting
Preliminary understanding of the size of one PE tile
Implementation without applying any physical constraints
Different synthesis options
  Logic-only
  Logic and DSP block
  Logic and BRAM block
  Logic, DSP and BRAM block
8

## Slide 9
Step 2 - Floorplanning
Physically constraining each PE tile in the CGRA
Floorplan
Alternative #1
Floorplan
Alternative #2
Floorplan
Alternative #3
6 PEs
8 PEs
7 PEs
9

## Slide 10
Step 3 - Building Initial PE Variants
PE Variants
  Same functionality
  Different underlying resource footprints
  Determined by the floorplan
  Built to be replicated across the device
10

## Slide 11
Step 3 - Building Initial PE Variants
Placed and routed PE variant
11

## Slide 12
Step 4 - Extracting PE Tiles
Discarding connection anchors
Script:
ClearSelection;
AddBlockToSelection
UpperLeftTile=INT_X1YI LowerRightTile=INT_X2Y2;
ExtractModule
XDL_Input=pe_variant.xdl XDL_Output=pe_tile.xdl;
12

## Slide 13
Step 5 - Relocating PE Tiles
Script:
# Instantiating the left PE column
Set Variable=PE_top Value="220";
SetLabel LabelName=LoopHead_1;
AddBlockToSelection UpperLeftTile=INT_X9Y[%PE_top%-1] LowerRightTile=INT_X9Y[%PE_top%-1];
Set Variable=PE_top Value=[%PE_top%-20];
GotoLabel LabelName=LoopHead_1 Condition=%PE_top%>170;
AddInstantiationInSelectedTiles = PE_Tile_1;
13

## Slide 14
Step 6 - Establishing interconnects
Script:
FuseNets
NetlistName=CGRA PrintProgress=True;
FuseNets
NetlistName=FPGA_Driver PrintProgress=True;
14

## Slide 15
Results
CGRA Size | ROB Methodology Time (seconds) |  |  |  | Speedup | 
 | Initial PE Building | Stitching | XDL Conversion* | Total Time | Use Case 1 | Use Case 2
18 PEs | 1080 | 40 | 69 | 1189 | 2.0x | 22.0x
41 PEs | 1080 | 56 | 210 | 1346 | 2.7x | 13.7x
49 PEs | 1080 | 78 | 277 | 1435 | 3.1x | 12.4x
57 PEs | 1080 | 81 | 377 | 1538 | 3.7x | 12.5x
65 PEs | 1080 | 88 | 449 | 1617 | 3.5x | 10.4x
77 PEs | 1080 | 106 | 695 | 1881 | 5.2x | 12.2x
89 PEs | 1080 | 113 | 844 | 2037 | 4.8x | 10.1x
101 PEs | 1080 | 125 | 1054 | 2259 | 4.9x | 9.3x
Two use cases were evaluated:
* XDL netlist conversion is entirely done using Xilinx tools.
15

## Slide 16
Results
Utilization and Fmax results comparison
Chart: Utilization and Fmax Comparison
| 18.0 | 41.0 | 49.0 | 57.0 | 65.0 | 77.0 | 89.0 | 101.0 | 18.0 | 41.0 | 49.0 | 57.0 | 65.0 | 77.0 | 89.0 | 101.0
Logic Utilization - ROB | 0.30414 | 0.45008 | 0.50096 | 0.55183 | 0.60271 | 0.70143 | 0.76959 | 0.83806
Logic Utilization - ISE | 0.33057 | 0.48124 | 0.54307 | 0.58641 | 0.64642 | 0.73641 | 0.80987 | 0.89116
Fmax - ROB | 120.6855 | 120.6855 | 120.6855 | 120.6855 | 120.6855 | 120.6855 | 120.6855 | 120.6855
Fmax - ISE | 114.9954 | 115.8346 | 88.1213 | 115.3669 | 108.8139 | 108.1315 | 102.5536 | 110.4606
16

## Slide 17
Conclusion
This paper developed the ROB methodology that utilizes (1)module relocation, (2)module variants, and (3)zipping to:
Obtain scalable speedups in building overlay designs
Achieve high logic utilization level with scalable speedups
Maintain higher and more consistent clock rates compared to ISE
17

## Slide 18
Thank you
18