## Slide 1: ME1000 RF CIRCUIT DESIGN
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.
http://dreamcatcher.asia/cw

## Slide 2: 2. Transmission Line Circuits and RF Microwave Network Analysis

## Slide 3: Review of Previous Lecture
In the previous lecture, we have studied how a transmission line (Tline) structure can guide a travelling EM wave.
We have covered the various types of propagation mode for EM waves, in particular, we are interested in the TEM and quasi-TEM mode operation.
In these two modes, the Tline can be represented by a distributed circuit model consisting of the RLCG network; the E-field corresponds to the transverse voltage Vt and the H-field corresponds to the axial current It; Vt and It are also propagating waves in the Tline.
We have also discussed how to derived the RLCG parameters under the low-loss condition.
Finally, in the last section of the previous chapter, we have also studied the design procedure of stripline structures on a printed circuit board.
In this chapter, we are going to study the characteristics of the Tline terminated with impedance, and how to use the Tline in RF microwave circuits and systems.

## Slide 4: 1.0 Terminated Transmission Line Circuit

## Slide 5: Lossless Transmission Line Circuit
A transmission line circuit consists of a source, load networks, and the Tline itself.
We will use the coordinates as shown. Some basic parameters will be derived in the following slides.
Source Network
Load Network
VL
ZL
IL
Tline
Zs
Vs
Vt(z)
It(z)
l
+z
z = 0
z = –l
The
schematic
The physical
system

## Slide 6: Voltage and Current on the Transmission Line Circuit
Assumption: Tline is lossless (=0), and is supporting the TEM mode.
At a position z along the Tline:
At z = 0:
(1.1a)
VL
l
+z
z = 0
Towards
source
ZL
IL
Z= –l
Incident V and I waves
Reflected
waves
Incident and reflected waves combine to produce load voltage and current
Using the definition
of Zc
(1.1b)

## Slide 7: Reflection Coefficient
The ratio of Vo– over Vo+ is described by a voltage reflection coefficient . At the load end, a subscript ‘L’ is inserted to denote that this is the ratio at load impedance:
Using (1.1b):
Similarly we could also derive the current reflection coefficient:
(1.2a)
(1.2b)
(1.2d)
(1.2c)
ZL
or

## Slide 8: Reflection Coefficient (cont’d)
At a distance l from the load, the voltage reflection coefficient is given by:
Note that this equation is only valid when the z = 0 reference is at the load impedance, AND l is always positive.
From now on, we will deal exclusively with voltage reflection coefficient.
(1.2e)
ZL
z = 0
z
z = -l
l
This product is usually called
electrical length, is given a
unit of radian or degree

## Slide 9: Reflection Coefficient (cont’d)
Ensure you know the physical implications of the reflection coefficient for various load impedance values.
z
z = 0
Zc
Zc
z
z = 0
ZL=0
Zc
z
z = 0
ZL
Zc
z
z = 0
ZL=R+jX
Zc

## Slide 10: Why Does Reflection Occur?
VL
z
z = 0
ZL
IL
At z = 0:
If Zc  ZL then
Assuming that IL < Io+, electric charges pile up at the Tline and load intersection. Since like charges repel each other, this forces the excess electric charge to flow back to the Tline. This constitutes the reflected current. From our understanding of the Tline theory, if there is current, there
is also associated voltage, hence
a reflected voltage and current
wave occurs.
Extra
Note that the total voltage at the Tline-load
intersection is Vo+ + Vo– = VL. Thus the current
drawn by load ZL will also increase from original
value of Vo+/ZL until equilibrium (Io+ - Io- = IL) is reached.

## Slide 11: Why Does Reflection Occur? (cont’d)
We can visualize the current flow as due to positive charges (conventional current).
When Io+ > IL
When Io+ < IL
IL
Io+
Io+
IL
–Io–
Tline
Tline
Load impedance
Load impedance
The Tline supplies more charges
per unit time than the load can absorb
so excess positive charges are reflected back
Positive
charge
Negative
charge
–(– Io–)
At the interface, positive and negative charge pairs
are created. The positive charge flows into the
load, while the negative charge flows back to the
source, constituting the reflected current
with negative polarity.
Of course there are only free
electrons in the conductor. When
a region is said to contain
positive charge, it actually
has less free electrons as
compared to the equilibrium state.
Extra

## Slide 12: Power Delivered to the Load Impedance
Power to load:
Thus when L = 0, all incident power is absorbed by ZL. We say that the load is matched to the Tline. Otherwise there will be reflected power in the form of:
The maximum power to the load is called the incident power Pinc:
Let Zc be real
(1.3)
ZL
Pinc
Pr
PL
Pincident
Preflected

## Slide 13: Impedance Matching
Thus the purpose of impedance matching is to reduce reflection from both the load and the source.
We strive to get maximum power from the source and transport this power (the available power) to the load.
In other words, impedance matching provides a ‘smooth’ flow of the EM wave along a system of interconnect.
Impedance matching – Make |L | 0

## Slide 14: Voltage Standing Wave Ratio (VSWR)
At any point z along the Tline:
Expressing Lin polar form
The ratio of maximum |V| to minimum |V| is known as VSWR.
(1.5)
(1.4)
Argand
Diagram
1
0
Re
Im
ZL

## Slide 15: Voltage Standing Wave Ratio (cont’d)
A similar expression can be obtained for I(z):
VSWR measures how good the load ZL is matched to the Tline. For a good match,  = 0 and VSWR=1. For a mismatch load,  >0 and VSWR >1.
We can view the incident and reflected waves as interfering with each other, causing standing wave along the Tline.
A similar phenomenon also exists in the waveguide, however the E- and H-field standing waves are being measured, so generally the alphabet ‘V’ is dropped when dealing with the waveguide.
Why is SWR popular ? – In the early days, waveguides are widely used, and a simple way to measure SWR is to use the slotted line waveguide with a diode detector.
(1.6)

## Slide 16: Example 1.1
A Tline has two conductors and is filled with air. A sinusoidal voltage of 2 V magnitude and 3.0 GHz frequency is launched into the Tline. The characteristic impedance of the Tline is 50 Ω and one end of the Tline is terminated with load impedance ZL=100+j100 @3.0 GHz. Assume phase velocity = C, the speed of light in vacuum.
  Find the load reflection coefficient L.
  Find the power delivered to the load ZL.
  Plot |V | and |I | versus l, the distance from ZL.
  Determine the VSWR of the system.
l
z
z = 0
ZL
Zc
Zc=50
2<0o

## Slide 17: Example 1.1 (cont’d)
The solution (as calculated using MathCAD):

## Slide 18: Example 1.1 (cont’d)
Plotting out the voltage and current phasor along the transmission line:
Magnitudes of V and I
are plotted using (1.4) and (1.6)
Note that |V | and |I | are always quarter wavelength or 90o out of phase. The values of |V | and |I | repeat themselves every half
wavelength or 180o.
l
ZL
|V(l)|
|I(l)|
z
ZL
Zc=50
Voltage phasor
magnitude
Normalized current
phasor magnitude
Distance in terms
of wavelength 

## Slide 19: Input Impedance of a Terminated Tline
Use (1.2b)
(1.7a)
At any length l from the termination impedance, we can compute the impedance looking towards the load:
ZL
Zc
l
Zin(l)
(1.7b)

## Slide 20: Special Cases of Terminated Lossless Tline
When ZL=0:
When ZL
l
z
z = 0
ZL=0
Zc
l
z
z = 0
Zc
(1.8a)
(1.8b)
ZL=0

## Slide 21: Special Cases of Terminated Lossless Tline (cont’d)
Zc
L
Reactance
Zc
Susceptance
A length of shorted Tline can be used to
synthesize an inductor or reactance, while a length of opened Tline can be used to
synthesize a capacitor or susceptance, within a limited range of frequency (l < /2) or (f < vp/(4l)).
l
X
0
B
l
0
This area corresponds to
l < /2, or l < /4
l

## Slide 22: Special Cases of Terminated Lossless Tline (cont’d)
Zc
Zc
A length of shorted Tline can be used to
approximate a parallel LC resonator, while
a length of opened Tline can be used to
approximate a series LC resonator.
Cp
Lp
Z
Cs
Ls
Z
l
X
0
B
l
0

## Slide 23: Example 1.2
A lossless Tline of length l = 10 cm supports the TEM propagation mode. The per unit length L and C are given as L = 209.4 nH/m, C = 119.5 pF/m. The Tline is terminated with a series RL load impedance:
Plot the real and imaginary parts of Zin from f = 1.0 GHz to 4.0 GHz.
2.5 nH
120
10 cm
ZL

## Slide 24: Example 1.2 (cont’d)
Note that the pattern of the waveform repeats
at an interval of close to 1 GHz, this is due to
the periodic nature of the tan(l) function.
n=1,2,3,4…
frequency

## Slide 25: Cascading Transmission Lines: Transmission Coefficient
z = 0
Zc1
Zc2
ZL=Zc2
Zc2
Using
(1.9)
At z = 0:
Matched termination

## Slide 26: Relationship Between Reflection and Transmission Coefficients
Tline1
Tline2 or a load impedance
V1+
V1–
V2+
Zc
ZL
(1.10)

## Slide 27: Power Relations
Zc1
Zc2
Pinc
Pref
Ptr
Pinc = Pref + Ptr

## Slide 28: Return Loss and Insertion Loss
Sometimes both voltage reflection and transmission coefficients are expressed in dB, these are then termed return loss (RL) and insertion loss (IL).
2 -Port
Zc2
Zc2
Zc1
Zc1
Vs
(1.11a)
(1.11b)

## Slide 29: Example 1.3
Find the return loss (RL) and insertion loss (IL) at the intersection between the Tlines. Assume the TEM propagation mode is at f = 1.9 GHz for both Tlines, Z1 =100, Z2 =50.
z
z = 0
Z1
Z2
0.05
Zin
z = –0.05
Interface
z
Z1

## Slide 30: Example 1.3 (cont’d)
z
z = 0
Z1
Z1
Z2
0.05
Zin

## Slide 31: Exercise 1.1
For a transmission line terminated with a short circuit:
From Example 5.1 (Chapter 1):
We would like to use a short length of transmission line to implement a reactance of X = 60 at 2.4 GHz. Show how this can be done using the microstrip line of Example 5.1, Chapter 1 – Advanced Transmission Line Theory. Hint: Use equation (1.8a).
9.24 mm
A number of plated through
holes to reduce the parasitic
inductance of the short.
Top
View
2.86 mm
1.57 mm
r=4.7 r=1.0
Zc  50
vp = 1.591x108
From Example 5.1,
Chapter 1:

## Slide 32: Terminated Lossy Tline
In the case of a lossy Tline, we replace j with  =  + j in equations (1.2) to (1.9). As seen from equation (2.7) (Advanced Transmission Line Theory), the characteristic impedance Zc becomes a complex value too.
Furthermore:
The losses have the effect of reducing the standing wave ratio SWR towards unity as the point of observation is moved away from the load towards the generator.
Most of the time the losses are so small that for the short length of Tline, the neglect of  is justified. However as frequency increases beyond 3 GHz, the skin effect and dielectric loss become important for the typical PCB dielectric and conductor.
(1.12)
Extra

## Slide 33: Terminated Lossy Tline (cont’d)
(1.13)
Loss due to incident wave
Loss due to reflected wave
Power delivered increases as we
proceed towards the generator!
At some point z = –l from the load-Tline interface, the power directed towards the load is:
Of the power given by (1.11), the power dissipated by the load is given by (1.3), the remainder is dissipated by the lossy line.
Extra

## Slide 34: Exercise 1.2
Considering a transmission line circuit below, determine Vin and VL.
Thus
Solving for Vo+:
VL
ZL
IL
Tline
Zs
Vin
Vt(z)
It(z)
+
-
Vs
Zc , 
z
0
Zin
l

## Slide 35: Exercise 1.2 (cont’d)
Knowing Vo+ , we can find Vin and VL:

## Slide 36: Demo: Transmission Line Simulation Exercise
Extra

## Slide 37: 2.0 Smith Chart and Its Applications

## Slide 38: Introduction
In analyzing electrical circuits, one very important parameter is the impedance Z or admittance Y seen at a terminal/port.
For time-harmonic circuits, Z or Y is dependent on the frequency and a complex value.
To visualize the arbitrary Z or Y value, we would need an infinite 2D plane:
R
X
0
Z = R + jX
Z = V/I = R + jX
Y = I/V = G + jB
Resistance
Reactance
Conductance
Susceptance

## Slide 39: Introduction (cont’d)
In RF circuit design, we can represent an impedance Z = R + jX in terms of its reflection coefficient with respect to a reference impedance (Zo):
Usually we would take Zo = Zc , the characteristic impedance of a Tline in the system.
 is also a complex value, however we have learnt that its magnitude is always < 1 for a passive impedance value.
Effectively if the reflection coefficient is plotted, all possible passive Z and Y values can be fitted into a finite 2D area.
–1
0
–1
1
1
Re()
Im()
Region for
passive Z or Y

## Slide 40: Introduction (cont’d)
To facilitate the evaluation of the reflection coefficient, a graphical procedure based on conformal mapping is developed by P.H. Smith in 1939.
This procedure, now known as the Smith Chart permits an easy and intuitive display of reflection coefficient  as well as impedance Z and admittance Y in one single graph.

## Slide 41: Introduction (cont’d)
An example of software Smith Chart with the impedance (Z) and admittance (Y) coordinate lines.
winRF CAD V0.78 by F.Kung (2007)

## Slide 42: Formulation
Let z = r + jx and  = U + jV:
Then
Equating real and imaginary parts:
Equation of circles for U and V:
Depends only on r (r circle)
Depends only on x (x circle)
Extra

## Slide 43: Formulation (cont’d)
jV
U
–1
1
–1
1
r circles
x circles
The complex plane
for reflection coefficient :
||=1
Extra
Imaginary axis
Real axis

## Slide 44: Formulation (cont’d)
Note that:
Let y = g + jb and  = U + jV:
Again proceeding as before we obtain:
Depends only on g (g circle)
Depends only on b (b circle)
Extra

## Slide 45: Formulation (cont’d)
jV
U
–1
1
–1
1
g circles
b circles
Extra

## Slide 46: Complete Smith Chart with r, x, g, and b circles
R=50
R=100
R=200
X=10
X=30
X= –10
X= –30
R and X
circles
G circles
+B circles
–B circles

## Slide 47: Smith Chart Example 1
Zo = 50 
Z = 50 + j0

## Slide 48: Smith Chart Example 2
Zo = 50 
Z = 50 + j30
Z = 50 – j30
Z
50
j30
R=50 circles
X=30 circles
X= –30 circles
Z
50
j30

## Slide 49: Smith Chart Example 3
Zo = 50 
Z = 100 + j30
Z
100
j30
Question: What would
you expect if the real part
of Z is negative ?

## Slide 50: Smith Chart Example 4
Zo = 50 
Z = 50//(–j40) or
Y = 0.020 + j0.025
Y
0.02
j0.025
B
G
Z
50
–j40
X
R
B =0.025 circle
G =0.02 circle

## Slide 51: Smith Chart Example 5
Zo = 50 
Z = 50//(j40) or
Y = 0.020 – j0.025
Z
50
j40
X
R
Y
0.02
–j0.025
B
G
G = 0.02 circle
B = –0.025 circle

## Slide 52: Smith Chart Summary
Thus a point on a Smith Chart can be interpreted as reflection coefficient .
It can also be read as impedance Z = R + jX.
It can also be read as admittance Y = G + jB.
Z = 30 + j20
Y = 0.023 – j0.015
 = 0.34<2.11

## Slide 53: Smith Chart Summary (cont’d)
When we add a reactance in series with Z, the point on the Smith Chart will move in such a way that it remains on the constant R circle.
When we add a susceptance in parallel to Y, the point on the Smith Chart will move in such a way that it remains on the constant G circle.
Z = 30+j20
Y = 0.023–j0.015
Y = 0.023–j0.015
 jB
Z = 30+j20  jX
+X
–X
+B
–B
jB
Y
jX
Z
Zin = ZL + jX
= RL + j(XL + X)
Yin = YL + jB
= GL + j(BL + B)

## Slide 54: Smith Chart Example 6
In this example we would like to observe the locus of impedance Zin as l is changed for ZL = 200 + j0 (Say at a certain operating frequency fo).
Recalling equations (1.2d) and (1.7) in this chapter:
l
z
z = 0
ZL= 200 + j0
Zc
Vs<0o
Zin , in
Tline with  and Zc = 50
with
where  is the wavelength

## Slide 55: Smith Chart Example 6 (cont’d)
Locus for in
(the SWR circle)
Direction
away from
load or towards
generator
Direction
away from
generator
or towards load
The locus in which
|in| is constant is also
known as the constant
SWR circle (as the
SWR depends on the
magnitude of the reflection coefficient).

## Slide 56: Typical Applications of the Smith Chart
The Smith Chart is used in impedance transformation and impedance matching. Although this can be performed using an analytical method, using a graphical tool such as the Smith Chart allows us to visualize the effect of adding a certain element in the network. The effective impedance of a load after adding a series, shunt, or transmission line section can be read out directly from the coordinate lines of the Smith Chart.
The Smith Chart is used in the RF active circuit design, e.g., when designing amplifiers. Usually certain contours in the form of circles are plotted on the Smith Chart.
2-port network parameters such as s11 and s22 are best viewed in the Smith Chart.

## Slide 57: Typical Applications of the Smith Chart (cont’d)
Classically the Smith Chart can also be used to find the position along the transmission line with maximum and minimum voltage or current.
ZL
Zc , 
Zc
z
z=0
z=-l
When voltage has
maximum magnitude
When voltage has
minimum magnitude

## Slide 58: Exercise 2.1: Impedance Transformation
Employing the software fkSmith (http://pesona.mmu.edu.my/~wlkung/), find a way to transform a load impedance of ZL = 10 + j75 into Z = 50 using either the lumped L, C, or section of the Tline. Assume an operating frequency of 1.8 GHz.
Zc
ZL=10+ j75
Vs<0o
2-port network
Z = 50

## Slide 59: 3.0 Practical Considerations for Stripline Implementation

## Slide 60: Practical Transmission Line Design and Discontinuities
Discontinuities in the Tline are changes in the Tline geometry to accommodate layout and other requirements on the printed circuit board.
Virtually all practical distributed circuits, whether in the waveguide, coaxial cables, microstrip line etc. must inherently contain discontinuities. A straight uninterrupted length of the waveguide or Tline would be of little engineering use.
The following discussion considers the effect and compensation for discontinuities in the PCB layout. This discussion is restricted to TEM or quasi-TEM propagation modes.

## Slide 61: Practical Transmission Line Discontinuities Found in PCB
Ground plane gap
trace
plane
gap
trace
ground plane
Bend
bend
Socket-trace interconnection
socket
pin
trace
via
Via
plane
cylinder
trace
pad
Junction
Bend
Line to Component
Interface
Step
Open
Here we illustrate the
discontinuities using the
microstrip line. Similar
structures also apply to
other transmission line
configurations.

## Slide 62: Practical Transmission Line Discontinuities Found in PCB (cont’d)
Further examples of microstrip and co-planar line discontinuities.
Gap
Pad or Stub
Coupled lines
Examples of bend and via
on co-planar Tline

## Slide 63: Discontinuities and EM Fields
Introduction of discontinuities will distort the uniform EM fields present in the infinite length Tline. Assuming the propagation mode is TEM or quasi-TEM, the discontinuity will create a multitude of higher modes (such as TM11 , TM12 , TE11 , …) in its vicinity in order to fulfill the boundary conditions. (Note: There is only one type of TEM mode!!)
Most of these induced higher order modes are evanescent or non-propagating as their cut-off frequencies are higher than the operating frequency of the circuit. Thus the fields of the higher order modes are known as local fields.
The effect of discontinuity is usually reactive (the energy stored in the local fields is returned back to the system) since loss is negligible.
The effect of the reactive system to the voltage and current can be modeled using LC circuits (which are reactive elements).
For the TEM or quasi-TEM mode, we can consider the discontinuity as a 2-port network containing inductors and capacitors.

## Slide 64: Discontinuities and EM Fields (cont’d)
Modeling a discontinuity using a circuit theory element such as RLCG is a good approximation for operating frequency from 6 – 20 GHz. This upper limit depends on the size of the discontinuity and dielectric thickness.
The smaller the dimension of the discontinuity as compared to the wavelength, the higher will be the upper usable frequency.
As an example, the 2-port model for microstrip bend is usually accurate up to 10 GHz.
A
A’
B’
B
0.25
0.25
Minimum distance
A
A’
B
B’
2-port
network
0.25

## Slide 65: Discontinuities and EM Fields (cont’d)
E.g., for a microstrip bend, below is a snapshot of the EM fields at a particular instance in time:
Non-TEM mode
field here*
Quasi-TEM
field
H-field
E-field
*This field can be decomposed into
TEM and non-TEM components
Direction of propagation

## Slide 66: Microstrip Line Discontinuity Models
Open:
Cf
The open end of a stripline contains a fringing E-field.
This is manifested as capacitor Cf . Cf gives the effect
of slightly increasing the phase of the input
impedance.
The approximate value of Cf has been derived by P. Silvester and P. Benedek from the
EM fields of an open-end structure using numerical method and curve fitted as follows:
[Source: P. Silvester and P. Benedek,”Equivalent capacitances
of microstrip open circuits”, IEEE Trans. MTT-20, No. 8
August 1972, pp. 511 – 576]
(3.1)
h=dielectric thickness
W=width

## Slide 67: Microstrip Line Discontinuity Models (cont’d)
Assuming the effect of Cf can be represented by a short length of the Tline:
Thus in the microstrip Tline design, we need to fore-shorten the actual physical length by leo to compensate for the fringing E-field effect.
(3.2)
Zc
Cf
Zc
leo
Zf
Zeo
Extra

## Slide 68: Microstrip Line Discontinuity Models (cont’d)
Shorted via or through-hole:
(3.3a)
Ls in nH
Cp in pF
h in mm
d and d2 in mm
r = dielectric constant of PCB
N = number of GND planes
(3.3b)
Cp/2
Ls
Cp/2
This is the capacitance between the via and
internal plane. If there are multiple internal
conducting planes, then there should be one
Cp corresponding to each internal plane.
Cross section
of a via
h
d = via diameter
GND planes
d2

## Slide 69: Microstrip Line Discontinuity Models (cont’d)
C1
C2
C1
T1
T2
Gap:
See Chapter 5, T.C. Edwards, “Foundation
for microstrip circuit design” [4], or
B. Easter, “The equivalent circuit of some microstrip
discontinuities”, IEEE Trans. Microwave Theory and Techniques
vol. MTT-23 no.8 pp 655-660,1975.

## Slide 70: Microstrip Line Discontinuity Models (cont’d)
90o Bend:
L
C
L
Approximate quasi-static expressions for L1, L2, and C:
T2
T1
w
for
for
(3.4)
r = dielectric constant of the substrate,
assumed to be non-magnetic.
d = thickness of the dielectric in meter.

## Slide 71: Example 3.1: Microstrip Line Bend
For a 90o microstrip line bend, with w = 2.8 mm, d = 1.57 mm, r = 4.2, find the values of L and C.
0.30 pF
18.05 pH
18.05 pH
At 1 GHz:
Reactance of C:
Reactance of L:
Typically the effect of bend is not
important for frequency below 1 GHz
This is also true for discontinuities like
step and T-junction.

## Slide 72: Microstrip Line Discontinuity Models (cont’d)
Step:
L1
C
L2
T2
T1
w2
w1
Approximate quasi-static expressions for L1, L2, and C:
Lm1 and Lm2 are the per unit length
inductance of T1 and T2 respectively.
for
for
(3.5)

## Slide 73: Microstrip Line Discontinuity Models (cont’d)
T-Junction:
T1
T3
T2
L1
C1
L1
T1
T2
T3
L3

## Slide 74: Effect of Discontinuities
Looking at the equivalent circuit models for the microstrip discontinuities, the sharp reader will immediately notice that all these networks can be interpreted as Low Pass Filters. The inductor attenuates electrical signal at high frequency while the capacitor shunts electrical energy at high frequency.
Thus the effect of having too many discontinuities in a high-frequency circuit reduces the overall bandwidth of the interconnection.
Another consequence of discontinuity is attenuation due to radiation from the discontinuity.
f
|H(f)|
0
f
|H(f)|
0

## Slide 75: Some Intuitive Concepts on Discontinuities
Looking at the equivalent circuit models on the previous slides, one can’t help but wonder how does one know which model to use for which discontinuity?
The answer can be obtained by understanding the relationship between electric charge, electric field, current, magnetic flux linkage, and quantities such as inductance and capacitance.
A few observations are crucial:
  As current encounters a bend, the flow is interrupted and the current is reduced. Moreover there will be accumulation of electric charges at the vicinity of the bend because of the constricted flow.
  As current encounters a change in the Tline width, the flow of charge either accelerates or decelerates.

## Slide 76: Intuitive Concepts
Excess charge – whenever there is constricted flow or a sudden enlargement of the Tline geometry, electric charge will accumulate. The amount of charge greater than the charge distribution on an infinite length of the Tline is known as excess charge. The excess charge can be negative. Associated with excess charge is a capacitance.
Excess flux – similarly in constricted flow or ease of flow, change in the Tline geometry also results in excess magnetic flux linkage. The amount of flux linkage greater than the flux linkage on an infinite length of the Tline is known as excess flux. This excess flux is associated with an inductance, again the excess flux can be negative although it is usually positive (inductance always corresponds to resistance in current flow; recall V = L(di/dt)).

## Slide 77: Intuitive Concepts
Both excess charge and excess flux can be computed from the higher order mode EM fields in the vicinity of the discontinuity. For instance, by subtracting the total E-field from the normal E-field distribution for an infinite Tline, we would obtain the higher order mode E-field (or local E-field). From the boundary condition of the local E-field with the conducting plate, the excess charge can be calculated. A similar procedure is carried out for excess flux.
This argument although refers to the stripline, is also valid for the coaxial line and waveguide in general.
Usually numerical methods are employed to determine the total E-field and H-field at the discontinuity; it is assumed the fields are quasi-static.

## Slide 78: Intuitive Concepts (cont’d)
E.g., in a bend, as current approaches point B, the current density changes. We can imagine that current flows easily in the middle as compared to near the edges. As a result, the flux linkage at B for both T1 and T2 increases as compared to the flux linkage when there is no bend. Associated with the excess flux, we introduce two series inductors, L1 and L2. The inductance values are similar if T1 and T2 are similar in geometry.
Also at B, more positive electric charges (we think in terms of conventional charge) accumulate as compared to the charge distribution for an infinite Tline. Thus we associate capacitance C1 at B.
L1
C1
L2
B
T1
T2
Harder to flow
Easier to flow
Constricted flow – L
Increased flow – C
Charge accumulation – C

## Slide 79: Exercise 3.1
What do you expect the equivalent circuit of the following discontinuity to be ?

## Slide 80: Methods of Obtaining the Equivalent Circuit Model for Discontinuities
Three typical approaches…
Method 1: Analytical solution – see Chapter 4, Ref. [3] on Model Analysis for waveguide discontinuities.
Method 2: Numerical methods such as
  Method of Moments (MOM)
  Finite-Element Method (FEM)
  Finite Difference-Time Domain Method (FDTD)
  And many others
Numerical methods are used to find the quasi-static EM fields of a 3D model containing the discontinuity. The EM field in the vicinity of the discontinuity is split into TEM and non-TEM fields. LC elements are then associated with the non-TEM fields using a formula similar to (3.1) in Part 3.
Agilent’s Momentum
Ansoft’s HFSS™
CST’s Microwave
Studio®
Sonnet™

## Slide 81: Methods of Obtaining the Equivalent Circuit Model for Discontinuities (cont’d)
Method 3: Fitting measurements with circuit models. By proposing an equivalent circuit model, we can try to tune the parameters of the circuit elements in the model so that frequency/time domain response from theoretical analysis and measurement match.
Measurements can be done in the time domain using time-domain reflectometry (TDR), and in the frequency domain measurement using a vector network analyzer (VNA).

## Slide 82: Radiation Loss from Discontinuities
At a higher frequency, say >5 GHz, the assumption of lossless discontinuity becomes flawed. This is because the higher order mode EM fields can induce surface wave on the printed circuit board; this wave radiates out so energy is loss.
Furthermore the acceleration or deceleration of electric charge also generates radiation.
The losses due to radiation can be included in the equivalent circuit model for the discontinuity by adding series resistance or shunt conductance.

## Slide 83: Reducing the Effects of Discontinuity
To reduce the effect of discontinuity, we must reduce the values of the associated inductance and capacitance. This can be achieved by decreasing the abruptness of the discontinuity, so that current flow will not be disrupted and charge will not accumulate.
Chamfering of bends
W
b
For a 90o bend:
The optimum chamfering is
observed to be b=0.57W
W
1.42W
W
W

## Slide 84: Reducing the Effects of Discontinuity (cont’d)
T2
T1
Mitering of junction
Mitering of step
T1
T3
T2
W2
W1
 0.7W1
T1
T3
T2
W2
W1
 2W2
0.5W2 or
smaller

## Slide 85: Connector Discontinuity: Coaxial – Microstrip Line Transition
Since most microstrip lines invariably lead to external connection from the printed circuit board, an interface is needed. Usually the microstrip line is connected to a co-axial cable.
An adapter usually used for microstrip to co-axial transition is the SMA-to-PCB adapter, also called the SMA end-launcher.

## Slide 86: Connector Discontinuity: Coaxial – Microstrip Line Transition (cont’d)
Again the co-axial-to-microstrip transition is a form of discontinuity, care must be taken to reduce the abruptness of the discontinuity. For a properly designed transition such as the one shown in the previous slide, the operating frequency could go as high as 6 GHz for the co-axial-to-microstrip line transition and 9 GHz for the co-axial-to-co-planar line transition.
Extra

## Slide 87: Exercise 3.2
Explain qualitatively the effect of compensation on the equivalent electrical circuits of the discontinuity in the previous slides.

## Slide 88: Example 3.2
A Zc = 50 Ω microstrip Tline is used to drive a resistive termination as shown. Sketch the equivalent electrical circuit for this system.
Extra
Top view

## Slide 89: 4.0 Linear RF Network Analysis: 2-Port Network Parameters

## Slide 90: Network Parameters
Many times we are only interested in the voltage (V) and current (I) relationship at the terminals/ports of a complex circuit.
If mathematical relations can be derived for V and I, the circuit can be considered as a black box.
For a linear circuit, the I-V relationship is linear and can be written in the form of matrix equations.
A simple example of a linear 2-port circuit is shown below. Each port is associated with two parameters, V and I.
Port 1
Port 2
R
C
V1
I1
I2
V2
Convention for positive
polarity current and voltage
+
–

## Slide 91: Network Parameters (cont’d)
For this two-port circuit, we can easily derive the I-V relations.
We can choose V1 and V2 as the independent variables, the I-V relation can be expressed in matrix equations.
2-Port
I2
V2
V1
I1
Port 1
Port 2
R
C
V1
I1
I2
V2
Network parameters
(Y-parameters)
C
I1
I2
V2
jCV2
R
V1
I1
V2

## Slide 92: Network Parameters (cont’d)
To determine the network parameters, the following relations can be used:
For example to measure y11, the following setup can be used:
This means we short-circuit the port
2-Port
I2
V2 = 0
V1
I1
or
Short-circuit

## Slide 93: Network Parameters (cont’d)
By choosing different combinations of independent variables, different network parameters can be defined. This applies to all linear circuits no matter how complex.
Furthermore this concept can be generalized to more than two ports, called N-port networks.
2-Port
I2
V2
V1
I1
V1
V2
I1
I2
H-parameters
Z-parameters
Linear circuit, because all
elements have linear I-V relation

## Slide 94: ABCD Parameters
(4.1a)
(4.1b)
2-Port
I2
V2
V1
I1
Take note of the direction of
the positive current!
Of particular interest in RF and microwave systems is the ABCD parameters. ABCD parameters are the most useful for representing the Tline and other linear microwave components in general.
Short-circuit Port 2
Open-circuit Port 2

## Slide 95: ABCD Parameters (cont’d)
The ABCD matrix is useful for characterizing the overall response of the 2-port networks that are cascaded to each other.
I2’
V2
V1
I1
I2
V3
I3
Overall ABCD matrix

## Slide 96: ABCD Parameters of Some Useful 2-Port Networks
Z
Y
(4.2a)
(4.2b)
 , Zc
l
(4.2c)
2-Port
I2
V2
V1
I1

## Slide 97: Example 4.1
Derive the ABCD parameters of an ideal transformer.
1:N
Hints: For an ideal transformer, the following relations for terminal voltages and currents apply:
Port 1
Port 2
Extra

## Slide 98: Exercise 4.1
Derive equations (4.2a), (4.2b), and (4.2c).
Hint: For the Tline, assume the voltage and current on the Tline to be the superposition of incident and reflected waves. Also let the terminals at port 2 correspond to z = 0 (assuming propagation along the z-axis).

## Slide 99: Partial Solution for Exercise 4.1
Case1: For I2= 0 (open-circuit port 2), L= 1, thus:
For (4.2c)…
First we note that for the terminated Tline, voltage and current along the z-axis
are given by:
Thus
 , Zc
l
Vs
z=0
z
y
V1
V2

## Slide 100: Partial Solution for Exercise 4.1 (cont’d)
 , Zc
l
Vs
Case 2: For V2= 0, L = –1.
Proceeding in a similar manner, we would be able to obtain the B and D terms.

## Slide 101: Exercise 4.2
Z1
Y
Z2
Hint: Consider each element as a 2-port network.
Find the ABCD parameters of the following network:

## Slide 102: Conversion Between ABCD and Z,Y Parameters for 2-Port Networks
By employing the definition of Z, Y and ABCD parameters for 2-port networks, we can easily show the following conversion formula between parameters.
From ABCD to Z:
From Z to ABCD:
Between Z and Y parameters:
(4.3a)
(4.3b)
(4.3c)

## Slide 103: S-Parameters: Why Do We Need Them?
Usually we use the Y, Z, H, or ABCD parameters to describe a linear 2-port network.
These parameters require us to open or short a network to find the parameters.
At radio frequencies, it is difficult to have a proper short- or open-circuit; there are parasitic inductance and capacitance in most instances.
Open and short conditions lead to standing wave, which can cause oscillation and destruction of the device.
For the non-TEM propagation mode, it is not possible to measure voltage and current. We can only measure power from E- and H-fields.

## Slide 104: S-Parameters
Hence a new set of parameters (S) is needed which
  Do not need open/short condition.
  Do not cause standing wave.
  Relates to incident and reflected power waves, instead of voltage and current.
As opposed to V and I, S-parameters relate to the reflected and incident
voltage waves.
S-parameters have the following advantages:
1. Relates to familiar measurements such as reflection coefficient,
gain, loss, etc.
2. Can cascade S-parameters of multiple devices to predict system
performance (similar to the ABCD parameters).
3. Can compute Z, Y, or H parameters from S-parameters if needed.

## Slide 105: Normalized Voltage/Current Waves
Consider an n-port network:
Each port is considered to be
connected to a Tline with
specific Zc.
Linear
n-port
network
Tline or
waveguide
Port 2
Port 1
Port n
Reference plane
for the local z-axis
(z = 0)
Zc2
Zc1
Zcn
z
z=0

## Slide 106: Normalized Voltage/Current Waves (cont’d)
There are voltage and current on each port.
This voltage (or current) can be decomposed into the incident (+) and reflected (–) components.
V1+ V1–
Linear
n-port
network
Port 2
Port 1
Port n
z = 0
V1
I1
+z
Port 1

V1
V1+
+
–
V1–
+

## Slide 107: Normalized Voltage/Current Waves (cont’d)
The port voltage and current can be normalized with respect to the impedance connected to it.
It is customary to define the normalized voltage waves at each port as:
(4.4a)
Normalized
incident waves
Normalized
reflected waves
(4.4b)
i = 1, 2, 3 … n

## Slide 108: Normalized Voltage/Current Waves (cont’d)
Thus in general:
Vi+ and Vi– are propagating
voltage waves, which can
be the actual voltage for TEM
modes or the equivalent
voltages for non-TEM modes.
(for non-TEM, V is defined as
proportional to the transverse E-field while I is defined as proportional to the transverse H-field).
a2
b2
a1 b1
an
bn
Linear
n-port
Network
Tline or
waveguide
Port 2
Port 1
Port n
Zc1
Zc2
Zcn

## Slide 109: Scattering Parameters
If the n-port network is linear (make sure you know what this means!), then there is a linear relationship between the normalized waves.
For instance, if we energize Port 2:
a2
b1
bn
Port 2
Port 1
Port n
Zc1
Zc2
Zcn
b2
Linear
n-port
network
Constant that
depends on the
network construction
In a nutshell: Linearity
When a sinusoidal EM wave
is injected into one port,
sinusoidal EM waves of similar
frequency are generated out
of all ports.

## Slide 110: Scattering Parameters (cont’d)
Considering that we can send energy into all ports, this can be generalized to:
Or written in a Matrix equation:
Where sij is known as the generalized Scattering (S) parameter, or just S-parameters for short. From (4.4), each port i can have different characteristic impedance Zci.
(4.5a)
(4.5b)
or

## Slide 111: Linear Relation Between ai and bi
That ai and bi are related linearly can be proved using Green’s Function Theory for partial differential equations.
Extra

## Slide 112: S-Parameters for 2-Port Networks
(4.6a)
(4.6b)
For 2-port networks, (4.5) reduces to:
Note that ai = 0 implies that we terminate the ith port with its characteristic impedance.
Thus zero reflection eliminates the standing wave.
Good termination can be established reliably for RF and Microwave frequencies in a number of transmission system. This will be illustrated in the following slides.

## Slide 113: Measurement of the S-Parameter for 2-Port Networks
2-Port
Zc2
Zc2
Zc1
Zc1
Vs
a1
b1
b2
b1
2-Port
Zc1
Zc2
Zc1
Zc2
Vs
b2
a2
Measurements for s11 and s21:
Measurements for s22 and s12:

## Slide 114: Example of Terminations
DIY 50 Ω Termination for grounded
co-planar Tline
2  100 Ω SMT resistor
(0603 package, 1% tolerance)
Another example
of broadband
50 Ω co-axial
termination
–20 dB
0 dB
Measured s11 from 10 MHz to 3 GHz
using Agilent’s 8753ES VNA
OSL calibration
performed on Port 1

## Slide 115: Practical Measurement of S-Parameters
Vector Network Analyzer (VNA) – an instrument that can measure the magnitude and phase of S11, S12, S21, S22.
An example of a VNA by
Agilent Technologies.
Other manufacturers
of the VNA are Advantek,
Wiltron, Anritsu, Rhode &
Schwartz, etc.
Device-under-test
(DUT)
Port 1
Port 2

## Slide 116: General Vector Network Analyzer Block Diagram
Extra
Measuring s11 and s21:
DUT
Receiver /
Detector
Processor and Display
Incident (R)
Reflected (A)
Transmitted (B)
Signal
Separation
Directional coupler
LO1
Reference
Oscillator
Sampler
+
ADC
Port 1
Port 2

## Slide 117: Relationship Between Port Voltage/Current and Normalized Waves
From the relations:
One can easily obtain a and b from the port voltages and currents (for instance a 2-port network):
This shows that S-parameters can be computed if we know the port voltage and current (take note these are phasors).
Most RF circuit simulator software use this approach to derive the S-parameters.
(4.7a)
2-port
network
V1
V2
I1
I2
a2
a1
b2
b1
Zc1
Zc2
Usually Zc1 = Zc2 = Zc
(4.7b)

## Slide 118: Example 4.2: Measuring Normalized Waves
This setup shows how one can measure a1 and b1 with an oscilloscope.
It can be done for frequency < 1 MHz where parasitic inductance and capacitance are not a concern.
2-port
network
V1
V2
I1
Zc = 50
Zc = 50
Rtest = 1
Channel 2
Channel 1
To oscilloscope
Signal generator
Extra
Assume Zc1 = Zc2 = 50
Rtest should
be as small
as possible

## Slide 119: Example 4.3: S11 Measurement Example in Time Domain
This experiment is done using a signal generator and Agilent Technologies Infinium Digital Sampling Oscilloscope.
Test resistor, as small
as possible, (V2–V1)/Rtest
gives the current flowing
into the network
Sample RLC network
Signal generator model
We would like to find what is
s11 at 10 kHz
Extra

## Slide 120: Example 4.3: S11 Measurement Example in Time Domain (cont’d)
Experiment setup
From signal
generator
Extra

## Slide 121: Example 4.3: S11 Measurement Example in Time Domain (cont’d)
V2 – V1
(16x averaging
10 mV per
division)
V2 – V1 peak-to-peak
amplitude  40.0 mV
Frequency  10 kHz
V2 peak-to-peak
amplitude  668 mV
V2 waveform
(200 mV per
division)
To = 1/10000 = 100 µsec
Extra

## Slide 122: Example 4.3: S11 Measurement Example in Time Domain (cont’d)
Zooming in to measure the phase angle
Phase = positive
if voltage leads
current, zero if
both voltage and
current have the same phase, and negative otherwise.
Phase calculation:
t
 8us
Voltage leads current
V2
V2 – V1
10 mV/division
Extra

## Slide 123: Example 4.3: S11 Measurement Example in Time Domain (cont’d)
Extra
Measured results
Converts into current phasor
e.g., I1 = Iamp ej , where  = phase
V1 is used as the reference for
phase measurement, hence V1 = Vampej0
where Vamp = Vpeak
Voltage and ‘current’
magnitude

## Slide 124: Example 4.3: S11 Measurement Example in Time Domain (cont’d)
Compare this with
measured results
Extra

## Slide 125: Power Waves
Consider port i, since assuming z = 0:
Power along a waveguide or transmission line on Port i:
Because of this, ai and bi are sometimes referred to as incident and reflected power waves. S-parameters relate the incident and reflected power of a port.
(4.8)

## Slide 126: More on S-Parameters
S-parameters are very useful at microwave frequency. Most of the performance parameters of microwave components such as attenuators, microwave FET/transistors, coupler, isolator, etc., are specified with S-parameters.
In fact, theories on the realizability of the 3-port and 4-port network such as the power divider in which the directional coupler is derived using the S-matrix.
In the subject “RF Transistor Circuit Design or RF Active Circuit Design”, we will use S-parameters exclusively to design various small-signal amplifiers and oscillators.
At present, the small-signal performance of many microwave semiconductor devices is specified using the S-parameters.

## Slide 127: Extra Knowledge 1: RF Transistor Datasheet
The performance of RF/microwave transistors are usually specified in terms of it S-parameters versus frequency.
For instance you can download the datasheet of the NPN RF bipolar transistor BFR92A from NXP Semiconductors:
http://www.nxp.com/pip/BFR92A_N.html
Another example is SiGe hetero-junction transistor (HBT) BFP420 from Infineon Technologies:
http://www.infineon.com
There are many more examples which you can search on your own.
Extra

## Slide 128: Extra Knowledge 2
We can actually use the S-matrix to relate reflected voltage waves to incident voltage waves. Call this the S’ matrix to distinguish from the S-matrix which relate the generalized voltage waves.
The reason generalized voltage and current are used more often is the ratio of generalized voltage to current at a port n is always 1. This is useful in deriving some properties of the S-matrix.
Of course when the characteristic impedance of all Tlines in the system are similar, then S’ = S.
Extra

## Slide 129: Example 4.4: S-Parameters for Series Impedance
Z
Zc2
Zc1
Find the S-matrix of the 2-port network below.
Refer to additional notes for the solution.

## Slide 130: Example 4.5: S-Parameters for the Lossless Tline Section
 , Zc
l
Derive the 2-port S-matrix for a Tline as shown below.
Case 1: Terminated Port 2
Since
Case 2: From symmetry, s11 = s22 = 0, s12=s21=ej:l
 , Zc
l
Zc
a1
b1
b2
Zin = Zc
+z
z=0
z

## Slide 131: Exercise 4.3: Conversion Between Impedance Z and the S-Matrix
Show how we can convert from the Z-matrix to the S-matrix and vice versa. Hint: Use equations (4.5) and (4.7) and the fact that:
For a system with Zc1= Zc2 = … = Zcn = Zc:

## Slide 132: S-Matrix for the Reciprocal Network: Symmetry
A linear N-port network is made up of materials which are isotropic and linear, the E- and H-fields in the network observe the Lorentz reciprocity theorem.
A special condition arises when the linear N-port network does not contain any sources (electric and magnetic current densities, J and M); the network is called reciprocal.
The reciprocal network cannot contain active devices, ferrites, or plasmas.
Active devices such as the transistor contains equivalent current and source in the model, while in ferro-magnetic material, the bound current due to magnetization* constitutes current source. Similarly the ions moving in a plasma also constitute current source.
Linear
n-port
Network
Port 2
Port 1
Port n

## Slide 133: S-Matrix for the Reciprocal Network: Symmetry (cont’d)
Under reciprocal condition, we can show that the S-Matrix is symmetrical, i.e., sij = sji .
E.g., for a 3-port reciprocal network:
Many types of RF components fulfill reciprocal and linear conditions, for example passive filters, impedance matching networks, power splitter/combiner, etc.
(4.9)
This is achieved using the Reciprocity Theorem in Electromagnetism, and using the definition of V and I from EM fields, one can show that the Z-matrix is symmetrical. Then using the relationship between S and Z matrices, we can show that S-matrix is also symmetrical.

## Slide 134: S-Matrix for Lossless Network: Unitary
When the network is lossless, then no real power can be delivered to the network. By considering the voltage and current at each port, and equating the total incident power to the total reflected power, we can show that:
S-matrix of this form is known as Unitary.
(4.10)

## Slide 135: Reciprocal and Lossless Network
Thus when the network is both reciprocal and lossless, symmetry and unitary of the S-matrix are fulfilled.
This is the case for many microwave circuits, for instance, those constructed using stripline technology.

## Slide 136: Conversion Between ABCD and S-Parameters
For 2-port networks, with Zc1 = Zc2 = Zo:
(4.11a)
(4.11b)

## Slide 137: Shift in Reference Plane
V’n+
V’n-
V2+
V2-
V1+ V1-
Vn+
Vn-
Linear
N-port
Network
0
0
0
z=-l2
z=-l1
z=-ln
V’2+
V’2-
V’1+ V’1-
+ve z direction
Note: For a wave propagating in +ve z direction, Vi+ e-jl
Let:
i = 1,2,…n
(4.12)
Extra

## Slide 138: Shift in Reference Plane (cont’d)
For a 2-port network:
(4.13)
Extra

## Slide 139: Cascading 2-Port Networks
a1A
a1B
a2B
a2A
b2A
b1A
b1B
b2B
A
B
New S-matrix:
Let:
a1A
a2B
b1A
b2B
(4.14)
Extra

## Slide 140: References
[1] R.E. Collin, “Foundation for Microwave Engineering”, 2nd Edition, 1992, McGraw-Hill.
[2] T. C. Edwards, “Foundations for Microstrip Circuit Design”, 2nd Edition, 1992, John-Wiley & Sons (3rd edition is also available).
[3] D.M. Pozar, “Microwave Engineering”, 2nd Edition, 1998, John-Wiley & Sons (3rd edition, 2005 from John-Wiley & Sons is also available).
A very advanced and in-depth book on microwave
engineering. A little complicated but the information is
very comprehensive. A classic work. Recommended.
Contains a wealth of practical microstrip design
information. A must have for every microwave
circuit design engineer.
Good coverage of the EM theory with emphasis on
applications.