## Slide 1: ME1000 RF CIRCUIT DESIGN
<number>
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.
Notes: <number>

## Slide 2: 8D. General Single-Stage Small-Signal Amplifier (SSA) Design
Notes: <number>

## Slide 3: 1.0 General Single-Stage Small-Signal Amplifier Design Procedures
Notes: <number>

## Slide 4: Practical Single-Stage Small-Signal Amplifier Design
Thus far, we have considered different aspects of a small-signal amplifier design
We have look at the stability analysis and simultaneous conjugate match for the maximum power gain under an unconditionally stable case
Using the constant GP circle to determine L for a conditionally stable amplifier, or when we do not require the maximum power gain
Plotting the constant noise figure circle to optimize s for optimum noise performance
Plotting the input mismatch circle to optimize for VSWRin and to set the actual transducer power gain (in collaboration of the constant Gp circle)
A general single-stage amplifier can be designed to meet multiple parameters, e.g., power gain, bandwidth, noise figure, input and output mismatchs
Notes: <number>

## Slide 5: Practical Single-Stage Small-Signal Amplifier Design (cont’d)
Unfortunately, these parameters compete with each other in determining the required load and source impedance values
For instance, when we want to maximize the power gain, we usually have to sacrifice the stability and noise performance
When we desire a low-noise figure, we have to trade off with a moderate input mismatch and lower power gain
In designing an amplifier, we use various circles learnt in the previous sections to help us to balance the trade-off carefully
After finding the optimum load and source reflection coefficients, impedance transformation is usually employed to map the actual load/source impedance to the desired value
Computer-aided design is often compulsory for an optimum design
Notes: <number>

## Slide 6: Practical Single-Stage Small-Signal Amplifier Design (cont’d)
ZL
Zc
Zc
Zs
Vs
VSWRin
VSWRout
PA
PL
GT
F
Stability
Factor
Bandwidth
Notes: <number>

## Slide 7: Single-Stage Small-Signal Amplifier Design Flow
Done
Find s
Meet
Requirement
Do Not
Meet Requirement
SCM
Start
Set the frequency range
Set the VSWR1
Set the NF
Set the GT or GP
Design the DC biasing, choose components.
Get the S-parameters
Check for stability
A
B
LNA/
non-SCM
Final verification using
a simulation software
Design the impedance
transformation network
A
Find sm and Lm
Find GP(max)
B
Draw the GP circles
Find L
Draw the input mismatch circle
Draw the F circle
Do Not Meet Requirement
Notes: <number>

## Slide 8: Summary for Chapters 7 and 8
Stability factor checks for unconditionally stable amplifier:
Simultaneous conjugate match:
Only when the amplifier is unconditionally stable, K > 1
Sets both L and s
Notes: <number>

## Slide 9: Summary for Chapters 7 and 8 (cont’d)
Constant power gain:
Can be applied for both unconditionally stable and conditionally stable amplifiers
Sets L
Notes: <number>

## Slide 10: Summary for Chapters 7 and 8 (cont’d)
Constant noise figure:
Sets s
Notes: <number>

## Slide 11: Summary for Chapters 7 and 8 (cont’d)
Constant input mismatch:
Sets s
Notes: <number>

## Slide 12: Example 1 (Textbook): General Amplifier Design Example
A BJT, biased at IC = 10 mA, VCE = 6 V is operated at f = 2.4 GHz. The biasing network is shown in the next slide. The corresponding S-parameters are s11 = 0.3 < 30°, s12 = 0.2 < –60°, s21 = 2.5 < –80°, s22 = 0.2 < –15°. The noise parameters of the BJT are Fm(dB) = 1.7 dB, Re = 4 , and m = 0.5 < 45°. Assume Zo = 50 .
Design a low-noise amplifier using the BJT circuit, with:
  A power gain Gp of at least 8 dB
  Noise figure F less than 2.0 dB
  VSWR1 less than 2.0
  The amplifier has a source of 50  and load of 50 
Notes: <number>

## Slide 13: DC Biasing Network
S11 = 0.3 < 30° = 0.260 + j0.150
S12 = 0.2 < –60° = 0.100 – j0.173
S21 = 2.5 < –80° = 0.434 – j2.462
S22 = 0.2 < –15° = 0.193 – j0.052
Cc1
Cc2
L1
L2
Cd
Rc
Vcc
Rb
Port 1
(input)
Port 2
(Output)
Ic = 10 mA
6 V
@ 2.4 GHz
Simulated S-parameters
Notes: <number>

## Slide 14: General Amplifier Design Example
Stability analysis: K = 1.178 > 1 and |D| = 0.555 < 1. So the amplifier is unconditionally stable and the maximum power gain is:
So the power gain fulfills the requirement. This is the value that can be obtained if we apply the Simultaneous Conjugate Match (SCM). In this case Gp = GT = GA.
Computing the source and load impedances for the maximum power gain:
For the next step, we will plot the constant input mismatch circles and constant noise figure (F) circles on the Smith chart for s plane, with L = Lm
Then we make sure that the location of sm fulfills the requirements of F < 2.0 dB and VSWR1 < 2.0
Notes: <number>

## Slide 15: General Amplifier Design Example (cont’d)
For L = Lm:
Now with this information we could calculate the radius and center of the constant input mismatch or VSWR1 circles
Notes: <number>

## Slide 16: General Amplifier Design Example (cont’d)
s plane
Circles:
VSWR1 = 2.0
Radius = 0.3071
Tcenter = 0.253 – j0.082
VSWR1 = 1.8
Radius = 0.262
Tcenter = 0.260 – j0.084
F = 2.0 dB (F = 1.5849)
Radius = 0.5772
Tcenter = 0.215 + j0.215
F = 1.8 dB (F = 1.5136)
Radius = 0.372
Tcenter = 0.292 + j0.292
Constant F
circle, F = 2.0 dB
m
Constant F
circle, F = 1.8 dB
VSWR1 = 2.0
sm
VSWR1 = 1.8
Notes: <number>

## Slide 17: General Amplifier Design Example (cont’d)
From the previous slide, we see that all the requirements are fulfilled. So the required source and load reflection coefficients are:
Noting that sm is near the F = 1.8 dB circle, the performance parameters of the amplifier are:
  Gp = 6.942 or 8.42 dB
  VSWR1 = 1 or M = 1
  F  1.568 or 1.5136 dB < 2.0 dB
Finding the source and load impedances:
Notes: <number>

## Slide 18: General Amplifier Design Example (cont’d)
Since the original source and load impedances do not correspond to these values, impedance transformation networks are used at the input and output ports of the amplifier
The final block diagram:
Amplifier
50
2.99 nH
0.80 pF
50
Zsm
ZLm
@ 2.4 GHz
1.14 nH
0.13 pF
VSWR1 = 1
Notes: <number>

## Slide 19: Complete Schematic of the Example
Cc1
Cc2
L1
L2
Cd
Rc
Vcc
Rb
2.99 nH
0.8 pF
1.14 nH
0.13 pF
Q1
C2
L4
L3
C1
Notes: <number>

## Slide 20: Suggested Layout for the Example
Proposed layout, on a 0.8 mm thick FR4 substrate. Bottom is the ground plane.
Vcc
GND
Cc2
Cc1
C1
Q1
L3
L4
C2
50
microstrip line
50 microstrip line
Rc
Cd
L1
L2
Rb
Plated through holes
Notes: <number>

## Slide 21: 2.0 Practical Amplifier Design Example: Low-Noise Amplifier with a Fixed GT and Input Mismatch
Notes: <number>

## Slide 22: Introduction
In this exercise, we are going to design and build a low-noise amplifier, optimized for operation at 850 to 920 MHz
The RF transistor BFR92A is used for this exercise. This is a wideband NPN transistor with fT = 5 GHz (at IC = 30 mA and VCE = 10 V). Using a transistor with fT > 5  fo allows us to reduce the DC collector current (IC), thereby reducing the idle power dissipation.
The circuit is intended for operation at a supply voltage of 3.0 to 3.3 V
The software Advanced Design System, ADS2003C from Agilent Technologies is used for the computer analysis
Notes: <number>

## Slide 23: DC Biasing Design
Voltage feedback bias is chosen
AppCAD is used to estimate the initial biasing resistor values and to perform the necessary DC stability analysis
From Datasheet
of BFR92A
DC stability analysis
results
Notes: <number>

## Slide 24: DC Biasing Design (cont’d)
Simulated result using a
nonlinear DC solver, with
SPICE model of BFR92A
IC = 3.0 mA
VCE = 1.33 V
Theoretical max voltage swing at the collector of Q1 = 2 x 1.33 = 2.66 V
Notes: <number>

## Slide 25: AC Analysis
Upon adding in the RF choke LC and coupling capacitors Cc1 and Cc2, small-signal AC simulation (S-parameters) is performed from 100 MHz to 3000 MHz
Note that noise calculation is enabled and the Roulette K factor macro is also inserted
Notes: <number>

## Slide 26: AC Analysis (cont’d)
S21 of the AC analysis indicates power gain Gp of greater than 9 dB between 800 to 900 MHz
Notes: <number>

## Slide 27: AC Analysis (cont’d)
Furthermore the basic amplifier circuit is unconditionally stable. As indicated by K > 1 and |D| < 1 within the analysis frequency range.
We do not have to worry about stability greater than 3 GHz as for the DC biasing used, fT of the transistor Q1 is expected to be less than 3 GHz
Also, noise calculation shows that theoretically, a noise figure of less than 1.26 can be achieved
Noise Figure (dB)
Minimum Noise
Figure
Notes: <number>

## Slide 28: AC Analysis at 900 MHz
To find Lat
Gp(max)
To generate points for the constant Gp circles for Gp = 8, 10, and 12 dB
To generate the points for the constant F circles for F = Fmin + 0.1 and Fmin + 0.3
Start and stop at 900 MHz, also enable computation of the Z-parameters
The target is to operate the amplifier in the vicinity of 900 MHz, thus we focus the analysis at this frequency
Notes: <number>

## Slide 29: AC Analysis at 900 MHz (cont’d)
We write our own macro to generate points for the constant input mismatch circle on the Smith chart for s. Here m1 and m2 are the markers in the Smith charts.
Minput is the user specified input mismatch factor
Notes: <number>

## Slide 30: AC Analysis at 900 MHz (cont’d)
Two Smith charts are plotted. Markers m1 and m2 are chosen such that the power gain Gp = 12.0 dB and the noise figure F is the minimum. As marker m1 changes, the constant input mismatch circle size and position on the s plane changes accordingly.
s plane
L plane
Constant Gp
circles
Lm
Constant input
mismatch circle
Constant F
circles
Sopt, S11 for the
lowest noise
figure NFmin
Notes: <number>

## Slide 31: AC Analysis at 900 MHz (cont’d)
From the Smith charts, after some tuning, the chosen load and source impedances are as shown
Observe that the transducer power gain GT = Minput x Gp. Or in dB, GTdB = 10log(Minput) + 10log(Gp) = –0.458 + 12 = 11.542
Noise figure of better than 1.264 + 0.1 dB can be achieved
Notes: <number>

## Slide 32: Input and Output Impedance Transformation Networks
The following LC networks are used:
Load Network: to transform ZL = 50 to 74 + j57 (approximate) at 900 MHz
Source Network: to transform Zs = 50 to 28 + j10 (approximate) at 900 MHz
Load network
Source network
Notes: <number>

## Slide 33: The Complete Schematic
Practical L and C values are used to approximate the source and load transformation networks
Notes: <number>

## Slide 34: AC Analysis of the Complete Schematic
The small-signal performance of the matched circuit, from 200 to 1600 MHz
Important parameters at 900 MHz:
Notes: <number>

## Slide 35: Large-Signal AC Analysis: Gain Compression
Finally a large-signal frequency domain analysis is carried out using the Harmonic Balance method
Input available power Pin is swept from –30 dBm to 10 dBm
Pin is swept
Consider up to 5th harmonic
Notes: <number>

## Slide 36: Large-Signal AC Analysis: Gain Compression (cont’d)
The node voltages VL, Vin and current I_in are arrays
The following equations are used to compute the load power PL1 and input power Pin1 at the fundamental frequency (RF_freq)
Index = 0: DC
Index = 1: Fundamental
Index = 2: 1st Harmonic
Index = 3: 2nd Harmonic
etc.
Power in dBm!
Notes: <number>

## Slide 37: Large-Signal AC Analysis: Gain Compression (cont’d)
The large-signal frequency domain analysis result
GA1_dB is the transducer power gain in dB at the fundamental frequency
As seen, 1 dB gain compression occurs around Pin = –12 dBm
1 dB gain compression here
Small signal,
constant GA
Notes: <number>

## Slide 38: Using Real Inductors and Capacitors
After the actual circuit is built, some tuning is performed on the passive component values
It is discovered that the following values give the optimum performance
These are replaced with a single 12 nH 0603 inductor (L3) from Vishay® Dale
Grounded coplanar
transmission line model
Notes: <number>

## Slide 39: Designing the Coplanar Transmission Line on Both Ends
Notes: <number>

## Slide 40: PCB Layout
Copper (1 ounce)
FR4 dielectric (62 mils or 1.57 mm thick)
A two-layer PCB used.
Top Copper
Bottom Copper
Notes: <number>

## Slide 41: The Actual Hardware
Grounded coplanar transmission line
PCB for power supply and GND
Notes: <number>

## Slide 42: Measurement Results
|S11|
|S22|
|S21| and
|S12|
The Agilent 8753ES Vector Network Analyzer is used to perform the small-signal S-parameters measurement. The power range is set to –30 dBm to –10 dBm. Frequency is sweep from 50 MHz to 3.0 GHz. Open-Short-Load calibration is used at the SMA end launchers.
Measured
Simulated
Notes: <number>

## Slide 43: Appendix 1: Monolithic Microwave Integrated Circuit (MMIC) Amplifier
Notes: <number>

## Slide 44: Monolithic Microwave Integrated Circuit (MMIC)
Nowadays you can easily built an RF amplifier using MMIC amplifier module.
These usually contain a Darlington transistor pair with series and shunt feedbacks. The feedback serve to increase the bandwidth of the amplifier and internally match the input and output impedance to 50Ω.
For example see Avago Technologies’ MSA series devices datasheet.
Series
feedback
Shunt
feedback
Example of an MMIC amplifier schematic
VCC
RF Choke (optional)
RC
Input
Output
DC Blocking
Capacitor
DC Blocking
Capacitor
Power Supply
Decoupling
Capacitor
MSA
Vd
Id

## Slide 45: Monolithic Microwave Integrated Circuit (MMIC) (cont’d)
In an MMIC the device current ID determines the gain, noise figure and other large-signal parameters (e.g. P1dB, TOI level etc). Generally the datasheet of the device will provide information on the optimum device current.
The procedures of setting the values of the coupling capacitors, the RF choke and the decoupling capacitors as discussed still applies to MMIC amplifier.
ID
Decoupling capacitor
Coupling capacitor