## Slide 1: ME1000 RF CIRCUIT DESIGN
<number>
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 8B. Small-Signal Amplifier (SSA) Design — Low-Noise Amplifier
Notes: <number>

## Slide 3: 1.0 Noise in Linear System
Notes: <number>

## Slide 4: Electrical Noise
Noise in an electronic circuit is due to random motions of electrons
This results in a potential difference and current which fluctuate randomly, which we call a noise signal
This noise signal is due to random processes occurring within the components or interference from the environment
The mechanisms causing the random electrical signal is not known exactly to us (by sheer complexity of the process, or by our own ignorance), thus we cannot determine, in a precise manner, the waveform of the signal
We have to rely on the probability and statistics to describe the waveform, thus a noise signal is also called a non-deterministic or stochastic process
Notes: <number>

## Slide 5: Electrical Noise (cont’d)
An example of a noise signal is shown below. This could be a voltage or current waveform
Note that as time progresses, the instantaneous value of the signal may fluctuates wildly
Also, when we measure the waveform, each measurement will produce a waveform that is different from the previous measurement (see Appendix 1)
t
v(t)
t1
t2
t3
0
Notes: <number>

## Slide 6: Noisy Signals
Noise reduces the sensitivity of an amplifier as it could overwhelm the required electrical signal
t
V(t)
A binary signal corrupted by
a little noise. High signal-to-noise
(SNR) ratio.
t
V(t)
A clean binary signal
t
V(t)
A binary signal corrupted by
a lot of noise. Low signal-to-noise (SNR) ratio.
Notes: <number>

## Slide 7: Noise Statistics
Often we are more interested in the effects of the noise signal on electronic systems over a period of time or over many measurements (called an ensemble and collection)
Thus, it is more meaningful to extract certain quantities from the noise signal instead of studying the waveform of the noise signal
These quantities are called the statistics of the noise signal, including parameters such as the average (or mean), maximum value, minimum value, mean square, etc.
Most noise signals in electronics swing with equal probabilities to the positive and negative values; hence they usually possess zero average value. This is called the zero-mean noise.
The square of a noise signal is always positive, and the average value, called the mean square, is a non-zero value and corresponds to the average power of the noise signal
Notes: <number>

## Slide 8: Noise Statistics (cont’d)
This example shows a noise voltage signal (red) and its average value (blue) over time
This example shows the square of the same noise voltage signal (red) and its mean square (blue), and root mean square (green) over time
T
Time
Statistics
Notes: <number>

## Slide 9: Noise Statistics (cont’d)
The previous slide shows the computation of a noise signal statistics in a time domain
We can also compute the noise statistics such as the average, mean square, root mean square in terms of an ensemble, called the ensemble statistics. For ensemble statistics we perform many measurements and only sample the value at a fixed instant, in general ensemble statistics depends on time.
The ensemble statistics are written as:
Average or mean
Mean-square
Root mean-square
Value of v at time t and for kth measurement
n
1
2
3
4
5
6
v(t1)
t
V(t)
t1
0
Notes: <number>

## Slide 10: Noise Statistics (cont’d)
When the ensemble statistics are independent of the time of measurement, the noise signal is said to be stationary
Thus, if for any time point where , the noise is said to be stationary in the mean
Similarly, if for any time point where , the noise is said to be stationary in the mean square
Notes: <number>

## Slide 11: Noise Statistics (cont’d)
When the noise statistics measured in a time domain approaches the noise statistics in an ensemble, the noise signal is said to be Ergodic
When a noise signal is stationary in the mean and mean square (Wide-Sense Stationary), we can show that it is also ergodic in the mean and mean square
Thus if , we say the noise signal is ergodic in the mean
Similarly if , we say the noise signal is ergodic in the mean square
Key Concepts:
Noise statistics – mean, mean square, root mean square, varians, etc.
Can be measured in a time domain or ensemble
Stationary property of statistics in an ensemble
Ergodicity
Note that ergodicity requires the noise source to be stationary.
Notes: <number>

## Slide 12: Representation of the Noise Power in a Frequency Domain: Power Spectral Density
For most electronic systems, the electrical noise signal usually fulfills a condition called the Wide-Sense Stationary (WSS) (see Appendix 1)
Under this condition, the ensemble mean square value is given by:
The integrand in the equation above is called the Power Spectral Density (PSD)
PSD tells us the spread of the noise energy as a function of frequency much like in deterministic signals
(1.1)
Mean-square of
noise signal v(t)
Notes: <number>

## Slide 13: Computation of Power Spectral Density from Measurements
Assuming noise signal v(t) fulfills the WSS condition. Measure v(t) from time t = 0 to a sufficiently long period*, say t = T.
1st
2nd
nth
0
t
T
0
t
T
f
f
0
t
T
f
f
Performing ensemble
averaging, then gradually
increasing T and repeat again
until the change in the result
is less than an acceptable
threshold.
Taking n and T large enough, the
result will approach the actual
PSD of the noise.
(1.2)
Fourier
transform
Measurement period
*For example 10x the duration where auto-correlation
drops to 10% of the peak value

## Slide 14: Analysis of Noise Sources
Using the concept of portraying a noise signal as a random process and the concept of stationary and ergodicity, researchers study various types of noise sources found in semiconductor devices and electronic systems.
Using the method outlined in the previous slides, the PSD for the noise source can be determined.
Note: There is an alternative method of
deriving the PSD for WSS noise source, by performing the Fourier
Transform on the auto-correlation function of the noise signal, called
the Wiener-Khintchin-Einstein Theorem (see Appendix 1).

## Slide 15: Analysis of Noise Sources (cont’d)
For instance, by measuring the potential difference across a real resistor:
An ideal oscilloscope
Resistor
0V
t
Ideal
resistor
t
0V
Real
Resistor
(noisy)
Fourier Transform
Ensemble Averaging
f
0
SV(f)
PSD
>100 GHz
We can assume PSD of resistor
To be constant for most
applications

## Slide 16: Noise and Linear System
Noise signal is usually very small in magnitude
Thus, if it is present at the input of an electronic system, the system can be considered linear
We restrict ourselves to the noise analysis with the linear system, and apply the concept of Transfer Function in linear analysis
Nonlinear systems are rarely encountered, unless for noise due to strong interference from nearby sources or impulsive noise sources, or for systems with both large and small signals (like in a mixer or oscillator)
Notes: <number>

## Slide 17: Noise and Linear Systems (cont’d)
Many of the frequency-domain operations used with deterministic signals can be applied to random process as well.
It can be shown that (Lathi [2] or Haykin [3]) if Sx(f) is the PSD applied to a linear time-invariant (LTI) system with transfer function H(f), then the output Power Spectrum Density is:
LTI
H(f)
Sx(f)
Sy(f) = Sx(f)|H(f)|2
f
f
0
1
0
f
0
Sx(f)
Sy(f)

## Slide 18: Effect of Filtering - Narrow-Band Noise
Thus, when the noise is imposed on a filter with the bandwidth f, the mean square value is approximately:
Thus, the average amount of noise power (over 1  load) contained in the bandwidth f about fc is approximately Sv(fc)f
Filter
Assuming the noise
source is ergodic
in the mean square
f
1
-fc
fc
f
0
Notes: <number>

## Slide 19: Illustration of the Effect of Band Limitation and PSD
Let us take our resistor and oscilloscope example again. Consider 3 cases of resistors connected to a oscilloscope with limited bandwidth.
t
0V
t
0V
t
0V
330Ω, 25oC
33000Ω, 25oC
33000Ω, 25oC
f
0
SV(f)
100 MHz
bandwidth
0.1 MHz
width
∆f=100 MHz

## Slide 20: Sources of Noise in Electronics and PSD
Thermal Noise – Random motion of electrons. Exists even when there is no current flow. Associated with the resistor, white noise.
Shot Noise – Due to the current flowing across the potential barrier in the PN junction. Only exist in the BJT, not in the FET. Exists when there is current flow. White noise.
Flicker Noise – Cause mainly by traps associated with the contamination and crystal defect. Exists when there is current flow. Low frequency noise.
PSD
PSD
R
(1.3a)
(1.3b)
(1.3c)
Notes: <number>

## Slide 21: Sources of Noise in Electronics and PSD (cont’d)
Burst Noise – Mechanism not fully understood. Low frequency noise.
Avalanche Noise – Due to the avalanche breakdown in a Zener diode. Low frequency noise.
(1.3d)
Notes: <number>

## Slide 22: Important Assumptions of Noise in Microwave and RF Systems
The amplitude of a noise signal (either voltage or current) is usually small
The system where a noise signal exists is linear
The noise signal is wide-sense stationary and ergodic in the mean and autocorrelation
The PSD of the noise signal is white
The random variable resulting from a sampling of the noise signal has the Gaussian PDF
Notes: <number>

## Slide 23: Example 1.1: Small-Signal RF Transistor Model with Noise Sources
Small-signal hybrid pi model of a transistor and its noise sources.
No thermal noise for these 2 resistors
since they are not physical resistors! They are added
to account for the mathematical relationship of the BJT I-V curve
CC
CE
rB’E
rCE
gmvB’E
B
C
E
B’
in
in
+
-
Shot Noise
for BE junction
Shot Noise for BC junction
Thermal Noise
for base-spreading resistor

## Slide 24: Example 1.2: AC Simulation with Noise
Most linear circuit simulator support noise simulation during a AC or frequency domain simulation
The example shows the PSPICE simulation control tab.
Enable noise sources
in a small-signal model
Notes: <number>

## Slide 25: Example 1.2: AC Simulation with Noise (cont’d)
With the Agilent Technologies ADS Software:
Double-click the
S-PARAMETERS
control, then go
to the ‘Noise’ tab
Notes: <number>

## Slide 26: 2.0 Small-Signal Low-Noise Amplifier Design
Notes: <number>

## Slide 27: Low-Noise Design Considerations
Only the thermal noise and shot noise remained at a very high frequency
As seen in the previous slide, the average noise power is proportional to:
Thus, if we could reduce the bandwidth of the system, we could in theory reduce the noise power at the output too
Resistor also contribute to the thermal noise, low-noise design entails using smaller resistance values
Notes: <number>

## Slide 28: Low-Noise Design Considerations (cont’d)
Furthermore, a FET does not have a shot noise as the charge carriers in the channel do not flow through a PN junction. Hence, the FET is usually used for an amplifier with a very low noise requirement.
Between using a discrete transistor and an integrated circuit (monolithic microwave integrated circuit, MMIC), usually a discrete transistor amplifier contributes a lower noise to the systems (lower noise figure). This is evident as every component in the circuit contributes noise; the more the components, the higher the total noise output of the circuit.
Certain balanced configuration can reduce the noise contribution, for instance, in a double-balanced mixer design
Notes: <number>

## Slide 29: Noise Figure (F) and Minimum Detectable Signal (MDS)
Noise from the environment is unavoidable; this sets the lowest signal level that can be detected by a receiver
The ratio of a time-averaged signal power to a time-averaged noise power is termed the Signal-to-Noise Ratio (SNR)
Most RF small-signal amplifiers are also designed to be of low-noise, i.e., the amplifier introduces very little noise to the output. The amplifier is an important component in the receiver chain.
Time-averaged noise power
at input due to Zs
Amplifier
ZL
Zs
Vs
Pin
N
GPPin
GPN
NA
VN
Noise
Note: input noise
power N is only due
to resistance of Zs
Notes: <number>

## Slide 30: Noise Figure (F)
When noise and a desired signal are applied to the input of a ‘noiseless’ network (i.e., an amplifier), both noise and signal powers will be attenuated or amplified by the same factor, thus the SNR at the input and output of the network will be similar
If the network is noisy, the SNRout will be smaller than the SNRin, since there is an additional noise power at the output, those that produced by the network itself.
Noise figure, or F, is a measure of the degradation in the SNR between the input and output of a component
We will see in the following slides that F is always greater than 1 for a noisy component, and it affects the Minimum Detectable Signal power for a receiver chain
By definition, noise figure is usually measured at a temperature of 290 K and matched impedance
Notes: <number>

## Slide 31: Noise Figure (F) (cont’d)
The Noise Figure (F) of a two-port network is defined as:
If NA= GPNE, where NE is the equivalent input noise, assuming the amplifier to be noiseless, then:
Noise Figure F is usually expressed in dB (10log10F), and the absolute value of F is usually called Noise Factor (NF), e.g. NF = 1.8 or F = 10log10(1.8) = 2.553 dB. Here we don’t make such distinction, and F and NF are used interchangeably.
Unless the amplifier is noiseless, F will always be greater than unity. A very good low-noise amplifier should have FdB < 2 dB (F < 1.5849)
(2.1b)
(2.1a)
Gp
Pin
GpPin
N
GpN
NA
Notes: <number>

## Slide 32: Minimum Detectable Signal (MDS) and Noise Figure (F)
Minimum Detectable Signal is the smallest signal power that can be differentiated by the receiver from noise power
We set the output signal power to be equal to the output noise power as the limit for detection. Thus, when Pin = MDS, SNRout = 1
Since N is usually the noise due to the input resistance and environment, there is nothing much we can do to reduce it. But we can reduce F. By having a smaller F, Pin(MDS) would be smaller, this means that the system is more sensitive.
We can also use a larger ratio, say SNRout = 2 for the limit of detection. This ratio is typically used in a receiver design.
(2.2)
Notes: <number>

## Slide 33: Minimum Detectable Signal (MDS) and Noise Figure (F) (cont’d)
When input signal power is > MDS:
Detector and
Demodulator
t
V(t)
t
0
t
Noise
0
MDS level
t
0
Signal
MDS level
When noise level is small, MDS level is also small. Signal > MDS level.
Correct data
Notes: <number>

## Slide 34: Minimum Detectable Signal (MDS) and Noise Figure (F) (cont’d)
When input signal power is < MDS:
Detector and
Demodulator
t
0
0
t
V(t)
0
t
When noise level is large, MDS level is high. Signal < MDS level.
t
0
MDS level
Incorrect data
Notes: <number>

## Slide 35: Minimum Detectable Signal (MDS) and Noise Figure (F) (cont’d)
In general, the previous analysis can be applied to any linear n-port networks, such as filters, power splitters, and mixers
For a three-port network such as a downconversion mixer, if we only consider the RF input and IF output, the mixer can be viewed as a two-port network
Also, for a system consisting of a few units cascaded together, we can compute the total noise figure of the system. Later slides will address this.
LO
RF
IF
Notes: <number>

## Slide 36: Summary for Noise Figure (F)
The previous slide shows the importance of the parameter Noise Figure (F)
A small F allows a smaller MDS power, thus resulting in a more sensitive amplifier. For example, in a wireless system an amplifier in the receiver stage with a smaller MDS can function over a larger separation.
An amplifier that is optimized to contribute very little noise to the system is known as a Low-Noise Amplifier (LNA)
Notes: <number>

## Slide 37: Use of a Low-Noise Amplifier (LNA)
LNA is usually used as the 1st stage amplifier for a receiving circuit. Since the signal from the antenna is very weak, the LNA amplifies the signal without contributing too much noise. This larger signal is then fed to the mixer, which generally has a higher noise figure. This will improve the overall F at the IF output (see Appendix 1 and 2).
To demodulator
circuits
LO
LNA
IF Amp.
A superheterodyne receiver
BPF
BPF
Image
Filter
Extra
Notes: <number>

## Slide 38: Use of Low-Noise Amplifier (LNA) (cont’d)
If the power gain of the 1st stage is around 10 or more, the signal will be sufficiently large at the output of the 1st stage, so that additional noise contributed by the following amplifier stages or mixer will have a small degrading effect on the overall SNR, provided the noise contribution of the following stages is moderate
In the design of the 1st stage, the minimum noise requirement is more important than the maximum power gain or VSWR
Extra
Notes: <number>

## Slide 39: Use of Low-Noise Amplifier (LNA) (cont’d)
In contrast, the following architecture suffers from a lower sensitivity due to the high noise figure of the mixer
Unless we can design a mixer that has a very low noise and at the same time provides a sufficient conversion gain, this architecture is generally avoided
LO
IF Amp.
BPF
IF Amp.
BPF
Extra
Notes: <number>

## Slide 40: Another Reason for Including a LNA in the Receiver Stage
Another reason why LNA is always used in the first stage of a wireless system is that it provides an isolation against the leakage of the local oscillator (LO) signal
The LNA has a small |s12|. It prevents the power from the LO going into the antenna and radiate out, causing unwanted radiation
LO
LNA
IF Amp.
A superheterodyne receiver
BPF
BPF
Image
Reject
Filter
Leakage LO signal
the mixer
Leakage LO signal
is highly antennuated
Antenna
Extra
Notes: <number>

## Slide 41: Representing Noise Contribution of Linear 2-Port Network
In analyzing the noise produced at the output of a linear 2-port network due to internal noise, we can account for the effect of all the internal noise sources by a series noise voltage generator and a shunt noise current generator at the input port (from Thevenin or Norton theorem).
Two equivalent sources are needed as when we open and short circuit the input port, we still get noise signals at the output. Shorting the input eliminate in, while open circuit the input eliminates en (See Chapter 11, Gray & Meyer [6]).
Noisy
Amplifier
ZL
Zs
Vs
Noiseless
Amplifier
ZL
Zs
Vs
Noisy Amplifier

## Slide 42: Optimum Source Impedance Zm
Assuming Gp and ZL of the amplifier are fixed. The total noise power at the output is thus a function of , and the thermal noise due to real part of ZS (Here EMI noise is ignored, assuming this can be eliminated).
Let us define the PSD of en and in as Se(f) = 4kTRe , Si(f) = 4kTGi. Re is called the equivalent noise resistance and Gi is called the equivalent noise conductance.
The equivalent noise sources en and in are due to some internal processes in the amplifier, thus there can be correlation between them, the correlation PSD is expressed as Sx(f) = 4kT(r + ji) (see [1]).

## Slide 43: Optimum Source Impedance Zm (cont’d)
Thus we can express the Noise Figure as a function of 6 parameters [1]: F = F(RS , XS, Re , Gi, r, i)
(2.3)

## Slide 44: Optimum Source Impedance Zm (cont’d)
For a certain a fixed Re, Gi, r and i, we can then find a value of ZS = RS + jXS which will minimize F. The details are shown in Collin [1], Chapter 10 and Ludwig & Bretchko [4], Appendix H.
Let this Zs value be Zm = Rm + jXm, and the corresponding minimum F be Fmin. It can be shown that ([1], [4]) F can be expressed in a useful form containing Zm , Fmin, Zs and either Re or Gi only:
(2.4)
You can adjust the source
impedance Zs to influence F
Minimum noise
figure Fmin
The corresponding
Zs when F=Fmin
Note

## Slide 45: Optimum Source Impedance Zm (cont’d)
When using BJT or FET, the 4 noise parameters (Zm, Fmin, Re or Gi ) are known through datasheet or direct measurement.
Optimum source impedance (Zm) or admittance will be provided (often m is given instead).
Note that the minimum noise figure Fmin depends on D.C. biasing condition and the operating frequency of the circuit.
The equivalent noise conductance Gi (some literature will use normalized conductance gn = GiZo instead) or noise resistance Re (or rn in normalized form) are related by:
With these parameters, we can easily find the noise figure F of a BJT or FET amplifier for any source impedance Zs using (2.4).
(See Collin [1], chapter 10 and
Ludwig & Bretchko [4], appendix H,
and also in the extra written notes)
(2.5)

## Slide 46: Constant Noise Figure Circle
In general the design engineer has the freedom to adjust s to affect F.
Given a certain F, Fmin , Zm or m and Re or Gi, we can plot a locus of points for s on the Smith chart using (2.4).
This locus happens to be a circle, called Constant Noise Figure Circle, that allow us to determine the corresponding source impedance that will produce F (see Collin [1] for the derivation).
Let (Zo is the reference impedance, for instance 50) :
The center and radius of Constant F Circle are:
Sometimes
RN=Re/Zo
or
GN=GiZo is
given.
(2.6)
(2.7a)
(2.7b)

## Slide 47: Example 2.1
A silicon bipolar transistor has the following parameters at 4 GHz, Ic = 2.0 mA, VCE = 2.7 V: S11 = 0.36 < 148°, S12 = 0.11 < 42°, S21 = 1.57 < 27°, S22 = 0.67 < –64°. m = 0.38 < –153°, Re = 20, Fm = 1.905 (2.8 dB) all measured with respect to Zo = 50. Plot the constant noise figure circles for F = Fm + 0.5 dB and F = Fm + 1.0 dB.
Notes: <number>

## Slide 48: Example 2.1 (cont’d)
F=Fm + 0.5 dB Constant F circle:
F = Fm + 1.0 dB Constant F circle:
Notes: <number>

## Slide 49: Example 2.1 (cont’d)
Fm + 1.0 dB
Fm + 0.5 dB
Fm
Constant Noise
Figure Circles
on the s plane
Notes: <number>

## Slide 50: Noise Figure of Cascaded Systems
ZL
Zs
Vs
Noiseless
Amplifier 1
Noiseless
Amplifier 2
Gp1, F1
Gp2, F2
Z2A
Z1B
Z1A
M1 and M2 are known as
the mismatch factor for stage
1 and stage 2 respectively.
These will be covered in
Chapter 8C. See
Collin [1] for derivation.
Total noise figure F:
(2.8a)
(2.8b)
If Gp is large F2 has minimal impact on overall F
Since
Gp = Power Gain
GA = Available Power
Gain

## Slide 51: Typical Noise Figure of an Amplifier and a Mixer
For a good amplifier, it is in the vicinity of 2.5 to 6.0 dB
For amplifier optimized to reduce noise (LNA), it is usually between 1.1 to 3.5 dB
For mixer, the noise figure is higher. Discrete single-ended mixer using FET or BJT has F around 7 to 10 dB
For double-balanced mixer such as the Gilbert cell, a typical F would be 10 to 15 dB
Notes: <number>

## Slide 52: Appendix 1: Brief Review of Noise Theory
Notes: <number>

## Slide 53: Nature of Noise Signal
A noise is a random signal. We have to use probability or chance to describe the occurrence of the signal.
For instance, consider the waveform above. As we move along the t axis, there is no obvious relationship of V(t) at one instance to the next.
Also, when we measure the waveform, each measurement will produce a waveform that is different from the previous measurement
0
t
V(t)
Notes: <number>

## Slide 54: Nature of Noise Signal (cont’d)
Furthermore, if we were to measure the amplitude v(t) at t = t1 for many times (say we power down the measuring instrument and power it up again), we see that the value v(t1) at each measurement is not predictable
0
t
t1
1st measurement
2nd measurement
0
t
t1
nth measurement
0
t
t1
A group of measurements
is called an Ensemble
Each measurement is a process. If the waveform of each measurement is non-deterministic, we call this the Random Process.
Notes: <number>

## Slide 55: Random Process and Random Variable
A noise signal is called a Random Process or Stochastic Process
A Random Variable (RV) maps a random event to a value
A Random Process (RP) maps a random event to a function of time f(t)
Actually we can say that a noise signal is random across measurement and along time. As we examine the noise signal along the time axis, the fluctuation of the level does not seems to be described by any proper function. This is a characteristic of a noise signal, although it is not necessary so for all random processes.
Notes: <number>

## Slide 56: Random Process and Random Variable (cont’d)
Random Process
0
t
v(t)
Random Variable
t1
V1= v(t1)
V(t1)
fV(t1) (V)
PDF of noise at t1
n
1
2
3
4
5
6
The sampled value
at t1 for 5th
measurement
A probability distribution
can be assigned for the
sample at t1
Notes: <number>

## Slide 57: More on Random Process
Noise can be characterized by a few statistical parameters
For instance, for randomness across sample, if we were to measure the amplitude at t = t1 many times, the amplitude is a random variable (RV) and has an associated probability density function (PDF)
Usually the value of a signal at any instance of time can range from 0 to . Often a smaller value is more probable while a large value occurs less often.
V(t1)
fV(t1) (V)
PDF of noise at t1
Time domain representation
of noise — larger signal occurs
less often
t
V(t)
t1
Notes: <number>

## Slide 58: Nature of Noise
Thus, for a sample noise signal measurement, if we were to consider the voltage level at t = t1, t2 … tn, then we would have n RVs. Here we will call each RV V1, V2 … Vn
Associated with each Vi is a PDF fv(ti)
Here we only talk about voltage, but a similar argument can be applied to the current signals too
t
V(t)
t1
t2
t3
0
Notes: <number>

## Slide 59: Probability Density Function
The notation for PDF is usually given as:
The product is the probability for v(t) to have a value between V to V + dV at the time t = t1
Similarly we will also have Joint PDF:
The product is the probability for v(t) to have a value between V1 to V1 + dV at t1 and V2 to V2 + dV at t2
This can be extended for more RVs. Joint PDF for more than two RVs is usually called a higher order joint PDF.
Notes: <number>

## Slide 60: Example A1
Probability for V(t1) to fall between the values va and vb, inclusive of both endpoints:
Probability for V(t1) to fall between the values va and vb, and V(t2) to fall between the values vc and vd, inclusive of all endpoints:
Extra
Notes: <number>

## Slide 61: Classification of Random Process: Stationary Random Process
When the PDFs and all the joint PDFs do not depend on the origin time of the measurement, the random process is said to be Stationary
To know whether a RP is stationary or not, we have to perform empirical measurements or study the mechanism causing the RP, the source of the noise
For instance, if a RP is stationary, then:
Notes: <number>

## Slide 62: Stationary Random Process
Specifically for joint PDF,  can be of any values, so we can set  = –t1 and:
The joint PDF of a stationary random process only depends on the time difference (t2 – t1) !
This can be extended for higher order joint PDFs
Usually in studying noise theory, we are only interested in the PDF and 1st order joint PDF (i.e., for two RVs). We don’t care much about the higher order joint PDFs of a RP.
A noise source or RP in which AT LEAST the PDF and 1st order joint PDF are stationary is known as the Wide-Sense Stationary
Notes: <number>

## Slide 63: Stationary Random Process (cont’d)
Random Process
Wide-sense stationary
Stationary (Strict)
Notes: <number>

## Slide 64: Characterizing Noise with Statistics
Since the amplitude of noise at any instance is a random variable, we are not interested to know its exact value; what is more useful would be the Average Value
Other statistical values of interest are its Autocorrelation Function, Mean Square Value, and the Power Spectral Density (PSD)
The most important statistical value is the mean square value, this gives the estimate of the average power dissipated on a 1 Ohm resistor due to the noise source. From this value we can also obtain the RMS (root mean square) value.
Notes: <number>

## Slide 65: Average Value or Mean
Average value can be defined along t or across samples
Assume that the RP or noise signal is nonzero when t > 0, and zero otherwise
Time average:
Average across samples or Ensemble average (say at t = t1). Where the operator E( ) is known as expectation.
PDF for v(t1) =V1
ith sample
Note the difference between the notation for time average and the ensemble average
Notes: <number>

## Slide 66: Average Value or Mean (cont’d)
For a stationary or wide-sense stationary random process:
The ensemble average does not depends on the time t.
Can you explain why?
Notes: <number>

## Slide 67: Autocorrelation Function
Autocorrelation across a sample is defined by:
When the signal/random process is stationary or wide-sense stationary, Rv( ) only depends on the time difference, and is given by:
Autocorrelation along time is defined as:
Again note the different notation for the time average and ensemble average
* This implies that the autocorrelation along time is only unique (e.g., independent of time of origin) when the random process is at least Wide-Sense Stationary
Notes: <number>

## Slide 68: More About Autocorrelation Function
Autocorrelation function can give an indication of the frequency content of a RP.
Assume an RP or noise signal is at least wide-sense stationary and consider ensemble autocorrelation:

Rv()
0

Rv()
0
t
V(t)
t1
t2

Low frequency
content
High frequency
content
t
V(t)
t1
t2

Notes: <number>

## Slide 69: A Note on Wide-Sense Stationary Random Process
Usually we do not have to analyze the PDF to determine whether a random process is stationary or not (it is very difficult to estimate the PDF of a random process)
If by practical measurement we could determine that the ensemble average and ensemble autocorrelation do not depend on the time (only on the time difference for Rx( )), then the random process is said to be wide-sense stationary
A truly stationary random process (strictly stationary) will have all its ensemble statistical quantities independent of time
Wide-sense
stationary
Notes: <number>

## Slide 70: Ergodicity
Assume a random process is wide-sense stationary. If it can be shown that the time average equals to the ensemble average:
The random process is said to be ergodic in the mean
Similarly, for a wide-sense stationary RP, if it can be shown that the autocorrelation along time equals to the ensemble autocorrelation:
The random process is said to be ergodic in the autocorrelation function
Notes: <number>

## Slide 71: Mean Square Value
The final statistical value of interest is the mean square value. This can be viewed as the average power across a 1 Ω resistor (for voltage noise and current noise).
For mean square value along time:
For ensemble mean square value (say at t = t1):
Notes: <number>

## Slide 72: Finding the Mean-Square Value of a WSS Noise (1)
Consider a voltage noise v(t), also let v(t) fulfills the WSS requirement.
Thus
Both (A1.1a) and (A1.1b) describes the mean-square of v(t) in time and ensemble statistics.
In the next few slides we are going to show that v(t) is ergodic in mean-square and there exists a convenient way to ‘estimate’ the ensemble means square value of (A1.1b).
We note that the computation of directly from (A1.1b) is not practical since N needs to be very large (>> 1000) to get sufficient data points.
(A1.1a)
(A1.1b)
nth time measurement
Each measurement should
be sampled at t

## Slide 73: Finding the Mean-Square Value of a WSS Noise (2)
Here we will derive an indirect way to estimate .
Let us define a time-limited version of v(t) and its mean-square in time:
Thus
(A1.2)
(A1.3)
(A1.4)

## Slide 74: Finding the Mean-Square Value of a WSS Noise (3)
Now let us find the ensemble average of .
Using (A1.4):
For WSS noise source,
Thus
(A1.5)
or
This is a constant
Equation (A1.5) shows
that v(t) is ergodic in
the mean-square.

## Slide 75: Finding the Mean-Square Value of a WSS Noise (4)
Since v1(t) is a time-limited version of v(t), it can be transformed using Fourier Transform.
By the usage of Parseval Theorem, (A1.5) can be put into frequency-domain form, which is very useful to show the distribution of the noise energy in frequency-domain.
Using (A1.6b), we can write (A1.5) as:
(A1.6a)
(A1.7)
(A1.6b)

## Slide 76: Power Spectral Density for WSS Noise Source (1)
It is customary to write (A1.7) as:
Where
Sv(f) is called the Power Spectral Density (PDF) of the noise v(t), it is similar to the PDF for deterministic signals, where Sv(f) gives the noise power over 1 Hz centered at frequency f.
Note: Some books will define the integration from - to + . Then the PSD is half of the PSD defined here.
(A1.8a)
(A1.8b)

## Slide 77: Power Spectral Density for WSS Noise Source (2)
The interpretation of PSD:
The PSD can be considered the ‘spectrum’ of the noise, just like we consider the Fourier Transform or Fourier Series as the spectrum of ordinary deterministic signal.
PSD of a noise signal indicates the spread of the noise power in terms of frequency, and it can be computed from measurements.
Fourier transform of a time-limited
noise function v1(t) which is non-zero
for 0 < t < T.
Ensemble average of
Performing
ensemble
averaging, then
increasing T

## Slide 78: Practical Measurement of Power Spectral Density with Instrument
PSD can be obtained from measurement using (A1.8b) as shown (Razavi [5]):
Initially T can be taken as 5x the time where autocorrelation drops below 10% of the peak value.
1st
2nd
nth
0
t
T
0
t
T
f
f
0
t
T
f
f
Perform ensemble
averaging
Taking n and T large enough, the
result will approach the actual
PSD of the noise.

## Slide 79: Power Spectral Density of Wide-Sense Stationary Noise Signal (1)
Another approach to obtain the PDF for WSS noise source is to use the auto-correlation function of the noise.
From Chapter 4, Haykin [3] or Chapter 11, Lathi [2], we can also show that :
Thus PSD of a wide-sense stationary noise signal is the Fourier Transform of the (time) auto-correlation function.
It is helpful to repeat here again that PSD does not exist for random processes that are not WSS.
(A1.9)
Also called the
Wiener-Khinchine
Theorem, see book
by Lathi[2].

## Slide 80: Summary on Noise
Random Process
Noise Signal
Wide-Sense Stationary (WSS)
Ergodics in mean and autocorrelation
Concept of PSD for WSS noise signal
Practical measurement of PSD for WSS
noise signal
PDF and joint PDF
Statistics:
Mean
Autocorrelation
Mean square
Across time
Across ensemble
For ergodic process both are equal in the limit.
Extra
Notes: <number>

## Slide 81: Appendix 2: Downconverter Noise Figure
Notes: <number>

## Slide 82: Mixer Noise Figure
Assuming NH = NL = N, and only one sideband of the signal is used, say SL = 0 (An image rejection filter is used) and SH = S. This is called the single-sideband (SSB) operation.
NH, NL are the bandpassed external noise power on the upper and lower sidebands which will be down converted to the IF. Similarly for SH and SL, the signal power.
Gc is the conversion gain of the mixer
NM is the noise power contributed by the mixer
LO
RF
IF
NH
NL
SH
SL
Gc
NM
Notes: <number>

## Slide 83: Mixer Noise Figure (cont’d)
(A2.1)
Notes: <number>

## Slide 84: Comparison of the Noise Figure for a Downconverter with and without LNA
LO
LNA
Image
Filter
S + N
Gp = Power gain of the amplifier
Gc = Conversion gain of the mixer
S = Signal power
N = External noise power (mean square)
NA = Noise power from the amplifier
NM = Noise power from the mixer
Assume the amplifier and the external noise is wideband (covering the upper and lower sidebands of the mixer)
(A2.2)
Notes: <number>

## Slide 85: Comparison of the Noise Figure for a Downconverter with and without LNA (cont’d)
Comparing the noise figure with and without the LNA:
If the power gain Gp of the LNA is greater than 10, then in theory we could make F2 < F1
Without LNA
With LNA
Notes: <number>

## Slide 86: Comparison of the Noise Figure for a Downconverter with and without LNA (cont’d)
An example: Let NA = 2N, NM = 10N, GP = 10, and Gc = 1
This corresponds to a low-noise amplifier having a noise figure FLNA = 1.2 or FLNA(dB) = 1.58 dB
Notes: <number>