## Slide 1: ME1000 RF CIRCUIT DESIGN
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 3A. Impedance Transformation and Impedance Matching
Notes: <number>

## Slide 3: 1.0 Lumped Impedance Transformation Network
Notes: <number>

## Slide 4: Impedance Transformation
An impedance transformation network is a 2-port network that when connected in series with an impedance ZL at one port, will result in Zs being seen on another port.
ZL is usually not equal to Zs (otherwise there will be no need for transformation). Zs is known as the image impedance of ZL.
We immediately notice that the transformation network is a 2-port network.
ZL
Zs
Transformation
Network
Notes: <number>

## Slide 5: Why is Impedance Transformation Needed?
Maximum power is delivered when the load is matched to the Tline (assuming the generator is matched).
Impedance matching on sensitive receiver components (antenna, low-noise amplifier, etc.) improves the signal-to-noise ratio of the system.
Impedance matching in a power distribution network (such as the antenna array feed network) will reduce amplitude and phase errors.
Notes: <number>

## Slide 6: Maximum Power Transfer Theory
Zs
ZL
Vs
IL
VL
Time-averaged power dissipated across
load ZL:
Letting
We find that the values for RL and XL that would maximize PL is
RL = Rs, XL = –Xs.
In other words: ZL = Zs*
To maximize power transfer to the load
impedance, ZL must be the complex
conjugate of Zs, a notion known as
Conjugate Matched.
where
Notes: <number>

## Slide 7: Impedance Transformation and Matching
This is an example of an RF system where every modules are internally matched to 50 Ω.
Standardizing to a fixed impedance simplifies system design, as each module can be replaced with a module of similar functions and we can be assured the power flow along the path is not affected.
Notes: <number>

## Slide 8: Types of Transformation Network
Single lumped element (either L or C)
Dual lumped elements (L impedance matching network)
Triple lumped elements (Pi or T impedance matching network)
More lumped elements (ladder type)
Distributed elements (consists of sections of Tlines)
Hybrid (consists of both Tline and lumped elements)
Notes: <number>

## Slide 9: Impedance Transformation Using Lumped Elements
Lumped components such as the surface mounted device (SMD) inductor and capacitor can be easily purchased nowadays.
SMD capacitors have a range of 0.47 pF to greater than 10000 pF, with a tolerance of less than 5% and an operating temperature between –55oC to 125oC.
SMD inductors have a range of 1.0 nH to greater than 4000 nH, with a tolerance from 2% to 10%, an operating temperature from –40oC to 125oC, and a Q factor from a minimum of 15 to greater than 45.
The inductors come in a variety of form, from coil-type, thin-film, to spiral inductors mounted in an SMD package. The self-resonance frequency ranges from 200 MHz to greater than 5 GHz for L<100 nH (thin-film).
Notes: <number>

## Slide 10: Ultra-High Frequency Passive Components (>250 MHz)
Other sizes from the
JEDEC Solid State
Technology Association:
0402, even smaller than 0603
1210, bigger than 0805
Nowadays, there are also 0201 and 01005
Multilayer electrolytic
capacitor (1812)
Aluminium oxide
0805
80mils
50mils
Thin film inductor
(0603)
Coil inductor
(0805)
Thick film resistor
Multilayer ceramic capacitor
(0603), NPO dielectric
(0805)
(1210)
(1210),
Y5V dielectric
(0603),
NPO dielectric
Notes: <number>

## Slide 11: Medium Frequency Passive Components (up to 250 MHz)
Coil inductor
with ferrite core
Multilayer
ceramic capacitor
Coil inductor
with air core
Carbon/metal
film resistor
Notes: <number>

## Slide 12: Passive Lumped Components for Incorporation into PCB and Other Substrates
Deposited carbon film, or semiconductor
Low resistance
High resistance
Resistors
Interdigital Capacitor
Series Single-Loop Spiral Inductor
Series Multi-Loop Spiral Inductor
Air Bridge
Shunt Multi-Loop Spiral Inductor
Via
Microstrip Line
Metal-Insulator-Metal (MIM)
Capacitor
High r dielectric
Add the corresponding schematics for these:
Notes: <number>

## Slide 13: Single Lumped Element Transformation Network
ZL = RL+ jXL
jX
Zs = ZL + jX
ZL
2-port network
Notes: <number>

## Slide 14: Single Lumped Element Transformation Network (cont’d)
ZL = RL+ jXL
jB
Ys = YL + jB
ZL
2-port networks
Notes: <number>

## Slide 15: Dual Lumped Element Transformation Network
jX
jB
RL + jXL
If Zs = Rs + jXs is given,
we could solve for X and
B by equating the real and
imaginary parts of the above expression:
This configuration
is only applicable
for Rs > RL
(1.1)
Notes: <number>

## Slide 16: Dual Lumped Element Transformation Network (cont’d)
RL + jXL
jX
jB
If Zs = Rs + jXs is given,
again we could solve for
X and B by equating the
real and imaginary parts
of the above expression:
This configuration
is only applicable
for RL> Rs
(1.2)
Notes: <number>

## Slide 17: Example 1.1
Transform ZL=100 + j80 to 50 + j40 at 410 MHz.
Since B is +ve, a capacitor can be used to realize it:
Since X is +ve, an inductor can be used to realize it:
RL>Rs
Notes: <number>

## Slide 18: Synthesizing Reactance (X) and Susceptance (B) Using Lumped Elements
For X:
For B:
X > 0 : Use an inductor to synthesize it.
L
X < 0 : Use a capacitor to synthesize it.
C
B > 0: Use a capacitor to synthesize it.
C
B < 0: Use an inductor to synthesize it.
L
Notes: <number>

## Slide 19: Example 1.1 (cont’d)
The final schematic:
100+j80
50+j40
At 410 MHz Only!
44.83 nH
5.47 pF
Notes: <number>

## Slide 20: Exercise
Transform ZL= 50 + j100 to 300 – j10 at 900 MHz using two lumped element matching networks.
Notes: <number>

## Slide 21: Example 1.2
Repeat Example 1.1 using a Smith Chart.
Notes: <number>

## Slide 22: 2.0 Nodal Q Factor and Approximate Bandwidth of the Impedance Transformation Network
Notes: <number>

## Slide 23: Bandwidth of the Matching Network
Assuming in Example 1.1, the load ZL is actually given by an inductor in series with a resistor, so that at 410 MHz, we obtain ZL = 100 + j80.
We input the above schematic in a circuit simulator (PSpice®) and run a frequency sweep (change the frequency of the source Vs while measuring I & V) from 100 MHz to 800 MHz.
44.83 nH
100 
Zs= 50+j40
at 410 MHz
5.47 pF
ZL
31.05 nH
I
Vs
V
Notes: <number>

## Slide 24: Bandwidth of the Matching Network (cont’d)
Within a range of frequencies near to the operating frequency fo= 410 MHz, Zs= Rs + jXs is quite near the desired value. We will call this range of frequency the bandwidth (BW) of the transformation network.
Re(Zs)
Im(Zs)
We see that the matching
network only transforms ZL
to 50+j40 at 410 MHz; at other
frequencies, Zs gradually
deviates from the desired
value.
410 MHz
Notes: <number>

## Slide 25: Bandwidth of the Matching Network (cont’d)
To examine this closer, we plot Zs in terms of its magnitude and phase.
|Zs| and Arg(Zs) are very close to the pattern of the series RLC circuit near operating frequency fo
|Zs|
Arg(Zs)
271.76 MHz
Following the theory
of the series RLC
network, we define
the 3 dB BW as the
range of freq., where
|Zs| is less than
, and Zo is the
magnitude of the
impedance at the
operating freq.,
fo = 410 MHz.
We see that the
‘measured’ BW is:
BW = 271.76 MHz
Notes: <number>

## Slide 26: Bandwidth of the Matching Network (cont’d)
Now consider the circuit of Example 1.1 again. We could compute a quantity known as the nodal Q factor, Qn as follows:
44.83 nH
100 
Zs= 50+j40
at 410 MHz
5.47 pF
ZL
31.05 nH
jX
jB
X=115.498, B=0.014
ZL=
100+j80
jX
X=115.498
Y’ = G’ + jB’
0.0061+ j0.0091
or
Z’ = 50.06 – j75.50
Last element
Compute the impedance or admittance
without the last element of the network.
Notes: <number>

## Slide 27: Bandwidth of the Matching Network (cont’d)
We can calculate the BW of the system using the equation in (1.4):
Surprisingly this is quite near the measured value using simulation. Both the measured and calculated BW using this method will match even closer if Zs is real, or Xs=0. This applies to all lumped element transformation networks as well (three elements or more).
When Xs is not 0, there is an error, the larger the |Xs|, the greater the error. However, this does not illustrate that we could in general compare the BW of various transformation networks merely by calculating Qn.
Generally high Qn denotes narrow BW, low Qn denotes wide BW.
271.76 MHz
Notes: <number>

## Slide 28: Nodal Q Factor, Qn
Qn for some favorite transformation networks:
jX2
jX1
jB1
ZL
Z’ = R’ + jX’
Y’ = G’ + jB’
jX1
jB1
ZL
Z’ = R’ + jX’
Y’ = G’ + jB’
jX1
jB2
ZL
Z’ = R’ + jX’
Y’ = G’ + jB’
jB1
TL1
jB1
ZL
Z’ = R’ + jX’
Y’ = G’ + jB’
Notes: <number>

## Slide 29: Example 2.1
Transform the load ZL = 200 – j40 to 50 + j20 at 2.4 GHz. Find the nodal Q factor and estimate the bandwidth of the circuit. Use a Smith Chart to aid the design.
Zs
ZL
Z’
X=109.2
ZL=200–j40
Zs=50+j20
B=0.00756
jX
jB
B
X
Notes: <number>

## Slide 30: Constant Qn Circles
Given a certain Qn, we can find the locus or curve of the corresponding impedance point on the Smith Chart. It turns out this locus is a circle, known as the Constant Qn Circle.
Qn depends on the point location on the Smith Chart. We can join all points on the Smith Chart given a similar Qn to form a curve or locus. It happens that this locus is a circle, known as the Constant Qn circles.
The center and radius for the circles can be derived as follows.
From the theory on the Smith Chart:
(2.1)
r
x
Notes: <number>

## Slide 31: Constant Qn Circles (cont’d)
Qn=1.0
Qn=1.0
Qn=0.5
Qn=0.5
Qn=3.0
Qn=3.0
Qn Radius Center
0.5 2.2360 0j2.000
1.0 1.4142 0j1.000
2.0 1.1180 0j0.500
3.0 1.0541 0j0.333
5.0 1.0198 0j0.200
Notes: <number>

## Slide 32: Limitation of the 2-Lumped Element Network
By now it is obvious of the limitation of the 2-lumped element network. For instance, in Example 2.1, there are only two ways to transform ZL= 200 – j40 to Zs= 50 + j20.
Therefore we cannot control the nodal Q factor of the 2-lumped element network, it is determined by the values of ZL and Zs.
Using an extra element, we have an extra degree of freedom and we can control the value of Qn in addition to performing impedance transformation/matching. This is the advantage of using the T or Pi network.
Notes: <number>

## Slide 33: Three or More Lumped Elements Transformation Network
For more than three lumped elements, an analytical method such as the one shown in previous slides is very cumbersome to apply.
It is easier to perform a 3-element transformation network design with the aid of the Smith Chart.
As opposed to the 2-lumped element network, a 3- or more lumped element network does not suffer from any blind spot. It can transform any passive load ZL to any required impedance value.
Notes: <number>

## Slide 34: Example 2.2
Repeat Example 2.1 using a 3-element impedance transformation network, either T or Pi, with the aid of a Smith Chart. Qn must be equal to 3. (ZL= 200 – j40, Zs= 50 + j20 at fo = 2.4 GHz).
ZL
jX2
jX1
jB1
Z’
X1 = 294.0
B1 = 0.0083
X2 = 174.6
Qn=3
Qn=3
B1
X1
X2
Z’
L1= 19.5 nH
C1 = 0.55 pF
L2 = 11.58 nH
Zs
Notes: <number>

## Slide 35: Example 2.3
Repeat Example 2.2 using a 3-element transformation network, either T or Pi, with the aid of a Smith Chart. Qn must be equal to 5. (ZL= 200 – j40, Zs = 50 + j20 at 2.4 GHz).
ZL
jX2
jX1
jB1
Z’
X1 = 488.6
B1 = 0.00584
X2 = 261.0
L1= 32.4 nH
C1 = 0.387 pF
L2 = 17.3 nH
Zs
Qn=5
Qn=5
B1
X1
X2
Z’
Notes: <number>

## Slide 36: Zs vs. f from the PSpice Simulation
Rs
Rs
Xs
Xs
Qn=3
Qn=5
Both circuits from Example
4 and 5 are fed into PSpice.
AC simulation is run from
1.8 GHz to 2.8 GHz and the
results are compared. It is
observed that the T network with a higher nodal Q factor has a narrower BW, characterized by a more rapid deviation from fo = 2.4 GHz.
Resonance
Frequency
Notes: <number>

## Slide 37: Exercise
Repeat Example 2.3 using a 3-element T transformation network, with the aid of a Smith Chart. Qn must be equal to 1. (ZL = 200 – j40, Zs = 50 + j20). Can you synthesize the T network? Suggest a solution for this.
Notes: <number>

## Slide 38: Exercise
Repeat Example 2.3 using a 3-element Pi transformation network, with the aid of a Smith Chart. Qn must be equal to 3. (ZL = 200 – j40, Zs = 50 + j20). Can this impedance transformation be realized? Discuss the result.
Notes: <number>

## Slide 39: Pros & Cons of the Lumped Element Network
The lumped element network is compact, small in size.
Suitable for use up to a frequency of 2.5 GHz.
Not every value of inductance and capacitance is available.
Stability, value changes with temperature.
Tolerance of components.
Difficult to tune.
Higher cost.
Notes: <number>

## Slide 40: Appendix 1 – Series/Parallel RLC Network, Nodal Q Factor Concepts
Notes: <number>

## Slide 41: Q Factor
The Q Factor of a series or parallel impedance is defined by:
By circuit theory and phasor analysis, we can easily show that (see any undergraduate level engineering circuit analysis textbooks):
jX
V()
I()
R
jB
V()
I()
G
(A.1a)
(A.1b)

## Slide 42: Q Factor Example
For instance consider a 47nH SMD inductor, in 0603 package. The inductor suffers some power losses, due to parasitic resistance, dielectric loss and skin effect. These losses can be accounted for by a series resistor. The resistance is usually frequency dependent.
Suppose at 100MHz, R = 0.9Ω. Therefore:
The Q factor thus indicate how good (or near to ideal) is the inductor. The higher the Q factor (e.g. the smaller is R), the better is the inductor.
A similar conclusion can be reached for a lossy capacitor, which is represented as a parallel RC network.
47nH
0603
47nH
0.9Ω
@ 100MHz

## Slide 43: Q Factor for Higher Order Networks
The concept of Q factor can be extended to series RLC network, and also parallel RLC network.
The impedance (or admittance) of these networks exhibit a resonance phenomena, in that the impedance (or admittance) becomes real at one particular frequency, called the Resonance Frequency (fo).
For series and parallel RLC networks, there is an interesting relationship between the Q factor, fo and the 3 dB bandwidth. The Q factor is usually used to indicate the 3 dB bandwidth of series and parallel RLC networks, see equations (A.2).
The definition of Q factor can also be applied to higher order circuits with more than one capacitors and inductors. Of course the expression for Q factor as a function of frequency will be more complicated than equations (A.1a) and (A.1b), and there is no elegant relationships between fo, Q factor and bandwidth as shown in equation (A.2) (see next slide).

## Slide 44: Q Factor and Series/Parallel RLC Network
Rp
Cp
Lp
Z
Rs
Cs
Ls
Z
(A.2)
o
Notes: <number>

## Slide 45: Frequency Response of the Series/Parallel RLC Network
Parallel RLC
R Q
R Q
Series RLC
R Q
R Q
+90o
Arg(Z())
-90o
0

+90o
Arg(Z())
-90o
0

|Z()|

o
R
3 dB Bandwidth
1
2

o
R
3 dB Bandwidth
1
2
|Z()|
Notes: <number>

## Slide 46: Poles and Zeros of Series and Parallel RLC Networks
For series RLC:
Two complex conjugate zeros
on the s-plane
One pole on the s-plane
For parallel RLC:

j
x
Resonance
Frequency
Two complex conjugate poles
One zero

j
x
Resonance
Frequency
x
Resonance frequency is
the frequency where an input impedance to a passive RLC network becomes real.
Pole
Zero
Notes: <number>

## Slide 47: Uses of RLC Networks
Series and parallel RLC networks are very useful. They are used as building blocks for band-pass filter (BPF) and band-stop filter (BSF), and also as resonator for oscillator and tuned amplifiers.
Consider series RLC network, you can see that at the resonance frequency fo current can easily flow through the network, but will be suppressed at lower or higher frequencies. Hence it has a band-pass response.
If we connect the series RLC in a shunt manner, then it has band-stop response since current at fo current will be shunted to ground.
Band-pass Response
Band-stop
Response

## Slide 48: Resonance Frequency of Higher Order Systems
For a system with more than one L and C, there will be higher order poles and zeros. These will distort the location of the fundamental resonance frequency of the network and introduce higher order resonance frequencies.

j
x
x
x
x
Higher order
poles and zeros
fresonance1
fresonance2 (higher
order)
fresonance3 (higher
order)
Z
Notes: <number>

## Slide 49: Resonance Frequency of Higher Order Systems (cont’d)
Since each resonance frequency is still due to the dominant poles and zeros, the concept of Q factor with regards to a 3 dB bandwidth can still be applied to the higher order network.

j
x
x
x
x
fresonance1
fresonance2 (higher
order)
Dominant poles and zeros contributing to (series) fresonance3
Dominant poles and zeros contributing to (parallel) fresonance1
Dominant poles and zeros contributing to (parallel) fresonance2
fresonance3 (higher
order)
Notes: <number>

## Slide 50: Resonance Frequency of Higher Order Systems (cont’d)
f
|Z|
0
fresonance1
fresonance3
fresonance2
Leq1
Ceq1
Req1
Leq2
Ceq2
Req2
Ceq3
Req3
Leq3
Notes: <number>

## Slide 51: Impedance Transformation Network as a Resonating Network
Impedance
Transform
Network
(Lossless)
RL
jXL
ZI
Impedance
Transform
Network
(Lossless)
RL
jXL
ZI
Augmented Network
If ZI = Rs, then the augmented
network is actually under
resonance during normal
operation. The concept of Q
factor can be applied. If ZI is
complex, the concept of Q factor
can still be applied if Xs is
small.
Notes: <number>

## Slide 52: 3.0 Distributed/Hybrid Impedance Transformation Network
Notes: <number>

## Slide 53: Distributed Transformation Network
Single stub transformation network.
jB can be implemented using a Tline with open/short circuit at one end. Lumped elements such as SMD capacitors can also be used. In this case, the network is known as a hybrid network.
No blind spot.
(3.1)
ZL
TL1
jB1
Z’ = R’ +jX’
Y’ = G’ +jB’
Zs
Zc , 
l
Notes: <number>

## Slide 54: Example 3.1
Transform the load ZL = 200 – j40 to 50 + j20 at 2.4 GHz. Find the nodal Q factor and estimate the bandwidth of the circuit. Use a Smith Chart to aid the design. Synthesize the circuit.
SWR
circle
Z’

B1
Zs
ZL
TL1
jB1
ZL
Z’ = R’ + jX’
Y’ = G’ + jB’
Notes: <number>

## Slide 55: Example 3.1 (cont’d)
Use a microstrip line to implement the circuit, Zc = 50 . Dielectric constant = 4.6, and d = 1.57 mm.
Step 1: Synthesize Tline.
From the microstrip Tline design example of Chapter 1, we notice that the required W must be roughly 2.88 mm.
Notes: <number>

## Slide 56: Example 3.1 (cont’d)
Step 2: Synthesize jB1.
We can use an inductor for B1:
Or we can use another short circuit Tline to generate B1:
Notes: <number>

## Slide 57: Example 3.1 (cont’d)
Thus the final circuit...
2.88 mm
11 mm
Other circuit
here
Or...
2.88 mm
5.4 mm
11 mm
Other circuit
here
ZL
Notes: <number>

## Slide 58: Double Stub Distributed Network
Can be adjusted
The single stub network suffers from the disadvantage of requiring a variable length of the Tline between the load and the stub. This may not be a problem for a fixed transformation network, but would pose some difficulties if an adjustable tuning network is desired.
To overcome this disadvantage, a double stub transformation network is used.
TL2
jB2
ZL
jB1
Zs
TL1
Optional
ZL’
Notes: <number>

## Slide 59: Double Stub Distributed Network (cont’d)
TL2
jB2
ZL
jB1
Zs
TL1
B1
TL2
B2
TL1
ZL
Zs
Assuming we want to
transform ZL to
Zs = 50 Ω
Adjustable short-circuit stubs
to produce various susceptance B
Rigid coaxial waveguide
Notes: <number>

## Slide 60: Quarter-Wave Transformer
(3.2a)
A quarter-wave transformer is a simple and useful circuit for matching a real load impedance to a transmission line or another real source impedance. An additional feature is that it can be extended to a multi-section design for a broader bandwidth.
Consider a terminated lossless Tline again, using the input impedance relation of the terminated Tline:
ZL
l
z = 0
Zc
Zin
Z1
Tline1
(3.2b)
To match Tline1 to ZL:
Notes: <number>

## Slide 61: Example 3.2
Design a quarter-wave transformer to transform a 200  load into 50  at 2.4 GHz using a microstrip line constructed on a dielectric with a dielectric constant of 4.6 and a thickness of 1.57 mm.
Using the microstrip design equations of “Chapter 1 – Advance Transmission Line”:
s = w/d
Notes: <number>

## Slide 62: Example 3.2 (cont’d)
200
18.0 mm
0.66 mm
2.88 mm
50 
Microstrip
Line
Top view
In this analysis, the reactance associated
with the discontinuities must be taken into account. The proper compensation technique must be used.
Notes: <number>

## Slide 63: Limitation of the Quarter-Wave Transformer
(3.3)
Although a quarter-wave transformer can, in theory, be used to match a complex impedance, it is more common to use it to match a real impedance.
However, bear in mind that a complex load impedance can always be transformed to a real impedance by adding the correct series or shunt reactive component.
At the operating frequency fo, the electrical length of the matching section is o/4. But at other frequencies, the length is different, so a perfect match is no longer obtained. The quarter-wave transformer has a limited bandwidth, like other transformation methods.
Writing Zin as:
Extra
This parameter is
frequency dependent
Notes: <number>

## Slide 64: BW of the Quarter-Wave Transformer
Using (3.2a) and (3.3):
For a frequency near fo, l  o /4, sec2 >>1, and this simplifies to:
(3.4a)
(3.4b)
Extra
Notes: <number>

## Slide 65: BW of the Quarter-Wave Transformer (cont’d)
Assume the maximum mismatch we can tolerate is ||max = m= 0.1, or return loss of –20log10(0.1) = –20 dB.
Plotting || =  versus  = l, we can determine the bandwidth of the quarter-wave transformer.
Extra
Notes: <number>

## Slide 66: BW of the Quarter-Wave Transformer (cont’d)
(3.5)

Quarter wavelength
Putting m into (3.4a) and solve for m :
Assuming the TEM or quasi-TEM mode:
And the bandwidth is given by:
Extra
Notes: <number>

## Slide 67: Example 3.3
From Example 5.1 of Chapter 1
Design a single-section quarter-wave transformer to match a 10 Ω load to a 50 Ω Tline, at fo = 2.4 GHz. Determine the bandwidth for which VSWR<1.3. Use the microstrip line design example of Chapter 1 to physically realize it.
Extra
Notes: <number>

## Slide 68: Pros & Cons of the Distributed Network
Easy to fabricate and incorporate into a microwave circuit. Utilizes the PCB itself.
Cheap and stable, good tolerance if the mechanical tolerance is properly controlled.
Easier to tune than the lumped element network.
Modern manufacturing facilities use LASER to trim the transmission line dimension during tuning.
At a low frequency, the length of the Tline can be unwieldy large.
Notes: <number>

## Slide 69: Increasing the Bandwidth of Quarter-Wave Transformer
From equation (3.5) we observe that the bandwidth increases (for fixed mismatch m) if the values of Zc and ZL are near.
For instance: ZC= 50, ZL= 80, fo= 3000MHz and m = 0.05:
If we reduce ZL to 60, keeping all other parameters the same:
The bandwidth increases from 0.81GHz to 2.22GHz. This fits our common sense as structure with less mismatch should have better matching across frequency.
ZC
ZL
Z1
ZC
ZL
Z1
Smaller BW
Larger BW
Extra

## Slide 70: Increasing the Bandwidth of Quarter-Wave Transformer (cont’d)
Thus came the idea that if we use multiple transmission line sections, with the characteristic impedance ZC of each section differ from one another by a small amount, an impedance transformer with bandwidth much larger than a single section can be attained.
A reflection coefficient n can be assign to the interface of each section, and each n will be small since ZC of each section differs by small amount.
Z0
Z1
Z2
ZL
Zn , where n = 0, 1, 2, … , the index of each section must increase or decrease monotonically, Zn must be real.
Extra

## Slide 71: Theory of Small Reflection – Single Section Transformer
Consider a single section transmission line, with the requirement 0  0 and 1  0.
There are two step discontinuities, and at each discontinuity, a total of 4 local reflection and transmission parameters can be defined:
Z0
Z1
ZL
Z0
Z1
Local reflection
coefficient
Overall reflection
coefficient
Extra

## Slide 72: Theory of Small Reflection – Single Section Transformer (cont’d)
Multiple reflection occurs when the system is excited by an incident wave, and we can compute the total reflection coefficient at the input as shown:
Z0
Z1
ZL
1
Incident
wave of
magnitude 1
Total reflected wave is the sum of individual
reflected components:
Since 0 and 1 0:
(3.6)
A geometric
series
Extra

## Slide 73: Theory of Small Reflection – Multiple Sections Transformer
By extension of equation (3.6) to multiple sections transformer circuit, with each section of similar l:
We observe that equation (3.7) is a power series in terms of e-j2 with 4 degrees of freedom.
By carefully choosing the values of 0, 1, 2, 3, we can make () goes to 0 at  =l=/2 (i.e. l = /4) and possess certain bandwidth around  =/2.
Z0
Z1
Z2
Z3
ZL
Total reflection coefficient
looking into discontinuity
between section 1 and 2
(3.7)
Extra

## Slide 74: Multiple Sections Transformer Implementation
Once each n is fixed, we can back calculate the corresponding characteristic impedance of each transmission line section.
The more sections are used, the more degrees of freedom we have and the better is the ability of the multiple section transformer to approximate certain reflection coefficient profile as a function of frequency.
Examples of typical profiles are the Binomial and Chebyshev profiles.
Extra

## Slide 75: Example – Comparison of Matching Bandwidth
Comparison of the matching characteristics for quarter-wave transformer and Binomial multiple section transformer for ZL = 100, Z0 (the feed transmission line impedance) = 50.
N = Number of sections
N=2
N=3
N=4
Quarter-wave
transformer
Extra

## Slide 76: Tapered Line Impedance Transformer
We could also increase the number of sections in the multiple section transformer while gradually reducing the length of each section. In the limit of infinite sections, this becomes the Tapered Line Impedance Transformer.
Top view of tapered line transformer
Extra

## Slide 77: Comparison of Various Multiple Sections Transformer
Binomial Transformer
impedances of consecutive 1/4 wave lines are proportional to binomial coefficients.
gives a maximally flat passband characteristic.
Chebyshev Transformer
wider bandwidth than the binomial transformer for the same number of 1/4 wave sections.
ripple over passband.
Tapered Transition
characteristic impedance varies continuously in a smooth fashion.
taper length of 0.5 –1.5 wavelength required.
Extra
Notes: <number>

## Slide 78: References
[1] R. Ludwig, P. Bretchko, “RF Circuit Design – Theory and Applications”, 2000, Prentice-Hall.
[2] D.M. Pozar, “Microwave Engineering”, 2nd Edition, 1998, John-Wiley & Sons (3rd Edition, 2005 by John-Wiley & Sons is also available).
[3] R.E. Collin, “Foundation for Microwave Engineering”, 2nd Edition, 1992, McGraw-Hill.
Notes: <number>