## Slide 1: ME1000 RF CIRCUIT DESIGN
<number>
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 5. Coaxial Components and Rectangular Waveguide Components
Notes: <number>

## Slide 3: 1.0 Coaxial Components

## Slide 4: Introduction
The microstrip and stripline structures are important for guiding electromagnetic waves on the printed circuit board (PCB).
For system-to-system or board-to-board, a cable is used for guiding electromagnetic waves.
The most common cable type for this purpose is the coaxial cable, which consists of two circular conductors: one is hollow and the other is usually solid, sharing a similar center axis (hence the name coaxial).
Although generally used for transporting high-frequency electrical signals, the coaxial cable can also be used for low-frequency signals by virtue of it being a two-conductor interconnection. One conductor would serve as the signal and the other for the return current.
The coaxial cable can support TEM, TE, and TM modes of propagating electromagnetic waves.

## Slide 5: Pictures of Coaxial Cables
Rigid coax cable
Semi-rigid coax cable
Flexible coax cable
Flexible Coax Cable
Semi-rigid Coax Cable
Inner conductor
Outer conductor
Dielectric (usually
uniform) filling the gap between conductors
Outer jacket
Outer jacket
Conducting
braid

## Slide 6: Flexible Coaxial Cables
Velocity of Propagation:
Solid Dielectric = 66.5 – 69% of the speed of light in vacuum
Foamed Dielectric = 72 – 85% of the speed of light
Single braid
Double braid
Outer jacket
Outer jacket
Inner jacket
Conducting braid
Dielectric
Center conductor
Outer braid
Inner braid
Dielectric
Center conductor
Notes: <number>

## Slide 7: Semi-Rigid Coaxial Cables
Solid Dielectric
Air Articulated
Typical dielectric types
are PTFE (Polytetraflouroethylene), foam, and air.
Center conductor
Solid outer conductor
Solid outer conductor
Center conductor
Dielectric
Dielectric sheet
Notes: <number>

## Slide 8: Coaxial Cable Parameters
The dominant propagation mode for electromagnetic waves in a coaxial cable is the TEM mode.
In this mode, the per unit length RLCG parameters (under low loss conditions) are given as follows:
(1.1)
(1.2a)
(1.2b)
(1.2c)
(1.2d)
D
d
c = Conductivity of the conductor
d = Effective conductivity of the dielectric at 
s = Skin depth of the conductor at 
Conductor
Dielectric
Notes: <number>

## Slide 9: Coaxial Cable Parameters (cont’d)
From these basic RLCG parameters under the TEM mode, other parameters of interest such as the characteristic impedance, the attenuation factor, the velocity of propagation, the maximum power handling, and the cut-off frequency (when non-TEM modes start to propagate) can be derived.
Other parameters, which are influenced by the mechanical aspects of the coaxial cable are the flexibility of the cable, the operating temperature range, the connector type, the cable diameter, the cable noise or shielding effectiveness, etc.
Of these, the most importance is the characteristic impedance Zc. Under lossless approximation, with R = G = 0, the characteristic impedance is given as follows:
Typical Zc values are 50, 75, and 93. Of these, Zc = 50 is the most common.
(1.3)

## Slide 10: Why Zc = 50 Ohms?
Most coaxial cables have Zc = 50  under low loss conditions, with 75  being used in television systems. The original motivation behind these choices is that an air-filled coaxial cable has a minimum attenuation for Zc = 75 , while the maximum power handling occurs for a cable with Zc = 30 .
A cable with Zc = 50  thus represents a compromise between minimum attenuation and maximum power capacity.
Bear in mind, this is only true for air-filled coaxial cable, but the tradition prevails for coaxial cable with other types of dielectric.
In the old days, a coaxial cable with Zc = 93  is also manufactured; these
are mainly used for sending digital signals between computers. The capacitance per unit length C is minimized for this impedance value.
Notes: <number>

## Slide 11: Cable Specifications
A series of standard types of coaxial cables were specified for military use in the United States, in the form "RG-#" or "RG-#/U". These specifications date back to World War II and were listed in MIL-HDBK-216 (1962).
These designations are now obsolete. The current US military standard is Military Specifications MIL-C-17. MIL-C-17 numbers, such as "M17/75-RG214," are given for military cables and manufacturers’ catalog numbers for civilian applications.
However, the RG-series designations were so common for generations that they are still used today, although the handbook has since been withdrawn.
Notes: <number>

## Slide 12: Cable Specifications (cont’d)

## Slide 13: Upper Usable Frequency
Since a coaxial cable supports TEM, TE, and TM electromagnetic wave propagation modes, the TE and TM modes will come into existence for sufficiently high operating frequency.
The Upper Usable Frequency (UUF) for coaxial cable refers to the frequency where the first non-TEM mode comes into existence.
For coaxial structure, the non-TEM mode with the lowest cut-off frequency (fc) is the TE11 mode.
The UUF can be estimated by Ref. [1]:
(1.4a)
(1.4b)
d
D
r
where c = speed of light in vacuum

## Slide 14: Example
For instance for RG-142 coaxial cable, with inner conductor radius = 0.89mm and outer conductor radius = 2.95mm, the estimated UUF is:
As a safety precaution we usually include some margin, say 5%, thus the upper usable frequency is rated at:

## Slide 15: Connectors and Adapters
The ends of a coaxial cable are fixed to connectors.
Such connectors are cylindrical in shape, thus the connectors also exhibit upper usable frequency limit.
Some common examples of connectors/adapters for coaxial cable are shown below.
3.5 mm/SMA connectors
PCB to coaxial adapter
Various
3.5 mm/SMA to N type
coaxial adapter
BNC to N type
adapter
BNC to SMA
adapter
Various SMA-to-SMA
(M-to-M and F-to-F)
connectors

## Slide 16: Connectors and Adapters (cont’d)
A comparison of RF/microwave connectors usable frequency range:
  BNC (baby N connector), for DC to 400 MHz.
  N connector, for DC to 8 GHz.
  SMA (Sub-miniature version A) connector (inner diameter, D 4.6mm), for DC to 18 GHz.
  3.5 mm connectors, for DC to around 30 GHz.
  2.9 mm connectors, for DC to around 40 GHz.
  2.4 mm connectors, for DC to around 50 GHz.
  1.8 mm connectors, for DC to around 65 GHz.

## Slide 17: Attenuators
T-section
-section
A commercial
coaxial attenuator
Conductor
Lossy material (for instance carbon
based)
Equivalent to
series resistor
Equivalent to
parallel resistor
Notes: <number>

## Slide 18: Terminations
A termination is a component which absorb all incident wave.
This can be approximated by having an attenuator in series with a short circuit. For instance in the example below, the reflected wave power will be 40 dB (or 10000 times) smaller than the incident wave power.
A range of
coaxial terminations
20-dB attenuator
Short-circuit plate
Short-circuit plate
Tapered load
Notes: <number>

## Slide 19: 2.0 Rectangular Waveguide

## Slide 20: Introduction
As we have seen earlier waveguides refer to any structure that can guide electromagnetic (EM) waves along its axial direction, which include transmission line.
Here we consider waveguide as specifically refers to long metallic structures with only 1 piece of conductor between the source and load end.
These metallic structures are usually hollow, so that EM fields are confined within the hollow and be guided along the axial direction.
Applying Maxwell’s Equations with the proper boundary conditions (see Appendix) shows that propagating EM waves can be supported by the waveguide.
Due to the absence of center conductor, only TE and TM mode exist.

## Slide 21: Rectangular Waveguide
b
a

## Slide 22
EM Waves Propagating Modes in Waveguide
Cut-off frequency for TEmn
or TMmn mode
The corresponding cut-off wavelength
for TEmn or TMmn mode
Thus we see that for m=1,
n=0 — the TE10 has the lowest cut-off frequency, and is the dominant mode.
a
b
Ey
Ex
Ey
Ex
Ey
Ex
TE10
TE11
TE21
Variation of the Ey component along the x-axis
Variation of the Ex component along the y-axis

## Slide 23
Dominant Mode for Rectangular Waveguide
Recommended operating
frequency range for a
rectangular waveguide
For TE10 mode, m=1, n=0,
thus the cut-off wavelength
is:

## Slide 24
Waveguide Wall Currents
The current on the wall of the rectangular waveguide at a certain instance in time for TE10 mode.
We can create a narrow slot
parallel to the center axis of
the waveguide without
disturbing the current flow,
hence the internal EM fields.
g/2
g = Guide wavelength

## Slide 25: Slotted-Line Probe
A short metal probe can be inserted into the slot with minimal disturbance to the EM fields of the TE10 mode. This probe can be used to measure the relative strength of the electric field in the waveguide cavity. Usually the microwave EM fields will be modulated by a low-frequency signal, and the diode/capacitor pair acts as an envelope detector to demodulate this low-frequency signal.
A
SWR meter
Rectifier
Variable short-circuit
tuner
Metal probe
(to detect electric
field intensity)
Rectangular waveguide
with slot

## Slide 26: Bends
H-bend
E-bend
a
b
a
b
E
H
The orientation of electric
(E) field is altered.
The orientation of magnetic
(H) field is altered.

## Slide 27
Matched Terminations
The gradual transition from the rectangular waveguide to the lossy material ensures minimal reflection of the electromagnetic wave.
Lossy material
Waveguide
Heatsink
Usually the heatsink will be
attached to the exterior for
heat dissipation
Rectangular
waveguide
Rectangular
waveguide
Short circuit

## Slide 28
Attenuators
An example of an waveguide attenuator: the lossy material is shaped to provide a gradual change in the waveguide internal geometry, resulting in a small reflection of the incident wave.
Tapered lossy material

## Slide 29: Waveguide Tees
Often used as
power dividers
E-plane Tee
1
2
3
H-plane Tee
1
2
3
E
1
3
2
3
1
2

## Slide 30: Circulator
An example of a rectangular waveguide circulator (see Chapter 4):
Permanent magnets
Ferrite post
B field

## Slide 31: Waveguide to Coaxial Adapter
Coaxial cable
Waveguide
A waveguide
to coaxial
adapter
Front view of
the adapter
Short
circuit
Metallic Ridges
Note: for modern design the ridges
can be replaced with taper structure.

## Slide 32: Appendix 1: Solution of Electromagnetic Fields for Rectangular Waveguide

## Slide 33: Introduction
Rectangular waveguides are one of the earliest waveguide structures used to transport microwave energies.
Because of the lack of a center conductor, the electromagnetic field supported by a waveguide can only be TM or TE modes.
For rectangular waveguide, the dominant mode is TE, which has the lowest cut-off frequency.

## Slide 34: Why does TEM Mode Not Exist in a Waveguide?
From Maxwell’s equations, the magnetic flux lines always close upon themselves. Thus if a TEM wave were to exist in a waveguide, the field lines of B and H would form a closed loop in the transverse plane.
However, from the modified Ampere’s law:
The line integral of the magnetic field around any closed loop in a transverse plane must equal the sum of the longitudinal conduction and displacement currents through the loop.
Without an inner conductor and with the TEM mode, there is no longitudinal conduction current and displacement current inside the waveguide. Consequently, this leads to the conclusion that there can be no closed loops of magnetic field lines in the transverse plane.

## Slide 35: Rectangular Waveguide
The perspective view of a rectangular waveguide is shown below.
The following slides will illustrate the standard procedures to obtain the electromagnetic (EM) fields guided by this structure.
z
y
x
0
a
b
Assume to be a very
good conductor (PEC)
and very thin
 

## Slide 36: TE Mode Solution
To obtain the TE mode electromagnetic (EM) field pattern, we use the systematic procedure developed in Chapter 1 – Advanced Transmission Line Theory.
We start by solving the pattern function for the z-component of the magnetic field:
Problem (1.1) is called the Boundary Value Problem (BVP) in mathematics.
Once we know the function of hz(x,y), the EM fields are given by:
and boundary conditions
(1.1)
(1.2b)
(1.2a)
Note: We only consider the
propagation in the positive
direction; treatment for the
negative propagation is similar.

## Slide 37: TE Mode Solution (cont’d)
Expanding the partial differential equation (PDE) of (1.1) in Cartesian coordinates:
Using the Separation of Variables Method, we can decompose hz(x,y) into the product of two functions and kc2 to be the sum of two constants:
Putting these into (1.3), and after some manipulation, we obtain two ordinary differential equations (ODEs):
(1.3)
(1.5a)
(1.5b)
(1.4a)
(1.4b)

## Slide 38: TE Mode Solution (cont’d)
From elementary calculus, we know that the general solution for (1.5a) and (1.5b) are:
Thus hz(x,y) is given by:
(1.6a)
(1.6b)
(1.7)

## Slide 39: TE Mode Solution (cont’d)
A, B, C, and D in (1.7) are unknown constants, to be determined by applying the boundary conditions that the tangential electric field must vanish on the conductive walls of the waveguide. From (1.2b):
z
y
x
0
a
b
(1.8a)
(1.8b)

## Slide 40: TE Mode Solution (cont’d)
Using (1.7) and applying the boundary condition (1.8a):
Using (1.7) and applying the boundary condition (1.8b):
In the above equations, we can combine the product of AC — let’s call it R. Common sense tells us that R would be different for each pair of integer (m,n), thus we should denote R as: Rmn

## Slide 41: TE Mode Solution (cont’d)
From (1.4b), kc and the propagation constant  are given by:
Since kc and  also depend on the integer pairs (m,n), it is more appropriate to write these as:
(1.9a)
(1.9b)

## Slide 42: TE Mode Solution (cont’d)
With these information, and using (1.2a) and (1.2b), we can write out the complete mathematical expressions for the EM fields under the TE propagation mode for a rectangular waveguide:
(1.10a)
(1.10b)
(1.10c)
(1.10d)
(1.10e)

## Slide 43: Cut-Off Frequency for TE Mode
Notice from (1.9b) that the propagation constant mn is real when:
When mn is imaginary, the EM fields cannot propagate.
Since =2f, we can define a limit for the frequency f as follows:
The lower limit of this frequency is called the Cut-off Frequency fc.
(1.11)

## Slide 44: Cut-Off Frequency for TE Mode (cont’d)
The TE mode electromagnetic field is usually labeled as TEmn since the mathematical function of the field components depends on the integer pair (m,n).
The pair (m,n) cannot be both zeros, otherwise from (1.10a) to (1.10e), Ex+, Ey+, Hx+, Hy+, Hz+ are all zero — no fields at all! This is a trivial solution, although a valid one.
The smallest combination of (m,n) are (m,n) = (1,0) or (0,1).
Since a > b (the lateral dimensions of the rectangle), we see that (m,n) = (1,0) produces a smaller fc, thus a lower cut-off frequency. Therefore the TE propagation mode TE10 is the dominant mode for TE waves. Its corresponding cut-off frequency is given by:
An excitation frequency greater than will cause EM waves to propagate within the rectangular waveguide.

## Slide 45: Example
Consider a rectangular waveguide, a = 45.0 mm, b = 35.0 mm, filled with air ( = o,  = o).

## Slide 46: Phase Velocity in Waveguide
Since phase velocity vp depends on the propagation constant mn, it too depends on the integer pair (m,n), hence the property of the TE mode fields.
We observe that the phase velocity of the TE mode has the peculiar property of traveling faster than the speed of light!
(1.12)
Speed of light in dielectric of (,)

## Slide 47: Group Velocity in Waveguide
The velocity of energy propagation, or the speed that information travel in a waveguide is given by the Group Velocity vg.
Thus from:
Since vp> c,
The group velocity is less than the speed of light in vacuum, maintaining the assertion of the Relativity Theory that no mass/energy can travel faster than the speed of light.

## Slide 48: TM Mode Solution
The procedure for obtaining the EM field solution for TM propagation is similar to the TE procedure.
We start by solving the pattern function for the z-component of the electric field:
As in solving the TE mode problem, the Separation of Variables Method is used in solving (1.13), and the integer pair (m,n) needs to be introduced in the TM mode solution.
The mathematical expressions for the EM field components depend on the integer pair (m,n), and are denoted by the TMmn field.
The derivation details will be omitted here due to space constraints. You can refer to standard EM theory textbooks for further details.
and boundary conditions
(1.13)

## Slide 49: TM Mode Solution (cont’d)
The complete expressions for the TMmn field components are shown below:
(1.14a)
(1.14b)
(1.14c)
(1.14d)
(1.14e)

## Slide 50: TM Mode Solution (cont’d)
Where
(1.15a)
(1.15b)

## Slide 51: Cut-Off Frequency for TM Mode
Since the propagation constant mn is similar for both the TEmn and TMmn mode, a cut-off frequency also exists for TMmn :
Observe that from (1.14a) to (1.14e), the EM field components become 0 if either m or n is 0. Thus TM00 , TM10, and TM01 do not exist. The lowest order mode is TM11.
It is for this reason that we consider TE10 to be the dominant mode of the rectangular waveguide.
(1.16)

## Slide 52: Appendix 2: Plots of Electromagnetic Fields for Rectangular Waveguide

## Slide 53: TE10 Mode
E
H
TE10
Cross section visualization
of the EM fields
Instantaneous
E field magnitude
Instantaneous
H field magnitude

## Slide 54: TE01
E
H
TE10
Cross section visualization
of the EM fields
Instantaneous
E field magnitude
Instantaneous
H field magnitude

## Slide 55: TE11
E
H
TE11
Instantaneous
E field magnitude
Instantaneous
H field magnitude

## Slide 56: TM11
E
H
TM11
Instantaneous
E field magnitude
Instantaneous
H field magnitude

## Slide 57: References
[1] D.M. Pozar, “Microwave Engineering”, 2nd Edition, 1998 John-Wiley & Sons. (3rd Edition, 2005 is also available from John-Wiley & Sons).
[2] R.E. Collin, “Foundation for Microwave Engineering”, 2nd Edition, 1992, McGraw-Hill.
[3] C.A. Balanis, “Advanced Engineering Electromagnetics”, 1989, John-Wiley & Sons.