## Slide 1: ME1000 RF CIRCUIT DESIGN
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.
http://dreamcatcher.asia/cw

## Slide 2: 4. 3-Port and 4-Port Microwave Components
Notes: <number>

## Slide 3: 1.0 3-Port Microwave Components/Networks

## Slide 4: Example of 3-Port Components: Power Divider and Combiner
Power division and combining can be achieved with 3-port networks.
Divider
or
Coupler
P1
P2 =  P1
P3 = (1– )P1
Divider
or
Coupler
P1=P2 +P3
P2
P3
Power division
Power combining
 is known as the division ratio

## Slide 5: Another Example: 1-to-N Power Divider
This is an example of a 1-to-4 power divider.
1-to-2 Power
Divider
P1
1 P1
(1–1 )P1
1-to-2 Power
Divider
1-to-2 Power
Divider
21 P1
(1–2 ) 1P1
2 (1–1 ) P1
(1–2 ) (1–1 ) P1

## Slide 6: General Properties of 3-Port Networks
Like the 2-port network, n-port networks are described by their corresponding S-matrix. For a 3-port network, the S-matrix has nine elements.
If all ports are matched, then sii = 0, i = 1,2,3… (explain this).
It can be shown that the S-matrix of a 3-port network cannot be matched, lossless, and reciprocal at the same time. One of these characteristics has to be given up if the 3-port network is to be physically realizable, see Exercise 1.1 for the mathematical proof.

## Slide 7: 3-Port Networks
A lossless network results in a Unitary S-matrix.
When the S-matrix is non-reciprocal ( sij sji ), but the conditions of port match and lossless apply, the 3-port network is known as a Circulator.
A circulator usually has ferrite material at the junction to cause the non-reciprocity condition.
1
2
3
1
2
3
Note:
Here  =1
Check that both
matrices are not
symmetrical
(1.1)

## Slide 8: 3-Port Networks (cont’d)
A lossy 3-port network can be reciprocal and matched at all ports.
This type of network is useful as a power divider, in addition it can be made to have isolation between its output ports (for instance, s23 = s32 = 0).
A third type of the 3-port network, which is also used as a power divider is reciprocal, lossless, and matched at only two ports. It can be shown with its S-matrix given by:
(1.2a)
(1.2b)

## Slide 9: Example 1.1A: Usage of the Circulator
In a transceiver, to separate the
transmit and received signal
Using a circulator as an
isolator
Transmit Power
Receive Power

## Slide 10: Example 1.1B: Construction of a Stripline Circulator
Stripline
conductor
Ferrite disks
Ground
planes
B
D.C. magnetic field to bias
the ferrite disks (This can comes from permanent magnet
of electromagnet)
Example of commercial
coaxial circulator

## Slide 11: Exercise 1.1
Show that the S-matrix of a 3-port network cannot be matched, lossless, and reciprocal at the same time. Hint: Use proof by contradiction; assuming all three conditions are fulfilled in a 3x3 S-matrix, show that this will lead to a contradiction.
Solution…
Since the 3-port network is assumed to be matched and reciprocal, the matrix would be:
(E1.1)
Including the unitary condition (for the lossless 3-port network):
(E1.2)
The diagonal elements are zero, and this matrix is symmetrical

## Slide 12: Exercise 1.1 (cont’d)
Expanding (E1.2):
(E1.3)
(E1.4)
To fulfill (E1.4) for arbitrary S-parameters, two of s12, s13, and s23 must be 0.
Substituting this result into (E1.3), it is discovered that (E1.3) cannot be
fulfilled. This leads to a contradiction, which shows that our assumption
of a 3-port network with matched, reciprocal, and lossless conditions is wrong.

## Slide 13: T- Junction Power Divider
The T-junction power divider is a simple 3-port network that can be used for power division or power combining, and can be implemented on stripline, coaxial cable, and waveguide technologies.
We can make B negligible, or cancel it over
a band of narrow frequencies by compensation.
The output impedances Z1 and Z2 can then be selected to provide various
power division ratio . Quarter-wave transformers can be used to bring the
output line impedance back to the desired levels.
(1.3a)
(1.3b)
The T-junction power divider is lossless and reciprocal. The input is matched but the output is not matched. Verify it for yourself by deriving the S-matrix!!
No dissipative component within
No magnetic and nonlinear material
Equivalent electrical
circuit:
jB
Yin
Zc
Z1
Z2
V
Port 1
Port 2
Port 3

## Slide 14: Example 1.2: T-Junction Power Divider Design
A lossless T-junction power divider has a source impedance of Zc = 50 . The impedance is matched at the input. Find the output characteristic impedance so that the input power is divided in a 2:1 ratio. Compute the reflection coefficients at the output ports.
Implement this power divider using microstrip line on a printed circuit board.
Input power to a matched divider:
Input impedance to the matched divider:
Output power:
In general this is true for the
arbitrary power divider ratio, 

## Slide 15: Example 1.2 (cont’d)
At the Z1 = 150 Ω output Tline, we observe:
At the Z2 = 75 Ω output Tline, we observe:
Port 1
Port 2
Port 3
Zc= 50 
Z1=150 
Z2=75 
Implementation
on the microstrip
line
PCB dielectric
Conductor
GND plane
at the bottom
of the PCB
Top view

## Slide 16: Example 1.2 (cont’d)
Including quarter-wave transformers and step compensations for the Tline...
Port 1
Port 2
Port 3
50 
150 
75 
/4
50 
61.24 
86.60 
50 
150 
75 
Recommended length
of at least quarter wavelength
Quarter-wave transformer
The observant reader will notice that this realization is a narrow-band
power divider, by virtue of the wavelength it is only valid at the operating frequency.
Top view

## Slide 17: T-Junction Power Divider S-Matrix
Based on the previous analysis, we can show that the S-matrix for the input matched T-junction power divider is as given below (try to derive this as an exercise, using the fact that the voltage on each port consists of incident and reflected components and Kirchhoff’s Laws).
jB
Yin
Zc
Z1
Z2
V
Port 1
Port 2
Port 3
Hint:
When energize Port 1, no reflection,
when energize Port 2 and 3, reflection
occurs.

## Slide 18: Resistive Divider
The circuit below shows a resistive divider; Port 1 is the input and Port 2 and 3 are the outputs. Z1, Z2, and Z3 can be selected to give a certain power division ratio. The resistance can also be selected so that all the three ports are matched. The circuit below can be analyzed using the circuit theory.
Zin
Zc
Zc
Zc
V
V1
V2
V3
Port 1
Port 2
Port 3
Z1
Z2
Z3

## Slide 19: Example 1.3: Resistive Divider Design
Zin
Zc
Zc
Zc
V
V1
V2
V3
Port 1
Port 2
Port 3
Zc/3
Zc/3
Zc/3
P1
P2
P3
The impedance Z, at the Zc/3
resistor followed by the output line is:
The input impedance of the divider is:
Since the network is symmetrical for all
the three ports, all ports are matched and:
S11 = S22 = S33 = 0
Analyze the resistive divider below, show that it is an equal split (–3 dB) divider.

## Slide 20: Example 1.3 (cont’d)
Let the input voltage at Port 1 follow the voltage division rules:
The output voltages at Port 2 and
3 are given by:
If we divide all port voltages by (Zc)0.5, we see
that S21 = S12 = S23 = 1/2. The network is
reciprocal, so the S-matrix is symmetrical:
The input power and output power are:
This shows that half of the supplied power is dissipated in the resistors.

## Slide 21: Wilkinson Power Divider
The Wilkinson power divider is a lossy 3-port network having all ports matched with isolation between the output ports.
The Wilkinson power divider can be made to give arbitrary power division. The example shown here is the equal-split (3 dB) case.
Port 1
Port 3
Port 2
(1.4)
Only valid at operating
frequency

## Slide 22: Wilkinson Power Divider (cont’d)
Despite being a lossy 3-port network, the Wilkinson divider has the property of being lossless for the ‘forward’ wave; it is only dissipative for reflected power.
No power loss
Power loss

## Slide 23: Analysis of the Symmetry Wilkinson Divider
The equal-split Wilkinson divider is a symmetrical structure, thus it can be analyzed using the even and odd mode analysis.
Any signal imposed on a pair of terminals can be split into even and odd mode components.
For a symmetry circuit, it can be split into even and odd half circuits; the voltages at Port 1, Port 2, and Port 3 being analyzed for each modes and summed up.
The S-matrix can then be obtained for the system.
V1
V2
Extra

## Slide 24: Analysis of the Symmetry Wilkinson Divider (cont’d)
Port 1
Port 3
Port 2
V2
V3
Port 1
Port 3
Port 2
V2
V3
Port 1
Port 2
Port 1
Port 2
Even-mode half circuit
Odd-mode half circuit
Virtual GND
No current flows
across this link,
it can be disconnected.
Extra

## Slide 25: Analysis of the Symmetry Wilkinson Divider (cont’d)
Port 1
Port 3
Port 2
4Vo
+
-
+
Port 1
Port 3
Port 2
2Vo
+
-
2Vo
+
-
Even excitation
Port 1
Port 3
Port 2
2Vo
+
-
–2Vo
+
-
Odd excitation
As in the 2-port case, to find
the values of S-parameters,
we need to energize each
port individually. Assume
we energize Port 2 first.
Extra

## Slide 26: Analysis of the Symmetry Wilkinson Divider (cont’d)
Even circuit analysis:
From the quarter-wave transformer
formula:
Also
Extra
Port 1
Port 2
V1e
V2e
2Vo
+
-
1
Zine
Z=0
+z
V2e=Vo
2Vo
+
-

## Slide 27: Analysis of the Symmetry Wilkinson Divider (cont’d)
Odd circuit analysis:
Port 1
Port 2
2Vo
V1o
V2o
+
-
Zino
The quarter-wave transformer
changes the shorted end into
an open-circuit as seen from V2o. Thus:
Extra

## Slide 28: Analysis of the Symmetry Wilkinson Divider (cont’d)
Due to the short and open circuits at the line-of-symmetry (the bisection):
By symmetry, it is obvious that a similar relationship
exists for voltage on Port 3, thus:
Finally, combining the even and odd responses to give the voltage on Port 1 and 2:
Extra

## Slide 29: Analysis of the Symmetry Wilkinson Divider (cont’d)
Port 1
Port 3
Port 2
2Vo
Port 1
Port 3
Port 2
2Vo
Z1 = Zc
Now, consider the
excitation source
at Port 1.
From the second
equivalent circuit
as shown below,
it is obvious that
s11 = 0.
Extra
(QED).

## Slide 30: Microstrip Realization of the Wilkinson Power Divider
An equal power division divider:
Port 1
Port 2
Port 3
SMT resistor
2Zc
Top view
We would like to keep the separation
between conductors of Port 2 and
conductors of Port 3 as large as
possible. This is the best configuration as it reduces EM field coupling between the two paths.

## Slide 31: An Example of DIY Equal Division Wilkinson Power Divider
FR4 substrate
100, 1% tolerance surface mount
resistor
Microstrip line
Commercial power splitter

## Slide 32: Example 1.4
Design an equal-split Wilkinson power divider using a microstrip line, with d = 1.57 mm, r = 4.2, and operating frequency at 1.8 GHz. The system uses a microstrip line with a 50  characteristic impedance.

## Slide 33: Example 1.4: ADS Software Simulation of the Wilkinson Divider
For d=1.57 mm,
r = 4.2,
Zc = 50 ,
operating frequency
= 1.8 GHz
Microstrip
T-junction
model
To be more realistic, you can
model the discontinuity at this node.

## Slide 34: Example 1.4: ADS Software Simulation of the Wilkinson Divider (cont’d)
S21,  –3 dB at 1.8 GHz
(power is divided by 2)
S23, indicating the isolation between Port 2
and Port 3, should be
as small as possible.
S11, input port matching,
should be as small as
possible at 1.8 GHz.
Frequency range
of interest

## Slide 35: Unequal Power Division Wilkinson Divider
Port 1
Port 3
Port 2
(1.5)
Analysis of the unequal power division Wilkinson divider has to be carried out using the circuit theory as in the previous derivation. Here, only the design equations are given.

## Slide 36: Increasing the Bandwidth of the Wilkinson Power Divider
Adding the compensation quarter wavelength transmission line in Port 1:
Port 1
Port 3
Port 2

## Slide 37: Increasing the Bandwidth of the Wilkinson Power Divider (cont’d)
Using the multi-stage power divider. See Wilkinson, E. J., “An n-way hybrid power divider”, IEEE Transaction on Microwave Theory and Techniques, MTT-8, pp.116 – 118, January 1960.
Port 1
Port 2
Port 3
Top view

## Slide 38: 2.0 4-Port Networks

## Slide 39: General Properties of 4-Port Networks
A 4-port network S-matrix contains 16 elements in a 4x4 arrangement.
Unlike a 3-port network, a 4-port network can be lossless, reciprocal, and matched at all ports simultaneously, i.e., the S-matrix has the following form (the matrix is symmetrical and unitary):
One way for the above matrix to satisfy the unitary condition is:
(2.1)
We have more degree
of freedom, so the problem
is not over-constrained;
a unique solution can exist.

## Slide 40: General Properties of 4-Port Networks (cont’d)
It is customary to fix s12, s13, and s24 as:
Further application of the unitary condition yields:
Letting n = 0, there are two choices that are commonly used in practice.
 =  = /2:  = 0,  = :
These two matrices
has the character-
istics of a directional
coupler.
(2.2a)
(2.2b)

## Slide 41: Directional Coupler
Consider the matrix of (2.2a), when an incident power wave a1 is directed to Port 1 (assuming all ports to be matched):
From the theory of S-parameters, the power delivered to Port 1, Port 2, and Port 3 are:
From the lossless condition of the 4-port network:
4-port
1
2
4
3
a1
 a1
j a1
0
0

## Slide 42: Directional Coupler (cont’d)
We could repeat the previous exercise, with an incident power wave a2 in Port 2.
We conclude that for this particular matched 4-port network, when power is injected into a port, a portion of the power is transmitted to the opposite port while another portion is coupled to the port adjacent to the opposite port, while the adjacent port is isolated.
This conclusion can also be derived if we use the matrix of (2.2b), the only difference being the phase of the output voltage waves.
1
2
4
3

## Slide 43: Directional Coupler (cont’d)
A 4-port network described by the S-matrix of (2.2a) or (2.2b) is known as a directional coupler. The following three quantities are used to characterize the quality of a directional coupler.
1
2
4
3
Input
Through
Coupled
Isolated
(2.3)

## Slide 44: Some Typical Directional Couplers
Hybrid couplers are directional couplers with coupling C = 3 dB. This implies
A quadrature hybrid has a 90o phase shift between Port 2 and 3 when fed at Port 1. It is an example of a symmetrical coupler.
A magic T or rat-race hybrid has a 180o phase difference between Port 2 and 3 when fed at Port 1. It is an example of an anti-symmetrical coupler.

## Slide 45: Branch Directional Coupler or Quadrature Hybrid
Quadrature hybrids are 3 dB directional couplers with a 90o phase difference in the outputs of the through and coupled arms. It is usually implemented in the microstrip or stripline form.
(2.4)
Input (1)
Isolated (4)
Output (2)
Coupled (3)
Zc
Zc
Zc
Zc
Top view

## Slide 46: Branch Directional Coupler
The operation of the branch coupler can be analyzed using the even and odd mode analysis due to its symmetrical nature.
Input (1)
Isolated (4)
Output (2)
Coupled (3)
Must terminate
here with Zc
Line of symmetry
Top view

## Slide 47: 1800 Hybrid Directional Coupler
The 180o hybrid junction is a 4-port network with a 180o/0o phase shift between the two output ports.
A signal applied at Port 1 will be evenly split into two in-phase (0o) components at Port 2 and Port 3, and Port 4 will be isolated.
A signal applied at Port 4 will be evenly split into two components with a 180o phase difference at Port 2 and 3, and Port 1 will be isolated.
When operated as a combiner, input signals are applied at Port 2 and 3; the sum will be formed at Port 1 while the difference will be formed at Port 4.
180o Hybrid
1
4
3
2

## Slide 48: 180o Hybrid Implementation on the Microstrip PCB
An implementation of the 180o hybrid using the microstrip line is shown below; this is commonly known as a ring hybrid or rat-race. Again, the analysis can be carried out using the even and odd mode analysis.
(2.5)
Top view
Port 1
Port 3
Port 2
Port 4

## Slide 49: Coupled Line Directional Couplers
When two unshielded Tlines are close together, power can be coupled between the lines due to the interaction of EM fields of each line. For TEM or quasi-TEM mode Tlines, this can be represented in an equivalent circuit for:
L11 z
C11 z
L22 z
C22 z
C12 z
L12 z
C12 = Per unit length mutual capacitance
L12 = Per unit length mutual inductance
s
Line 1
Line 2
Top view

## Slide 50: Crosstalk
This phenomenon of the coupling of EM energy from one Tline to another is commonly known as crosstalk in a high-speed digital circuit design.
The amount of crosstalk is determined by L12 and C12.
For instance, when an electrical pulse is sent down Tline 1, electrical signal will appear at both ends of Tline 2 due to crosstalk.
The crosstalk signals are divided into near-end crosstalk (NEXT) and far-end crosstalk (FEXT).

## Slide 51: Crosstalk (cont’d)
Note:
Observe that there is a possibility for the far-end crosstalk to cancel off. By incorporating a proper design of the Tlines, this can be done, and Port 3 will become isolated. This is the principle of the coupled line directional coupler.
Port 1
Near-End
Crosstalk
NEXT
+
–
Current due to C12
Current due to L12
Far-End
Crosstalk
FEXT
Port 4
Port 2
Port 3

## Slide 52: Single-Stage Coupled Line DC Design
Similar to the quadrature hybrid and 180o hybrid directional coupler, the coupled line directional coupler can be analyzed using the odd and even mode circuit concept.
In this case, three impedances can be defined. (A) The characteristic impedance of each Tline, Zc. (B) The impedance when the odd mode signal is travelling along both lines, Zoo. (C) The impedance when the even mode signal is travelling along both lines, Zoe.
Zoo and Zoe for stripline and microstrip line configurations are widely tabulated.
V2
V1
Zc
Zc
Zc
Zc
Notes: <number>

## Slide 53: Single-Stage Coupled Line DC Design (cont’d)
(2.6a)
(2.6b)
(2.6c)
o is the wavelength at the intended
operating frequency
3 – Coupled
1 – Input
4 – Isolated
2 – Through
S
W
Top view

## Slide 54: Single-Stage Coupled Line DC Design (cont’d)
From the previous slide, we begin the design by specifying C. Then, use (2.6b) and (2.6c) to obtain the even and odd mode impedances. From the design tables or design equations for coupled microstrip or stripline, physical dimensions such as W, S, and d (dielectric) thickness can be obtained.
Note that this design only works best at fo, the intended operating frequency; it is narrowband. For a wideband directional coupler, we will need to cascade a few stages of the narrow-band directional coupler.
Finally, a good coupled line directional coupler is usually constructed using the stripline, as the microstrip line does not support pure TEM mode, and suffers from dispersion.

## Slide 55: Design Example
For instance, suppose we wish to design a lossless coupled line directional coupler with C = 0.1 or -20 dB, with Zo = 50 at 3GHz on FR4, with substrate thickness of 1.0mm
The synthesis of the
coupled microstrip
line can be performed
using LineCal tool from
Agilent ADS software
as shown on the left.
Thus:
Electrical length (l ), 90o for quarter
wavelength.
Zoe
Zoo
Zo
Voltage coupling
factor in dB
The required physical
dimensions

## Slide 56: Design Example (cont’d)
Alternatively we can implement our own design tool, as shown below implemented on Microsoft Excel.
Based on design equations from Garg R., Bahl I. J.,”Characteristics of coupled microstriplines”, IEEE
Transaction on Microwave Theory and Techniques, MTT-27, No.7, pp. 700-705,July 1979.

## Slide 57: Coupled Microstrip Line Example
An example of coupled microstrip lines which can be modified to become a coupled line directional coupler.
50 termination

## Slide 58: Lange Coupler
Able to achieve a coupling C of more than 3 dB, not easily achieved with the coupled line directional coupler. Recall that the quadrature hybrid and 180o hybrid have a coupling C of 3 dB only.
Higher bandwidth than the coupled line directional coupler.
90o phase difference between Port 2 and 3.
Input (1)
Isolated (4)
Through (2)
Coupled (3)
Zc
Zc
Zc
Zc
/4
The GND plane
is assumed at
the bottom of
the PCB
Top view

## Slide 59: Another Form of the Lange Coupler: The Unfolded Form
Input (1)
Isolated (4)
Through (2)
Coupled (3)
Zc
Zc
Zc
Zc
/4
Top view

## Slide 60: Examples of the Directional Coupler
Thin-film multi-layered ceramic
3 dB directional couplers from AVX Corporation (2007) (www.avx.com).
Commercial directional
coupler with coaxial terminals
880 to
2300 MHz

## Slide 61: Examples of the Directional Coupler (cont’d)
Example of the coil-ferrite type
directional coupler from
Mini-Circuits Corporation
(Source: www.minicircuits.com)
10 – 1500 MHz
Example of the lumped LC
directional coupler (narrowband).
Notes: For calculations of Ls, Cp1, and Cp2, refer to C. W. Sayre, “Complete Wireless Design”, 2001, McGraw Hill.
<number>

## Slide 62: Items for Self-Study
Single-ended-to-differential converter, or Balanced-Unbalanced Converter (Balun)
RF transformer
Waveguide Magic-T (180o hybrid coupler)
Tapered line 180o hybrid coupler
Waveguide Bethe hole coupler
Multi-section coupled line directional coupler

## Slide 63: Miscellaneous: Microwave Switches
Can be constructed using circulators, with the permanent magnet replaced by an electromagnet
Mechanical-type relay
Semiconductor-type switch, using PIN diodes, GaAs field-effect transistor etc.

## Slide 64: Miscellaneous: Examples of the RF/Microwave Integrated Circuit and PCB Assemblies
Quarter-wave Tline (microstrip) as RF choke
Hybrid impedance matching network
RF transformer implemented on PCB
Co-planar Tline
Narrow-band LC
balun (balanced-unbalanced
converter)