## Slide 1: ME1000 RF CIRCUIT DESIGN
<number>
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 11. Broadband Amplifiers
Notes: <number>

## Slide 3: Introduction
Up to now we have been looking at the amplifier design at one frequency or over a narrow band of frequencies centered at fc (the carrier frequency). Narrow band in this context implies a 5% of fc or smaller.
Here we will review broadband amplifier design
Some issues related to the broadband amplifier design:
  The S-parameters of a transistor are dependent on the frequency. Typically S21 decreases at a rate of 20 dB/decade as the frequency increases and S12 increases at the same rate with the frequency.
  S11 and S22 are also frequency dependent; this affect the input and output matchings
  There is a degradation of the noise figure and VSWR in some frequency range of the amplifier
Notes: <number>

## Slide 4: Typical Methods of Achieving the Broadband Operation
Basically, the design of a constant gain amplifier over a broad frequency range is a matter of properly designing the matching networks or feedback networks to compensate for the variation of the S-parameters with the frequency
Below are some methods of achieving the broadband operations:
  Use of the compensated impedance matching networks
  Use of the negative feedback
  Balanced design — combining either (1) or (2) with the balanced design approach
  Distributed amplifier (not covered in this lecture)
Notes: <number>

## Slide 5: 1.0 Compensated Impedance Matching
Notes: <number>

## Slide 6: Compensated Impedance Matching
A strategy of designing a wideband amplifier using the compensated impedance matching approach is to examine the expression for the transducer power gain
If we enforce s = 0 (i.e., make Zs = Zo), then
A wideband impedance transformation network can then be designed to transform the load impedance ZL so that L fulfills (1.2) within the operating frequency band
(1.1)
(1.2)
Notes: <number>

## Slide 7: Compensated Impedance Matching (cont’d)
For a fixed GT, the values of L which fulfills (1.2) is a circle on the Smith chart. First we write (1.2) as:
This can be expanded to:
(1.3b)
(1.3c)
(1.3a)
Notes: <number>

## Slide 8: Compensated Impedance Matching (cont’d)
A few constant GTL circles will be plotted on the Smith chart for L at different frequencies
From these circles, suitable values of ZL’ will be identified at each frequency and a wideband impedance transformation network is designed to transform the actual load impedance ZL to ZL’ at the designated frequency
Usually, the computer optimization method is needed for this procedure
An example will serve to illustrate this concept
Notes: <number>

## Slide 9: Example 1: Wideband Amplifier Design with the ADS Software Using the Compensated Impedance Matching Method
In this exercise, an attempt is made to design a wideband amplifier using the compensated impedance transformation technique. The active device used is the Phillips BFR92A bipolar junction transistor.
The intention is to design an amplifier with a transducer gain GT = 30 (14.77 dB) under the condition shown, with a bandwidth of 350 MHz to 450 MHz
Zs = 50
ZL = 50
Notes: <number>

## Slide 10: Example 1 (cont’d)
As a start, the following CE amplifier is constructed. The DC and S-parameter analysis are performed.
IC = 4.57 mA
VC = 3.0 V
Notes: <number>

## Slide 11: Example 1 (cont’d)
From the magnitude of S21, it is evident that this circuit can provide GT in excess of 30 when s = L = 0 (ZL = Zs = Zo = 50)
Zs = 50
ZL = 50
Notes: <number>

## Slide 12: Example 1 (cont’d)
A plot of GT versus frequency is shown below. Note that the transducer power gain varies greatly from around 65 to 45 over the intended operating frequency range.
Required frequency
range
Required GT
Notes: <number>

## Slide 13: Example 1 (cont’d)
Equations (1.3b) and (1.3c) are used to find the center and radius corresponding to the constant GT circle (GT = 30). The macros below are used in the ADS data display for this purpose.
Circle for 350 MHz
Circle for 400 MHz
Circle for 450 MHz
Notes: <number>

## Slide 14: Example 1 (cont’d)
Three constant GTL circles are plotted, for f = 350 MHz, 400 MHz, and 450 MHz. Three convenient points, as shown, are chosen for the required L.
ZL(350 MHz) = 16.45 + j0
ZL2(400 MHz) = 20.55 + j0
ZL3(450 MHz) = 25.85 + j0
L(350 MHz) = –0.505 + j0
L(400 MHz) = –0.481 + j0
L(450 MHz) = –0.319 + j0
Notes: <number>

## Slide 15: Example 1 (cont’d)
A Pi network is then proposed as the impedance transformation network that would give the required ZL at f = 350 MHz, 400 MHz, and 450 MHz
NOTE: A Pi network is proposed as we have three variables in the Pi network (C1, C2, and L1) and three degrees of freedom. This bodes well with the three constraints as determined by the real values of ZL at 350 MHz, 400 MHz, and 450MHz.
Optimization is carried out to find the best values for C1, C2, and L1 that will do the job. The optimization control with the associated goal functions are shown in the next slide.
Notes: <number>

## Slide 16: Example 1 (cont’d)
Notes: <number>

## Slide 17: Example 1 (cont’d)
The transformed load impedance using the Pi network
The optimized
results, after 12
iterations
Compare
these with
the requirements
Notes: <number>

## Slide 18: Example 1 (cont’d)
Finally, the Pi network is incorporated into the original circuit, and an S-parameter analysis is performed to verified the performance of the complete circuit
Notes: <number>

## Slide 19: Example 1 (cont’d)
Roulette stability factor
30
Operating region
GT
Zs = 50
ZL = 50
Notes: <number>

## Slide 20: Drawbacks of This Approach
Usually limited to a bandwidth of one decade
Considerable ripple is present within the operating bandwidth
The design of the required impedance transformation network is more of an art, largely a hit or miss affair
Power gain is not optimized, as seen in this example; there is a large amount of mismatch at the input and output. Power gain is sacrificed at the expense of the wideband operation.
Notes: <number>

## Slide 21: 2.0 Negative Feedback
Notes: <number>

## Slide 22: Negative Feedback
Negative feedback is widely used in an amplifier design for the following reasons:
  To stabilize the gain of the amplifier against the parameter changes in the active device due to voltage variation, temperature drift, or device aging
  To increase the bandwidth of the amplifier (at the expense of the maximum gain)
  To improve the gain linearity of an amplifier
  To change the input and output impedances of the amplifier
Notes: <number>

## Slide 23: Negative Feedback Review
+
–
E(s)
So(s)
Si(s)
A(s)
F(s)
Closed-loop gain
Loop gain
Stabilization of the gain against the parameter variation
Properties of G(s):
(2.1)
(2.2)
Extra
Notes: <number>

## Slide 24: Negative Feedback Review (cont’d)
Four basic configurations of the feedback system:
  Shunt-shunt feedback
  Shunt-series feedback
  Series-shunt feedback
  Series-series feedback
Log f
A(f) (Open loop)
Larger bandwidth
Improvement of bandwidth
Extra
Notes: <number>

## Slide 25: Implementing the Local Negative Feedback on Transistor and FET
RF2
RF1
RF2
RF1
Shunt feedback
Series feedback
The shunt and series feedbacks can be implemented
separately or together
We sample the output voltage and feedback in the form of modifying the input current
We sample the output current and feedback in the form of modifying the input voltage
Notes: <number>

## Slide 26: More on the Local Feedbacks on the Transistor and FET
RF2
Zin
Vs
Rs
RF1
IC
IE
IB
VB
VB
Only shunt feedback:
Only series feedback:
Output
voltage is
shifted by
180°
Note that
+
–
vb
RF1
ic
Notes: <number>

## Slide 27: Using the Y and Z-Parameters with Feedback
YA
YB
I1
I2
I1A
I2A
I2B
I1B
V1
V2
ZA
ZB
V1A
V1B
V2A
V2B
I1
I2
I1
I2
(2.3a)
(2.3b)
Extra
Series Feedback
Shunt Feedback
Notes: <number>

## Slide 28: Using the Y and Z-Parameters with Feedback (cont’d)
RF2
RF1
RF1
RF2
(2.4c)
(2.4a)
(2.4b)
Z matrix for the BJT
Extra
Using the Y to S matrix transformation
Notes: <number>

## Slide 29: Simplified Low-Frequency Feedback Analysis
Consider a low frequency FET model with feedback:
RF2
RF1
gmvgs
G
D
S
The Yt matrix can be easily derived:
And converted to the S-parameter:
This is also applicable to the BJT provided:
(2.5)
(2.6)
(2.7)
Extra
Notes: Refer to Chapter 4 of Gonzalez for more detailed derivations: G. Gonzalez, “Microwave Transistor Amplifiers: Analysis and Design”, 2nd Edition 1997, Prentice-Hall.
<number>

## Slide 30: Simplified Low-Frequency Feedback Analysis (cont’d)
If we require that:
Then
In the case when only the shunt feedback is applied (RF1 = 0):
(2.8)
(2.10a)
(2.10b)
(2.9a)
(2.9b)
(2.9c)
Observe that the S-parameters is no longer
dependent on the active device parameter
For the BJT additional requirement:
Extra
Notes: <number>

## Slide 31: Typical Local Negative Feedbacks on Transistor and FET at RF
RF2
RF1
LF2
At high frequency, the phase difference between the voltages at the collector and base will be less than 180°. Instead of a negative feedback, this could lead to a positive feedback, resulting in instability. LF2 is used to introduce a 90° phase lead when the phase difference between C and B is less than 90°.
The phase difference information can be obtained from S21
Notes: <number>

## Slide 32: Design Equations for the Negative Feedback Amplifier
In general, to implement a local feedback on a BJT or FET, we begin with the low frequency design
Equations (2.8) and (2.9b) are used to find the approximate values for RF1 and RF2:
In the low frequency model, S21 is negative (e.g., 180° phase shift), hence (2.9b) can be written as:
Since at high frequency the parasitic capacitance and inductance effects become evident, CAD software is then used to fine-tune the resistor values to obtain a good input/output VSWR (i.e., S11t and S22t close to 0) and a fairly constant S21t and S12t as a function of frequency
(2.12)
(2.11)
Notes: <number>

## Slide 33: Example 2: Negative Feedback Amplifier Design Example with the ADS Software
In this exercise, an attempt is made to design a wideband amplifier using the negative feedback technique. The active device used is the BFR92A bipolar junction transistor.
The objectives:
  To stabilize the |S21t| to around 3.2 between 100 MHz to 1000 MHz
  S11t and S22t close to zero within the same frequency range
Notes: <number>

## Slide 34: Example 2 (cont’d)
The basic circuit, with a DC biasing network, will gives
IC = 4.57 mA, VC = 3.0 V
Notes: <number>

## Slide 35: Example 2 (cont’d)
The S-parameters for the basic circuit:
Note that the small K stability factor indicates that the basic amplifier is less stable at the low frequency range
S21 has a magnitude > 3.2 from 100 MHz to 1000 MHz. Also note that the phase is less than 90° beginning from 700 MHz. So we choose S21(feedback) = 3.2
Notes: <number>

## Slide 36: Example 2 (cont’d)
Finding the low frequency approximation values for RF1, RF2, and the approximation for LF2:
Notes: <number>

## Slide 37: Example 2 (cont’d)
Feedback network is added. Tuning is carried to optimize the S-parameters of the resulting amplifier.
The final values:
RF1 = 270 Ohm
RF2 = 2.2 Ohm
LF2 = 33.0 nH
A capacitor Cf1 is added in series to act as a DC block.
Noise analysis
is enabled
Capacitor CE1 for a high frequency bypassing and CE2 for a low frequency bypassing (to maintain the stability for f < 200 MHz)
Notes: <number>

## Slide 38: Example 2 (cont’d)
The S-parameters for the amplifier with shunt and series feedbacks:
Magnitude of S21t did not
change much
Also note that because of the feedback, the amplifier becomes
unconditionally stable throughout
the operating range
Good matching to Zo = 50
for input
Notes: <number>

## Slide 39: Example 2 (cont’d)
Plotting the transducer gain GT with Zs = ZL= Zo. Also plotted is the noise figure at the output.
RF1 and RF2 degrade the noise
performance slightly
Noise figure without feedback
NFmin
Nf(2)
GT without feedback
GT with feedback
Notes: <number>

## Slide 40: 3.0 Balance Amplifier
Notes: <number>

## Slide 41: Balanced Amplifier
The first 90° 3 dB coupler divides the input signal into two equal amplitude components with a 90° phase difference
The second 90° 3 dB coupler recombines the amplifier outputs
Because of the phasing properties of the coupler, reflections from the amplifier inputs cancel at the input to the coupler, resulting in an improved impedance match
A similar condition occurs at the output
RF out
Zo
3 dB 90° Hybrid
3 dB 90° Hybrid
Zo
RF in
V1+
V1–
V2–
VB1
VB2
VA1
VA2
–90°
0°
Notes: <number>

## Slide 42: Derivation of the S-parameters for a Balanced Amplifier
Assume the 3 dB hybrid couplers are ideal and impedance looking into each port is equal to Zo. Then:
In a similar manner:
(3.1a)
(3.1b)
Extra
Notes: <number>

## Slide 43: Derivation of the S-parameters for a Balanced Amplifier (cont’d)
If both the amplifiers are equal:
And
Finally, using a similar approach, it can also be shown that:
(3.2)
Extra
Notes: <number>

## Slide 44: Advantages of a Balanced Amplifier
A balanced amplifier has the following interesting advantages:
  The individual amplifier stages can be optimized for the gain flatness or noise figure, without concern for the input and output matchings
  Reflections are absorbed in the coupler terminations, improving the input/output matching as well as the stability of the individual amplifiers
  Bandwidth greater that a decade or more can be achieved; primarily limited by the bandwidth of the coupler
  The essence of a wideband balanced amplifier — each amplifier must be a wideband
Notes: <number>

## Slide 45: References
[1]* G. Gonzalez, “Microwave Transistor Amplifiers: Analysis and Design”, 2nd Edition 1997, Prentice-Hall.
[2] D. M. Pozar, “Microwave Engineering”, 2nd Edition, 1998 John-Wiley & Sons.
[3] G. D. Vendelin, A. M. Pavio, U. L. Rohde, “Microwave Circuit Design Using Linear and Nonlinear Techniques”, 1990, John-Wiley & Sons (2nd edition 2005 is available).
Notes: <number>