## Slide 1: ME1000 RF CIRCUIT DESIGN
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 6. Passive and Active RF Lumped Components
Notes: <number>

## Slide 3: Agenda
Passive lumped components at RF
Surface-mounted devices
Active lumped components characteristics at RF
Biasing circuit design for bipolar junction transistors
Frequency response for basic amplifier circuits

## Slide 4: 1.0 Lumped Components at Radio Frequency

## Slide 5: Passive Lumped Components at RF
At radio frequencies, a component is not what it appears to be.
For instance a resistor:
R
Ideally:
A more accurate representation would be:
Note: Make sure you
understand the meaning
of ‘lumped’, and its opposite,
the ‘distributed’

## Slide 6: Effect of Packaging
How the component is packaged is very important at high frequencies.
To reduce unwanted lead inductance and capacitance, a smaller package size with shorter leads is preferred. This results in the birth of surface-mount technologies (SMT). SMT also enables the miniaturization of physical circuits.
Clead
Llead
Magnetic flux linkage
Electric field
linkage
A Resistor

## Slide 7: Passive Lumped Components at RF
The magnitude and phase of the resistor’s impedance as a function of frequency:
Only in this range will the component
behave as an ideal resistor — usually medium
to low frequency (< 250 MHz) for leaded components
Self-resonance
Self-resonance
frequency, fres

## Slide 8: Passive Lumped Components at RF (cont’d)
For a capacitor:
Self-resonance
Capacitive response

Lead inductance and resistance

## Slide 9: Passive Lumped Components at RF (cont’d)
An approximate model for a practical inductor:
R
C1
C2
L
C3
Parasitic
capacitance
to the ground
plane
Parasitic
capacitance
to the ground plane
Capacitance between the windings of the inductor
Skin effect loss
on the winding
Nominal inductance

## Slide 10: Surface-Mounted Package
Surface-mount technology (SMT) was developed in the 1960s and became widely used in the late 1980s. Much of the pioneering work in this technology was done at IBM.
Instead of leads, components were mechanically redesigned to have small metal tabs or end caps to be directly soldered to the surface of the PCB.
Components became much smaller. The elimination of leads also reduces parasitic inductance and capacitance within the component, allowing operation at higher frequencies.
PCB
Copper pad
Surface-mounted package
Metal
tab
Soldering

## Slide 11: Who Determines the Package Dimension?
A package dimension and style is usually determined by the needs of the electronic industry.
Usually a dominant component manufacturing company will introduce a new package type based on current needs.
If sufficient players adopt the package, it will become an accepted standard and a formal document is drafted to describe its characteristics.
At present in North America, the standards for SMT and other components are drafted by the JEDEC Solid State Technology Association (JEDEC – Joint Electron Device Engineering Council ), http://www.jedec.org/.
JEDEC also works closely with Electronic Industries Association of Japan (EIAJ) to focus on similar package outlines from each organization into one worldwide standard package outline.

## Slide 12: Active Lumped Component: Bipolar Junction Transistor
TO-92 packages
SOT-23 package
SOT-143
E
B
C
2N3094
Medium Freq.
200 MHz
BFG520
EHF
9 GHz
BFR92A
UHF
5 GHz
BF199
UHF
500 MHz
E
C
B
C
B
E
E-Line package
ZTX313
Medium Freq.
300 MHz
B
E
C
E
E
B
C
SMT components usually come in a strip

## Slide 13: Passive Lumped Components for Ultra High Frequencies (UHF) (>300 MHz) Application
Other standard sizes are:
0402, smaller than 0603
0201, even smaller than 0402
210, bigger than 0805.
Multilayer electrolytic
capacitor (1206)
aluminum oxide
0805
80 mils
50 mils
Thin film inductor
(0603)
Coil inductor
(0805)
Thick film resistor
Multilayer ceramic capacitor
(0603), NPO dielectric
(0805)
(1206)
(1206),
Y5V dielectric
(0603),
NPO dielectric

## Slide 14: More Examples
Inductors
Thick film Resistors
Various types of capacitors
Transistors and
MMIC (monolithic
microwave integrated circuit)
0402
0603
0805
1206
1210
SOT-23
SOT-143
Variable
capacitor
86 plastic
package
Various types of diodes
MINIMELF
SOD-110
SOD-323
Rectifying
diode
Zener diode
RF varactor
RF amplifier
Metal Electrode Faced

## Slide 15: More Examples (cont’d)
24 Leads QFN
Various packaging for piezoelectric
crystal and related components
Various SOIC and QFP packages
32 leads
PLCC
60 leads
TQFP
44 leads
TQFP
Non-standard
package
HC49/U
HC49/4H
surface accoustic wave
(SAW) resonator
Crystal resonator
Crystal resonator
QCC8C

## Slide 16: Passive Lumped Components for Medium Frequency (up to 300 MHz)
Coil inductor
with Ferrite core
Multilayer
ceramic capacitor
Coil inductor
with air core
Carbon/metal
film resistor

## Slide 17: Passive Lumped Components for Incorporation into PCB and Other Substrates
Deposited carbon film, or semiconductor
Low resistance
High resistance
Resistors
Interdigital Capacitor
Series Single-Loop
Spiral Inductor
Series Multi-Loop Spiral Inductor
Air Bridge
Shunt Multi-Loop Spiral Inductor
Via
Microstrip Line
Metal-Insulator-Metal (MIM)
Capacitor
High r dielectric

## Slide 18: RF Bipolar Junction Transistor (BJT)
A discrete BJT housed in SOT-23 plastic package.
Simplified cross section view of a BJT.
N (Collector)
N (Emitter)
P (Base)
E
C
B
Bond-wire

## Slide 19: RF Bipolar Junction Transistor (BJT) (cont’d)
E
B
Interdigital E and B
contacts
Silicon
Oxide-Nitrite
Insulator
Cross section view of an
NPN RF Transistor
C
P
N
B
B
B
E
E
N++
N++
Very thin base region to improve transistor  at high frequencies

## Slide 20: RF BJT Construction
Almost all RF transistors are NPN, because the mobility of electrons is higher than holes in Silicon (e = 0.13 m2V–1s–1, h = 0.05 m2V–1s–1). The mobility is inversely proportional to the base transit time, .
The Base thickness is very thin to improve current gain hfe at high frequencies. The hfe is related to a parameter known as the base transit time ; a smaller  yields a larger hfe.
Interdigital Base and Emitter contacts are employed to reduce the base spreading resistance rb’b and to reduce the noise generated by the transistor.
The base transit time  can be reduced further if electrons are accelerated across the base by an E-field. This is achieved by a deliberately introduced doping profile in the base.
Commercial RF transistors in a discrete form can have fT up to 10 GHz. Examples of RF BJTs are the BFR92A (fT = 5 GHz) and the BFG520 (fT = 9 GHz), from Philips Semiconductor (www.nxp.com) and Infineon Technologies.

## Slide 21: RF BJT Construction (cont’d)
N (Collector)
N (Emitter)
P (Base)
E
C
B
x
Dopant
concentration
Donor
Acceptor
E
B
C
E-field
Electrostatic force on electrons
A doping profile in Base for an
NPN transistor:
Doping profile
No doping profile

## Slide 22: BJT Operating Regions
Various operating region of a bipolar junction transistor (BJT).
IC
VCE
B
C
E
IB
IE
Only VCE and IC
are needed to know
the state of the BJT
ACTIVE:
BE forward-biased
BC reverse-biased
INVERSE:
BE reverse-biased
BC forward-biased
SATURATION:
BE, BC junction forward-biased
Extra
CUT-OFF:
BE, BC junction reverse-biased
IC
VCE
0
IB1
IB2
IB3
IB4
IB5
B
C
E
BC junction
BE junction
NPN
Transistor

## Slide 23: Small-Signal Model of Transistor at High Frequency: the Hybrid-Pi Model
N (Collector)
N (Emitter)
P (Base)
E
C
B
The Hybrid-Pi Model:
Fixing the d.c. IC, IB, and VCE, the response of the transistor for
small variations of IC+ic , IB+ib , and VCE+vce is given by the
small-signal model. How to fix the DC current and voltage,
known as biasing the transistor, will be discussed shortly.
IC
VCE
0
IB1
IB2
IB3
IB4
IB5
DC load line
Extra

## Slide 24: The Parameters of Hybrid-Pi Model (1)
The Hybrid-Pi model is a fairly accurate description of the BJT small-signal response up to GHz frequency range. You can find more information on the Hybrid-Pi model
in [4].
The names of the various parameters:
rbb’ - Base spreading resistance (also given as rx)
gm – Transconductance (it relates voltage to current)
Ce - Emitter capacitance
Cc - Collector capacitance
rb’c - Collector to base resistance (also given as r)
rb’e - Base to emitter resistance (also given as r)
rce - Output resistance (also given as ro)
Extra

## Slide 25: The Parameters of the Hybrid-Pi Model (cont’d)
Extra
Notes: <number>

## Slide 26: The Parameters of the Hybrid-Pi Model (cont’d)
Extra

## Slide 27: Validity of the Hybrid-Pi Model
Approximate relationship between IC and VBE:
(BJT under the active region)
Upon using Taylor’s expansion:
Say
Let :
These higher-order
terms (HOT)
are ignored
Then :
Extra

## Slide 28: Conditions When the Hybrid-Pi Model Can Be Applied
1. Only valid for small-signal operation; not valid for power amplifiers.
2. Extra conditions:
    hfe close to hFE (small-signal current gain similar to large-signal current gain).
Example
Assuming VBE << VT implies VBE < 0.1VT.
VBE must be smaller than 2.6 mV
for the hybrid-pi model to be accurate.
Extra

## Slide 29: Useful BJT Parameter: The Transition Frequency (fT)
The transition frequency, fT is the frequency where the small-signal current gain io/is of the circuit approaches unity.
It is related to the small-signal capacitance Ce and Cc by:
Beyond fT, a transistor is useless as an amplifier (for both current and voltage amplification). Hence fT fixes the upper usable frequency of a BJT device.
fT is a function of DC condition, fT(IC, VCE); can you explain why?
Note that a similar
definition to fT can
also be applied to FET.
iS
io
This is the AC
equivalent
circuit!
0
Log10 fT
Log10 f

## Slide 30: PN Junction Capacitance and the Base Transit Time
The PN junction capacitance can be written as CX = CDX+ CTX for BC and BE junction, x = C or E.
CDX is the diffusion capacitance while CTX is the depletion region capacitance (also called the space charge capacitance).
CDX is negligible when the PN junction is reverse biased and is the dominant capacitance when the PN junction is forward biased.
Thus for a BJT operating in the Active Region, CE  CDE and CC  CTC.
Where CDE = F gm and CTC is given by:
F is the base transit time (the average lifetime of minority charge carrier in base – for NPN transistor, this is the average lifetime of electrons in the base before being ‘sucked’ into the collector region).
Cjx is the depletion region capacitance when VBX=0 and m and Vjx are parameters usually determined empirically from measurement. A smaller F will yield a larger fT.
Extra

## Slide 31: More on PN Junction Capacitance
The diffusion capacitance is given by:
Ihpn is the current component due to the injection of holes from P to N region, while Ienp is the component from the injection of electrons from N to P region. Together they constitute the forward biased current IF .
Similarly under reverse biased, the diffusion capacitance is given by:
Since Iepn and Ihnp are extremely small, CD is also very small (<10–13 is typical).
P
N
Ihpn
Ienp
IF
PN junction is
forward biased
+
–
P
N
Iepn
Ihnp
IR
PN junction is
reverse biased
–
+
Extra

## Slide 32: More on PN Junction Capacitance (cont’d)
For a typical NPN transistor, the N-type region of the Emitter is highly doped and P-type region of the Base is lightly doped.
Thus under forward biased (BE junction forward biased), Ihpn << Ienp, IE  Iepn. And CDE can be approximated as:
Recognizing that F = e,
A plot of CT versus junction voltage is shown below. Again, the charge-control description of a PN junction is used to derive the capacitance.
CT
Vjunction
Region where the expression breaks
down.
0
Cj
Extra

## Slide 33: RF Transistor Selection
Example of how the parameters of RF devices are tabulated in an electronic components catalog.
[Adapted from the catalog
of Farnell Components.]
fT
Power dissipation
VCE (max)
hFE (min)
Pm(max)
www.farnell.com

## Slide 34: RF Transistor Selection (cont’d)
[Image adapted from
RS Components Malaysia
www.rsmalaysia.com]

## Slide 35: Other Active Devices: MOSFET and MESFET
N-channel
Metal-Oxide
Semiconductor
Field Effect Transistor
(MOSFET)
N-channel
Metal-Semiconductor
Field Effect Transistor
(MESFET)
The substrate (usually
made of composite semi-
conductor such as
Gallium Arsenide)
Oxide layer
S
D
G
n+
n+
p
n
Oxide Layer
The substrate
(usually made
of element
semiconductor
such as Silicon)
Extra
PN junction contact
Semi-insulating layer (usually undoped semiconductor)
S
D
G
p
Metal-Semiconductor rectifying contact
Ohmic Metal-Semiconductor
contact

## Slide 36: MOSFET and MESFET (cont’d)
For operating frequency > 2 GHz, FETs are usually used in place of BJTs in microwave circuits. Typically MESFET is used in both discrete and integrated circuit form, while MOSFET is only used in integrated circuits.
Among BJT, MOSFET, and MESFET; MESFET has the highest transition frequency fT and is often used for high-performance RF/microwave circuits:
  FET has better noise characteristics (lower noise figure).
  FET such as MESFET can be constructed from compound semiconductor such as Gallium Arsenide (GaAs) (the so-called III-V compound) which has a higher electron mobility than Silicon.
  Smaller Gate capacitance in the MESFET structure. The Schottky barrier (Metal-Semiconductor contact) on the Gate of MESFET has a smaller capacitance compared to the gate oxide capacitance of MOSFET, the PN junction in JFET, or the C of BJT.
  Also, the ohmic contact on the Drain and Source on the MESFET reduces the corresponding Drain and Source capacitance.
(2), (3), and (4) contributed to much higher fT in a MESFET.
Extra

## Slide 37: Small-Signal Model for FET
Extra
Cgs
G
Cgd
Gmvin
rd
Cds
D
S
Causes the reduction of voltage and current gain
at high frequencies
rG
rD
rS
rGS
vin

## Slide 38: End Notes on Active RF Components
Most modern high-performance RF/microwave circuits employ FETs; for instance, GaAs (Gallium Arsenide) MESFETs for an operating frequency > 3 GHz. GaAs MESFETs can operate in excess of 10 GHz.
Since the late 1990s, Hetero-junction Bipolar Transistor (HBT) has been introduced commercially. In HBT, different semiconductor material is used for the Base, Emitter, and Collector region. For instance, P-type GaAs for the Base, N-type GaAs for the Collector and N-type AlGaAs for the Emitter. Another example of HBT is the SiGe (Silicon-Germanium) on Silicon process — a compound of SiGe is used for the Base. An example of discrete SiGe HBT is the BFP620 from Infineon Technologies (www.infineon.com) with an fT of 65 GHz!
Extra
P
N
B
B
B
E
E
N++
N++
Si
SiGe
Si
C
An example of SiGe
HBT

## Slide 39: End Notes on Active RF Components (cont’d)
The hetero-junction structure results in a valence band discontinuity between the Base and Emitter of an NPN structure.
This discontinuity reduces the injection of holes from the Base to the Emitter, while allowing the injection of electrons from the Emitter to the Base. This effect improves emitter efficiency ().
The emitter efficiency is further improved by constructing a transistor with a heavily doped and very thin Base region, thus the base-spreading resistance (rb’b) and the base-transit time (F) are reduced.
A smaller F results in a smaller Ce.
Extra

## Slide 40: End Notes on Active RF Components (cont’d)
Hetero-junction approach is also applied to MESFET, in the channel region of the FET, called the Modulation-Doped Field Effect Transistor (MODFET).
However, since the FET operation does not depend on charge injection, but of charge transport in the channel between the Drain and Source terminals, the introduction of the hetero-junction structure in the channel serves to increase the electron mobility, allowing very rapid exchange of electrical signals between the Drain and the Source. This improves the fT of the FET.
The resulting FET is usually called a High Electron Mobility Transistor (HEMT). A higher electron mobility allows the device to respond to rapid changes in its Gate. Effectively this reduces Cgs.
Such transistors can operate well into the millimeter wave region or in excess of 100 GHz.
Extra

## Slide 41: End Notes on Active RF Components (cont’d)
An example of HEMT using GaAs as the substrate.
S
D
G
Metal
N
Undoped
AlGaAs spacer
 10 nm
Undoped GaAs
Semi-insulating GaAs layer
AlGaAs
Oxide
2D Electron
Gas (2 DEG)
layer
N+
N+
Usually in depletion mode.
But can be designed to work
in both depletion
and enhancement mode
Extra

## Slide 42: End Notes on Active RF Components (cont’d)
Since 2006, the CMOS technology, where the main active component is the MOSFET, is also used extensively for applications up to a few GHz. This is usually implemented in integrated circuit form.
For all these active devices, the small-signal equivalents are almost similar to the hybrid-pi model of the BJT, so in this course we only concentrate on RF circuit design using the BJT. The major difference is in the way we bias the active devices. FET active devices, which come in enhancement and depletion mode, will require different biasing circuits. Also, depletion mode devices sometimes require a negative DC supply.
Extra

## Slide 43: 2.0 Review of BJT Amplifier Biasing and S-Parameters Computation

## Slide 44: DC Biasing for BJT and FET
Biasing means putting proper DC voltages and currents at a transistor terminals (Collector, Base, Emitter) so that the device is in the required operating region when no AC signal is applied.
A bipolar junction transistor (BJT) has four operating regions: Active, Cut-off, Saturation and Inverse.
For small-signal amplifiers, we bias the transistors in the Active region. Small-signal amplifiers are usually of the Class-A type because they need to have linear response.
IC
VCE
0
IB1
IB2
IB3
IB4
IB5
We fix the DC current
and voltage, IC, IB, and
VCE of a BJT to the
Active Region (BC
junction RB, BE junction
FB)
Key point of BJT biasing
for small-signal
operation, NPN transistor:
VC>VB>VE (Active region)

## Slide 45: DC Biasing for BJT and FET (cont’d)
For large-signal amplifiers, we may bias the transistors in the Active and the Cut-off regions, depending on the Class of the amplifier.
Biasing also applies to the field effect transistor (FET), which has four distinct operating regions: Active (also called Saturation), Linear, Cut-off, and Inverse.
Small-signal FET amplifier is usually biased in the Active region.
Large-signal FET amplifier can be biased in the Active and Cut-off regions.
The key point of FET biasing
for small-signal operation, N-channel:
VD >VG > VS (Active region)
VDS > VGS – VTN
Threshold voltage

## Slide 46: BJT Amplifier Configuration
A transistor is a three-terminal device. Two of the terminals can be used for signal input and output. The third terminal can be grounded, usually AC grounded with respect to the other terminals.
This grounded terminal is called the common terminal, and hence the name for the transistor amplifier configuration.
Note that a similar situation exists for FET amplifiers; we call these common-source, common-drain, and common-gate FET amplifiers.
vin
vout
vin
vout
vin
vout
Common-Emitter (CE)
Common-Collector (CC)
Common-Base (CB)
Can you explain
why there are no other
permutations?

## Slide 47: Typical DC Biasing Circuits for BJT
Vcc
Rb1
Rb2
Rc
Re
Emitter bias (suitable for low frequencies up to the UHF band):
RF choke
Coupling capacitor
Bypass capacitor
Decoupling capacitor
Basic biasing network
Input
Output
Common
Emitter
configuration!
Cc1
Ce
Cd
Vcc
Rb1
Rb2
Rc
Re
Cc2
L1
L2
L3
After adding coupling,
bypass capacitors,
and RF chokes.
We usually
use the triangle
symbol to model the amplifier
circuit
This is the basic amplifier
circuit

## Slide 48: Typical DC Biasing Circuits for BJT (cont’d)
Bypass or decoupling capacitors are used to stabilize the DC voltage and current levels, and to isolate RF signals from other circuitry.
Sometimes these capacitors can be put right after the RF choke to improve their effectiveness.
Vcc
Rb1
Rb2
Rc
Re
Cc2
L1
L2
L3
Cd1
Cd2
Cc1
Cd3
Ce
Input
Output
To shunt out the RF power
that leaks from the RF choke

## Slide 49: Typical DC Biasing Circuits for BJT (cont’d)
Other forms of emitter bias:
Vcc
Rb1
Rb2
Re
Cc1
Cc2
Ce
L1
L2
L3
Cd
Cd
Common emitter
configuration
with no collector
resistor
Common collector
configuration
Vcc
Rb1
Rb2
Re
Cc1
Cc2
L1
L2
L4
This will allow a
higher maximum
voltage swing
at the Collector
terminal

## Slide 50: Typical DC Biasing Circuits for BJT (cont’d)
Voltage feedback bias (suitable for low frequencies up to the microwave band):
Rc
Vcc
Rb
Basic biasing network,
common emitter configuration.
After adding coupling,
bypass capacitors,
and RF chokes.
Cc1
Cc2
L1
L2
Cd3
Cd2
Vcc
Rb
Input
Output
Rc
Cd1

## Slide 51: Typical DC Biasing Circuits for BJT (cont’d)
Active bias (suitable for low frequencies to the microwave band):
Cc1
Cc2
L1
L2
Cd
Vcc
Rb1
Rb2
Rc
Input
Output
RF transistor
Low frequency
transistor

## Slide 52: Typical D.C. Biasing Circuits for BJT (cont’d)
Another form of active bias using current mirror, popular for high power application with large collector current IC. Usually IC >> Iref.
Cc1
Cc2
L1
L2
Cd
Vcc
Rc
Input
Output
Large
RF transistor
Low frequency
and small transistor
Iref
IC
Where:
AE1 = Emitter area
for transistor Q1
AE2 = Emitter area
for transistor Q2
Q2
Q1
Note that no resistor in the
high current path

## Slide 53: Some Issues Concerning DC Biasing
Biasing network must not interfere with the flow of RF energy during normal operation. Hence the quality of the bypass capacitors and RF chokes is vital.
Temperature stability. The bias point or quiescent point (i.e., IC, VCE) of the BJT must not change a lot with temperature variation, to ensure that the performance of the active circuit is not affected by temperature variations. In this sense, active bias is the most stable, followed by emitter bias and voltage feedback bias.
Compensation for temperature variations using a diode in emitter bias is available.
Stability against parameter variations of the BJT. Again, active bias and emitter bias are less susceptible.

## Slide 54: FET Amplifier Biasing
Due to time constraint we will not focus on field-effect transistor (FET).
However it needs to be mentioned that for the FET amplifier can also be classified into Common-Source (CS), Common-Gate (CG) and Common-Drain (CD).
The DC biasing circuit discussed can also be modified to FET amplifier. Again for RF/microwave circuits typically N-channel device is used.
Common-Source
(CS)
Common-Drain
(CD)
Common-Gate
(CG)
vin
vout
vin
vout
vin
vout

## Slide 55: Example 2.1: BJT Amplifier Biasing and Small-Signal Equivalent Circuit
Determine the quiescent point (Q) of the transistor and its DC stability. Given: hFE(min)=100, hFE(max)= 200.
Derive the approximate small signal equivalent circuit of the following amplifier schematic. Use the hybrid-pi model for the BJT. Given VA=74.03 V, Cjc=3.638 pF, Cje=4.493 pF, rb’b=10, hfe=300, Vjc=0.75, m=0.3085, F = 301.2 pS.
If the circuit is going to be used at 430 MHz, suggest suitable values for Cc1, Cc2, Ce and the required RF choke inductance.
Finally, suggest a suitable value for Cd.
Cd
Input
Vcc
10k
4.7k
470
220
Cc2
L1
L2
L3
Ce
Output

## Slide 56: Example 2.1 Solution
Vcc=5 V
10k
4.7k
470
220
VB
VE
VC
I1
IC
IB
IE
DC Analysis:
Assuming hFE is large, I1 >> IB.
Assuming transistor is in the active
region, VBE = 0.6V.
Using Ohm’s Law:
Assuming hFE is large, IC >> IB.
Using Kirchoff’s Voltage Law:
Verify that transistor is under the Active Region:
Thus, the BC junction is reverse biased. In previous slide, it has been
shown that the BE junction is forward biased. So the transistor is biased
in the Active Region. The circuit is destined for Class A operation.
VCE and IC constitute
the Q point

## Slide 57: Example 2.1 Solution (cont’d)
DC biasing stability analysis (Stability Factor):
Variation of Ic when Ico changes
Variation of Ic when VBE changes due to temperature changes
Variation of Ic due to device parameter variations

## Slide 58: Example 2.1 Solution (cont’d)
Deriving small-signal hybrid-pi model parameters:
Can be ignored, considered an open circuit

## Slide 59: Example 2.1 Solution (cont’d)
Since the BE junction is forward biased:
Since the BC junction is reverse biased:
Small-signal
equivalent
circuit:
53.734 pF
2.682 pF
0.1748 vb’e
16.288 k
1.682 k
10
B
B’
E
C

## Slide 60: Example 2.1 Solution (cont’d)
Finding values of the coupling capacitors, the bypass capacitor and the RF choke.
Thus we can use 390 nH (standard value) for L1, L2, and L3. Make sure that the self-resonance frequency and Q-factor of the chosen practical inductor is sufficient for this purpose.
Similarly, 390 pF is chosen for Cc1, Cc2, and Ce.
Typically, values of L1, L2, and L3 should be chosen so that the reactance of the inductors is greater than 1000 at the operating frequency. The values of Cc1, Cc2, and Ce are chosen so that the reactance of the capacitors is less than 1 at the operating frequency. Care must be taken to ensure that the actual component’s self-resonance frequency be at least 50% higher than the operating frequency.

## Slide 61: DC Biasing Design with Agilent’s AppCAD

## Slide 62: Characterizing the Frequency Response of the Basic Amplifier Circuit
We would like to find out how the circuit will behave if a sinusoidal voltage of a certain frequency is injected into its input.
It is reasonable to expect that the amplifier circuit to behave differently at different frequencies.
Of interest is the ratio of the various voltages and currents on the terminals of the basic amplifier circuit, i.e., the classical parameters.
RL = Zc
Zc
Zc
Rs = Zc
Vs
V1
V2
I1
I2
Optional
transmission line
Output
impedance
Zo
Voltage gain
Current gain
Power gain
Input Impedance

## Slide 63: Characterizing the Frequency Response of the Basic Amplifier Circuit (cont’d)
For an amplifier operating at RF and microwave frequencies, the more convenient parameters are the S-parameters.
The amplifier is considered as a 2-port network, and the S-parameters s11, s12, s21, and s22 can be measured or derived. Bear in mind that we assume the amplifier to be linear or small-signal.
The S-parameters can be reliably measured at RF and microwave frequencies using an instrument called a Vector Network Analyzer, or derived from linear circuit analysis.
Instead of dealing with absolute voltages and current phasors, the S-parameters deal with the ratio of incident and reflected waves. This is based on the fact that a high frequency amplifier can be connected to transmission lines/waveguides at both its terminals. Of course in the extreme case, the transmission line can be so short that it vanishes.
The next slide shows how the S-parameters are obtained. For more information please refer to the notes in RF Circuit Design – Passive Circuit.

## Slide 64: Measurement of S-Parameters for 2-port Networks
Measurement of s11 and s21:
Measurement of s22 and s12:
Zc
Zc
Zc
Zc
Vs
a1
b1
b2
Port 1
Port 2
b1
Zc
Zc
Zc
Zc
Vs
b2
a2

## Slide 65: Example 2.1: Computing S-Parameters from a Circuit Simulator
Setting up small-signal
S-parameters computation
in a commercial simulator
Extra

## Slide 66: Example 2.1 (cont’d)
Note that the S-parameters, like
voltage and current phasor,
are complex values.

## Slide 67: Example 2.2: Deriving Small-Signal S-Parameters for BJT Amplifier Analytically
Consider the circuit of Example 2.1 being terminated with a source and load impedance of Ro. Ignoring the package parasitic, the small-signal equivalent circuit is shown below.
Z4
gmV3
R1
Vs/Ro
Z3
R5
R2
V1
V3
V2
Load network
Ce
Cc
gmV3
rce
rb’e
rbb’
Ro
Ro
Rb
Vs
Source network
V1
V3
V2
Port 1
Port 2
Extra

## Slide 68: Example 2.2 Solution
Using Nodal Analysis:
Node 1:
Let
Node 3:
Node 2:
(1)
(2)
(3)
From (1):
(4)
From (2):
(5)
Extra

## Slide 69: Example 2.2 Solution (cont’d)
Putting (4) & (5) into (2):
Using (4):
Using (5):
(6)
(7)
(8)
Extra

## Slide 70: Example 2.2 Solution (cont’d)
(9)
(10)
Using the relationship between port voltage, current, and the normalized voltage waves in S-parameter theory (see Chapter 2):
From (9)
Extra

## Slide 71: Example 2.2 Solution (cont’d)
Hence:
By injecting the source at the output, we can obtain expression for s22 and s12. This is the procedure used by most CAD tools to obtain the S-parameters for linear circuits.
Extra

## Slide 72: Appendix 1: Some Do-It-Yourself (DIY) RF Circuits

## Slide 73: UHF Low-Noise Amplifier
Extra
Supply: 3.0–4.0 V
Bandwidth: 850–910 MHz
Transducer Power Gain (GT): 11–12 dB Noise Figure (F): < 1.45
Grounded co-planar
transmission line
Zener diode
voltage regulator
circuit
BFR92A

## Slide 74: L-Band (1.8 GHz) Fixed Frequency Oscillator
Extra
Spiral Inductor
(to set the
oscillation
frequency)
Output
(1–3 dBm
into 50 Ω)
3.3–4.5 V DC Power Supply
Schottky diode
(Baker’s clamp)
Philips Semiconductor BFG520

## Slide 75: 400 to 550 MHz UHF Frequency Synthesizer Prototype
This is a low-cost frequency synthesizer using a digital phase-locked loop (PLL) integrated circuit from National Semiconductor, the LMX2306. The voltage controlled oscillator (VCO) is designed using the techniques presented in this course.
Microcontroller and buffer
to generate the reference
clock and control signals
for the LMX2306.
Ouput
LMX2306
VCO
Loop filter
Extra
SMD
prototyping
board by
F. Kung

## Slide 76: TRM Calibration Structures for Grounded Co-Planar Waveguide and Antenna

## Slide 77: 810 to 910 MHz UHF Frequency Synthesizer
Crystal
reference
oscillator
Voltage controlled
oscillator
Optional voltage
doubler (for the
charge-pump)
Optional PIN diode
attenuator
Programmable
phase-locked loop IC
To the microcontroller-based
master unit

## Slide 78: MMIC Amplifier and SMT Prototyping of RF Circuits
MMIC amplifier
3M copper tape
2-stage wideband amplifier
RF amplifier

## Slide 79: References
[1] Ludwig R., Bretchko P., “RF Circuit Design – Theory and Applications”, 2000, Prentice Hall.
[2] Laverghetta T.S., "Practical Microwaves", 1996, Prentice-Hall.
[3] Robertson I. D., Lucyszyn S. (Editors), “RFIC and MMIC Design and Technology”, 2001, IEE Circuits, Devices and Systems Series 13.
[4] Gray P. R., Meyer R. G., “Analysis and Design of Analog Integrated Circuits”, 3rd Edition, 1993, John-Wiley & Sons. Note: 4th edition of this book, by Gray, Meyer, and Hurst P. J., Lewis S. H. “Analysis and Design of Analog Integrated Circuits, John-Wiley & Sons, 2001, are available with newer materials.
[5] Millman J., Halkias C. C.,”Integrated Electronics”, 1972, McGraw-Hill.
[6] Massobrio G., Antognetti P., “Semiconductor Device Modeling with SPICE” 2nd Edition 1993, McGraw-Hill.
[7] Sze S. M., “Semiconductor Devices – Physics and Technology”, 2nd Edition 2002, John-Wiley & Sons.
[8] Gilmore R., Besser L.,”Practical RF Circuit Design for Modern Wireless Systems”, Vol. 1 and 2, 2003, Artech House.