## Slide 1: ME1000 RF CIRCUIT DESIGN
<number>
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 10. RF Oscillators
<number>

## Slide 3: Main References
[1]* D.M. Pozar, “Microwave engineering”, 2nd Edition, 1998 John-Wiley & Sons.
[2] J. Millman, C. C. Halkias, “Integrated electronics”, 1972, McGraw-Hill.
[3] R. Ludwig, P. Bretchko, “RF circuit design - theory and applications”, 2000 Prentice-Hall.
[4] B. Razavi, “RF microelectronics”, 1998 Prentice-Hall, TK6560.
[5] J. R. Smith,”Modern communication circuits”,1998 McGraw-Hill.
[6] P. H. Young, “Electronics communication techniques”, 5th edition, 2004 Prentice-Hall.
[7] Gilmore R., Besser L.,”Practical RF circuit design for modern wireless systems”, Vol. 1 & 2, 2003, Artech House.
[8] Ogata K., “Modern control engineering”, 4th edition, 2005, Prentice-Hall.
<number>

## Slide 4: Agenda
Positive feedback oscillator concepts.
Negative resistance oscillator concepts (typically employed for RF oscillator).
Equivalence between positive feedback and negative resistance oscillator theory.
Oscillator start-up requirement and transient.
Oscillator design - Making an amplifier circuit unstable.
Constant |1| circle.
Fixed frequency oscillator design.
Voltage-controlled oscillator design.
<number>

## Slide 5: 1.0 Oscillation Concepts
<number>

## Slide 6: Introduction
Oscillators are a class of circuits with 1 terminal or port, which produce a periodic electrical output upon power up.
Most of us would have encountered oscillator circuits while studying for our basic electronics classes.
Oscillators can be classified into two types: (A) Relaxation and (B) Harmonic oscillators.
Relaxation oscillators (also called astable multivibrator), is a class of circuits with two unstable states. The circuit switches back-and-forth between these states. The output is generally square waves.
Harmonic oscillators are capable of producing near sinusoidal output, and is based on positive feedback approach.
Here we will focus on Harmonic Oscillators for RF systems. Harmonic oscillators are used as this class of circuits are capable of producing stable sinusoidal waveform with low phase noise.
<number>

## Slide 7: 2.0 Overview of Feedback Oscillators
<number>

## Slide 8: Classical Positive Feedback Perspective on Oscillator (1)
Consider the classical feedback system with non-inverting amplifier,
Assuming the feedback network and amplifier do not load each other, we can write the closed-loop transfer function as:
Writing (2.1a) as:
We see that we could get non-zero output at So, with Si = 0, provided 1-A(s)F(s) = 0. Thus the system oscillates!
<number>
+
+
E(s)
So(s)
Si(s)
A(s)
F(s)
Positive
Feedback
Loop gain (the gain of the system
around the feedback loop)
Non-inverting amplifier
(2.1a)
(2.1b)
Feedback network
High impedance
High impedance

## Slide 9: Classical Positive Feedback Perspective on Oscillator (1)
The condition for sustained oscillation, and for oscillation to startup from positive feedback perspective can be summarized as:
Take note that the oscillator is a non-linear circuit, initially upon power up, the condition of (2.2b) will prevail. As the magnitudes of voltages and currents in the circuit increase, the amplifier in the oscillator begins to saturate, reducing the gain, until the loop gain A(s)F(s) becomes one.
A steady-state condition is reached when A(s)F(s) = 1.
<number>
For sustained oscillation
For oscillation to startup
Barkhausen Criterion
(2.2a)
(2.2b)
Note that this is a very simplistic view of oscillators. In reality oscillators
are non-linear systems. The steady-state oscillatory condition corresponds
to what is called a Limit Cycle. See texts on non-linear dynamical systems.

## Slide 10: Classical Positive Feedback Perspective on Oscillator (2)
Positive feedback system can also be achieved with inverting amplifier:
To prevent multiple simultaneous oscillation, the Barkhausen criterion (2.2a) should only be fulfilled at one frequency.
Usually the amplifier A is wideband, and it is the function of the feedback network F(s) to ‘select’ the oscillation frequency, thus the feedback network is usually made of reactive components, such as inductors and capacitors.
<number>
+
-
E(s)
So(s)
Si(s)
-A(s)
F(s)
Inverting amplifier
Inversion

## Slide 11: Classical Positive Feedback Perspective on Oscillator (3)
In general the feedback network F(s) can be implemented as a Pi or T network, in the form of a transformer, or a hybrid of these.
Consider the Pi network with all reactive elements. A simple analysis in [2] and [3] shows that to fulfill (2.2a), the reactance X1, X2 and X3 need to meet the following condition:
<number>
+
-
E(s)
So(s)
-A(s)
X1
X3
X2
If X3 represents inductor, then
X1 and X2 should be capacitors.
(2.3)

## Slide 12: Classical Feedback Oscillators
The following are examples of oscillators, based on the original circuit using vacuum tubes.
<number>
+
-
+
-
+
-
Hartley
oscillator
Clapp
oscillator
Colpitt
oscillator
+
-
Armstrong oscillator

## Slide 13: Example of Tuned Feedback Oscillator (1)
<number>
A 48 MHz Transistor Common
-Emitter Colpitt Oscillator
+
-
E(s)
So(s)
Si(s)
-A(s)
F(s)
Extra
t
0
1

## Slide 14: Example of Tuned Feedback Oscillator (2)
<number>
A 27 MHz Transistor Common-Base
Colpitt Oscilator
+
+
E(s)
So(s)
Si(s)
A(s)
F(s)
Extra

## Slide 15: Example of Tuned Feedback Oscillator (3)
<number>
A 16 MHz Transistor Common-Emitter
Crystal Oscillator
Extra

## Slide 16: Limitation of Feedback Oscillator
At high frequency, the assumption that the amplifier and feedback network do not load each other is not valid. In general the amplifier’s input impedance decreases with frequency, and it’s output impedance is not zero. Thus the actual loop gain is not A(s)F(s) and equation (2.2) breakdowns.
Determining the loop gain of the feedback oscillator is cumbersome at high frequency. Moreover there could be multiple feedback paths due to parasitic inductance and capacitance.
It can be difficult to distinguish between the amplifier and the feedback paths, owing to the coupling between components and conductive structures on the printed circuit board (PCB) or substrate.
Generally it is difficult to physically implement a feedback oscillator once the operating frequency is higher than 500MHz.
<number>

## Slide 17: 3.0 Negative Resistance Oscillators
<number>

## Slide 18: Introduction (1)
An alternative approach is needed to get a circuit to oscillate reliably.
We can view an oscillator as an amplifier that produces an output when there is no input.
Thus it is an unstable amplifier that becomes an oscillator!
For example let’s consider a conditionally stable amplifier.
Here instead of choosing load or source impedance in the stable regions of the Smith Chart, we purposely choose the load or source impedance in the unstable impedance regions. This will result in either |1 | > 1 or |2 | > 1.
The resulting amplifier circuit will be called the Destabilized Amplifier.
As seen in Chapter 7, having a reflection coefficient magnitude for 1 or 2 greater than one implies the corresponding port resistance R1 or R2 is negative, hence the name for this type of oscillator.
<number>

## Slide 19: Introduction (2)
For instance by choosing the load impedance ZL at the unstable region, we could ensure that |1 | > 1. We then choose the source impedance properly so that |1 s | > 1 and oscillation will start up (refer back to Chapter 7 on stability theory).
Once oscillation starts, an oscillating voltage will appear at both the input and output ports of a 2-port network. So it does not matter whether we enforce |1 s | > 1 or |2 L | > 1, enforcing either one will cause oscillation to occur (It can be shown later that when |1 s | > 1 at the input port, |2 L | > 1 at the output port and vice versa).
The key to fixed frequency oscillator design is ensuring that the criteria |1 s | > 1 only happens at one frequency (or a range of intended frequencies), so that no simultaneous oscillations occur at other frequencies.
<number>

## Slide 20: Recap - Wave Propagation Stability Perspective (1)
From our discussion of stability from wave propagation in Chapter 7…
<number>
Z1 or 1
bs
bs1
bss 1
bss 12
bss 212
bss 213
Source
2-port
Network
Zs or s
Port 1
Port 2
bss 313
bss 314
a1
b1
Compare with
equation (2.1a)
Similar mathematical
form
Extra

## Slide 21: Recap - Wave Propagation Stability Perspective (2)
We see that the infinite series that constitute the steady-state incident (a1) and reflected (b1) waves at Port 1 will only converge provided | s1| < 1.
These sinusoidal waves correspond to the voltage and current at the Port 1. If the waves are unbounded it means the corresponding sinusoidal voltage and current at the Port 1 will grow larger as time progresses, indicating oscillation start-up condition.
Therefore oscillation will occur when | s1 | > 1.
Similar argument can be applied to port 2 since the signals at Port 1 and 2 are related to each other in a two-port network, and we see that the condition for oscillation at Port 2 is |L2 | > 1.
<number>
Extra

## Slide 22: Oscillation from Negative Resistance Perspective (1)
Generally it is more useful to work with impedance (or admittance) when designing actual circuit.
Furthermore for practical purpose the transmission lines connecting ZL and Zs to the destabilized amplifier are considered very short (length  0).
In this case the impedance Zo is ambiguous (since there is no transmission line).
To avoid this ambiguity, let us ignore the transmission line and examine the condition for oscillation phenomena in terms of terminal impedance.
<number>
Zs
Zo
Z1
Destabilized
Amp. and
Load
Very short Tline

## Slide 23: Oscillation from Negative Resistance Perspective (2)
We consider Port 1 as shown, with the source network and input of the amplifier being modeled by impedance or series networks.
Using circuit theory the voltage at Port 1 can be written as:
<number>
Source
Network
Port 1
Zs
Z1
(3.1)
jXs
Rs
jX1
R1
V
ZL
Z2
Vamp
Port 2
Amplifier with load ZL

## Slide 24: Oscillation from Negative Resistance Perspective (3)
Furthermore we assume the source network Zs is a series RC network and the equivalent circuit looking into the amplifier Port 1 is a series RL network.
Using Laplace Transform, (3.1) is written as:
<number>
Rs
Cs
R1
L1
V
ZL
Z2
Vamp
Vs
Zs
Z1
where
(3.2a)
(3.2b)

## Slide 25: Oscillation from Negative Resistance Perspective (4)
The expression for V(s) can be written in the “standard” form according to Control Theory [8]:
The transfer function V(s)/Vs(s) is thus a 2nd order system with two poles p1, p2 given by:
Observe that if (R1 + Rs) < 0 the damping factor  is negative. This is true if R1 is negative, and |R1| > Rs.
R1 can be made negative by modifying the amplifier circuit (e.g. adding local positive feedback), producing the sum R1 + Rs < 0.
<number>
(3.3a)
where
(3.4)
(3.3b)

## Slide 26: Oscillation from Negative Resistance Perspective (5)
Assuming ||<1 (under-damped), the poles as in (3.4) will be complex and exist at the right-hand side of the complex plane.
From Control Theory such a system is unstable. Any small perturbation will result in a oscillating signal with frequency that grows exponentially.
Usually a transient or noise signal from the environment will contain a small component at the oscillation frequency. This forms the ‘seed’ in which the oscillation builts up.
<number>


Re
Im
0
Complex
pole pair
Complex Plane
t
A small disturbance
or impulse ‘starts’ the
exponentially growing
sinusoid
Time
Domain
v(t)

## Slide 27: Oscillation from Negative Resistance Perspective (6)
When the signal amplitude builds up, nonlinear effects such as transistor saturation and cut-off will occur, this limits the  of the transistor and finally limits the amplitude of the oscillating signal.
The effect of decreasing  of the transistor is a reduction in the magnitude of R1 (remember R1 is negative). Thus the damping factor  will approach 0, since Rs+ R1  0.
Steady-state sinusoidal oscillation is achieved when  =0, or equivalently the poles become
The steady-state oscillation frequency o corresponds to n,
<number>

## Slide 28: Oscillation from Negative Resistance Perspective (7)
From (3.3b), we observe that the steady-state oscillation frequency is determined by L1 and Cs, in other words, X1 and Xs respectively.
Since the voltages at Port 1 and Port 2 are related, if oscillation occur at Port 1, then oscillation will also occur at Port 2.
From this brief discussion, we use RC and RL networks for the source and amplifier input respectively, however we can distill the more general requirements for oscillation to start-up and achieve steady-state operation for series representation in terms of resistance and reactance:
<number>
(3.6a)
(3.6b)
(3.5a)
(3.5b)
Steady-state
Start-up

## Slide 29: Illustration of Oscillation Start-Up and Steady-State
The oscillation start-up process and steady-state are illustrated.
<number>
Destabilized
Amplifier
ZL
Zs
t
R1+Rs
0
Oscillation
start-up
Steady-state
Z1
Zs
We need to note that this is a very simplistic view of oscillators.
Oscillators are autonomous non-linear dynamical systems, and the steady-state
condition is a form of Limit Cycles.

## Slide 30: Summary of Oscillation Requirements Using Series Network
By expressing Zs and Z1 in terms of resistance and reactance, we conclude that the requirement for oscillation are.
A similar expression for Z2 and ZL can also be obtained, but we shall not be concerned with these here.
<number>
Source
Network
Port 1
Zs
Z1
jXs
Rs
jX1
R1
V
ZL
Z2
Vamp
Port 2
(3.6a)
(3.6b)
(3.5a)
(3.5b)
Steady-state
Start-up

## Slide 31: The Resonator
The source network Zs is usually called the Resonator, as it is clear that equations (3.5b) and (3.6b) represent the resonance condition between the source network and the amplifier input.
The design of the resonator is extremely important.
We shall see later that an important parameter of the oscillator, the Phase Noise is dependent on the quality of the resonator.
<number>

## Slide 32: Summary of Oscillation Requirements Using Parallel Network
If we model the source network and input to the amplifier as parallel networks, the following dual of equations (3.5) and (3.6) are obtained.
The start-up and steady-state conditions are:
<number>
jBs
Gs
jB1
G1
V
ZL
Z2
Vamp
Port 1
Steady-state
Start-up
(3.7a)
(3.7b)
(3.8a)
(3.8b)

## Slide 33: Series or Parallel Representation? (1)
The question is which to use? Series or parallel network representation? This is not an easy question to answer as the destabilized amplifier is operating in nonlinear region as oscillator.
Concept of impedance is not valid and our discussion is only an approximation at best.
We can assume series representation, and worked out the corresponding resonator impedance. If after computer simulation we discover that the actual oscillating frequency is far from our prediction (if there’s any oscillation at all!), then it probably means that the series representation is incorrect, and we should try the parallel representation.
Another clue to whether series or parallel representation is more accurate is to observe the current and voltage in the resonator. For series circuit the current is near sinusoidal, where as for parallel circuit it is the voltage that is sinusoidal.
<number>

## Slide 34: Series or Parallel Representation? (2)
Reference [7] illustrates another effective alternative, by computing the large-signal S11 of Port 1 (with respect to Zo) using CAD software.
1/S11 is then plotted on a Smith Chart as a function of input signal magnitude at the operating frequency.
By comparing the locus of 1/S11 as input signal magnitude is gradually increased with the coordinate of constant X or constant B circles on the Smith Chart, we can decide whether series or parallel form approximates Port 1 best.
We will adopt this approach, but plot S11 instead of 1/S11. This will be illustrated in the examples in next section.
Do note that there are other reasons that can cause the actual oscillation frequency to deviate a lot from prediction, such as frequency stability issue (see [1] and [7]).
<number>

## Slide 35: 4.0 Fixed Frequency Negative Resistance Oscillator Design
<number>

## Slide 36: Procedures of Designing Fixed Frequency Oscillator (1)
Step 1 - Design a transistor/FET amplifier circuit.
Step 2 - Make the circuit unstable by adding positive feedback at radio frequency, for instance, adding series inductor at the base for common-base configuration.
Step 3 - Determine the frequency of oscillation o and extract S-parameters at that frequency.
Step 4 – With the aid of Smith Chart and Load Stability Circle, make R1 < 0 by selecting L in the unstable region.
Step 5 (Optional) – Perform a large-signal analysis (e.g. Harmonic Balance analysis) and plot large-signal S11 versus input magnitude on Smith Chart. Decide whether series or parallel form to use.
Step 6 - Find Z1 = R1 + jX1 (Assuming series form).
<number>

## Slide 37: Procedures of Designing Fixed Frequency Oscillator (2)
Step 7 – Find Rs and Xs so that R1 + Rs<0, X1 + Xs=0 at o. We can use the rule of thumb Rs=(1/3)|R1| to control the harmonics content at steady-state.
Step 8 - Design the impedance transformation network for Zs and ZL.
Step 9 - Built the circuit or run a computer simulation to verify that the circuit can indeed starts oscillating when power is connected.
Note: Alternatively we may begin Step 4 using Source Stability Circle, select s in the unstable region so that R2 or G2 is negative at o .
<number>

## Slide 38: Making an Amplifier Unstable (1)
An amplifier can be made unstable by providing some kind of local positive feedback.
Two favorite transistor amplifier configurations used for oscillator design are the Common-Base configuration with Base feedback and Common-Emitter configuration with Emitter degeneration.
<number>

## Slide 39: Making an Amplifier Unstable (2)
<number>
Positive feedback
here
Common Base
Configuration
This is a practical model
of an inductor
An inductor is added
in series with the bypass
capacitor on the base
terminal of the BJT.
This is a form of positive
series feedback.
Base bypass
capacitor
At 410MHz

## Slide 40: Making an Amplifier Unstable (3)
<number>
Unstable Regions
s22 and s11 have magnitude > 1
L Plane
s Plane

## Slide 41: Making an Amplifier Unstable (4)
<number>
Positive feedback here
Common Emitter
Configuration
Feedback

## Slide 42: Making an Amplifier Unstable (5)
<number>
Unstable
Regions
S22 and S11 have magnitude > 1
L Plane
s Plane

## Slide 43: Precautions
The requirement Rs= (1/3)|R1| is a rule of thumb to provide the excess gain to start up oscillation.
Rs that is too large (near |R1| ) runs the risk of oscillator fails to start up due to component characteristic deviation.
While Rs that is too small (smaller than (1/3)|R1|) causes too much non-linearity in the circuit, this will result in large harmonic distortion of the output waveform.
<number>
V2
Clipping, a sign of
too much nonlinearity
t
Rs too small
t
V2
Rs too large
For more discussion about the Rs = (1/3)|R1| rule,
and on the sufficient condition for oscillation, see [6], which list further requirements.

## Slide 44: Aid for Oscillator Design - Constant |1| Circle (1)
In choosing a suitable L to make |L | > 1, we would like to know the range of L that would result in a specific |1 |.
It turns out that if we fix |1 |, the range of load reflection coefficient that result in this value falls on a circle in the Smith chart for L .
The radius and center of this circle can be derived from:
Assuming  = |1 |:
<number>
By fixing |1 | and changing L .
(4.1a)
(4.1b)

## Slide 45: Aid for Oscillator Design - Constant |1| Circle (2)
The Constant |1 | Circle is extremely useful in helping us to choose a suitable load reflection coefficient. Usually we would choose L that would result in |1 | = 1.5 or larger.
Similarly Constant |2 | Circle can also be plotted for the source reflection coefficient. The expressions for center and radius is similar to the case for Constant |1 | Circle except we interchange s11 and s22, L and s . See Ref [1] and [2] for details of derivation.
<number>

## Slide 46: Example 4.1 – CB Fixed Frequency Oscillator Design
In this example, the design of a fixed frequency oscillator operating at 410MHz will be demonstrated using BFR92A transistor in SOT23 package. The transistor will be biased in Common-Base configuration.
It is assumed that a 50 load will be connected to the output of the oscillator. The schematic of the basic amplifier circuit is as shown in the following slide.
The design is performed using Agilent’s ADS software, but the author would like to stress that virtually any RF CAD package is suitable for this exercise.
<number>

## Slide 47: Example 4.1 Cont...
Step 1 and 2 - DC biasing circuit design and S-parameter extraction.
<number>
Port 1 - Input
Port 2 - Output
Amplifier
Port 1
Port 2
LB is chosen care-
fully so that the
unstable regions
in both L and s
planes are large
enough.

## Slide 48: Example 4.1 Cont...
<number>
Unstable Regions
Load impedance here will result
in |1| > 1
Source impedance here will result
in |2| > 1

## Slide 49: Example 4.1 Cont...
Step 3 and 4 - Choosing suitable L that cause |1 | > 1 at 410MHz. We plot a few constant |1 | circles on the L plane to assist us in choosing a suitable load reflection coefficient.
<number>
LSC
|1 |=1.5
|1 |=2.0
|1 |=2.5
L = 0.5<0
This point is chosen
because it is on
real line and easily
matched.
L Plane
Note: More difficult
to implement load
impedance near
edges of Smith
Chart
ZL = 150+j0

## Slide 50: Example 4.1 Cont...
Step 5 – To check whether the input of the destabilized amplifier is closer to series or parallel form. We perform large-signal analysis and observe the S11 at the input of the destabilized amplifier.
<number>
We are measuring
large-signal S11 looking
towards here
Extra
Large-signal
S-parameter
Analysis control
in ADS software.

## Slide 51: Example 4.1 Cont...
Compare the locus of S11 and the constant X and constant B circles on the Smith Chart, it is clear the locus is more parallel to the constant X circle. Also the direction of S11 is moving from negative R to positive R as input power level is increased. We conclude the Series form is more appropriate.
<number>
Region where R1 or G1 is negative
Direction of S11 as magnitude
of P_1tone source is increased
Compare
Locus of S11 versus P_1tone
power at 410MHz
(from -20 to -5 dBm)
Boundary of
Normal Smith Chart
Region where R1 or G1 is positive
Extra

## Slide 52: Example 4.1 Cont...
Step 6 – Using the series form, we find the small-signal input impedance Z1 at 410MHz. So the resonator would also be a series network.
For ZL = 150 or L = 0.5<0:
Step 7 - Finding the suitable source impedance to fulfill R1 + Rs<0, X1 + Xs=0:
<number>
R1
X1

## Slide 53: Example 4.1 Cont...
The system block diagram:
<number>
Common-Base (CB)
Amplifier
with feedback
Port 1
Port 2
Zs = 3.42-j7.851
ZL = 150

## Slide 54: Example 4.1 Cont...
Step 5 - Realization of the source and load impedance at 410MHz.
<number>
CB Amplifier
3.42
27.27nH
49.44pF
50
Zs= 3.42-j7.851
ZL=150
@ 410MHz
3.49pF
Impedance transformation
network

## Slide 55: Example 4.1 Cont... - Verification Thru Simulation
<number>
Vpp = 0.9V
V = 0.45V
Power dissipated in the load:
BFR92A
Vpp

## Slide 56: Example 4.1 Cont... - Verification Thru Simulation
Performing Fourier Analysis on the steady state wave form:
<number>
484 MHz
The waveform is very clean with
little harmonic distortion. Although
we may have to tune the capacitor
Cs to obtain oscillation at 410 MHz.

## Slide 57: Example 4.1 Cont... – The Prototype
<number>
Voltage at the base terminal and 50 Ohms load resistor of the
fixed frequency oscillator:
Output port
Vout
Vbb
V
ns
Startup transient

## Slide 58: Example 4.2 – 450 MHz CE Fixed Frequency Oscillator Design
Small-signal AC or S-parameter analysis, to show that R1 or G1 is negative at the intended oscillation frequency of 450 MHz.
<number>
Selection of load
resistor as in
Example 4.1.
There are simplified
expressions to find C1
and C2, see reference [5].
Here we just trial and
error to get some
reasonable values.
Destabilized
amplifier

## Slide 59: Example 4.2 Cont…
The large-signal analysis to check for suitable representation.
<number>
Direction of S11 as magnitude
of P_1tone source is increased
from -5 to +15 dBm
Compare
Since the locus of S11 is close in shape to
constant X circles, and it indicates R1 goes from
negative value to positive values as input power
is increased, we use series form to
represent the input network looking towards
the Base of the amplifier.
Boundary of
Normal Smith Chart
Extra
S11

## Slide 60: Example 4.2 Cont…
Using a series RL for the resonator, and performing time-domain simulation to verify that the circuit will oscillate.
<number>
vL(t)
|VL(f)|
Large coupling
capacitor

## Slide 61: Example 4.3 – Parallel Representation
An example where the network looking into the Base of the destabilized amplifier is more appropriate as parallel RC network.
<number>
S11
Compare
Direction of S11 as magnitude
of P_1tone source is increased
from -7 to +12 dBm
S11 versus
Input power

## Slide 62: Frequency Stability
The process of oscillation depends on the non-linear behavior of the negative-resistance network.
The conditions discussed, e.g. equations (3.1), (3.8), (3.9), (3.10) and (3.11) are not enough to guarantee a stable state of oscillation. In particular, stability requires that any perturbation in current, voltage and frequency will be damped out, allowing the oscillator to return to it’s initial state.
The stability of oscillation can be expressed in terms of the partial derivative of the sum Zin + Zs or Yin + Ys of the input port (or output port).
The discussion is beyond the scope of this chapter for now, and the reader should refer to [1] and [7] for the concepts.
<number>

## Slide 63: Some Steps to Improve Oscillator Performance
To improve the frequency stability of the oscillator, the following steps can be taken.
Use components with known temperature coefficients, especially capacitors.
Neutralize, or swamp-out with resistors, the effects of active device variations due to temperature, power supply and circuit load changes.
Operate the oscillator on lower power.
Reduce noise, use shielding, AGC (automatic gain control) and bias-line filtering.
Use an oven or temperature compensating circuitry (such as thermistor).
Use differential oscillator architecture (see [4] and [7]).
<number>

## Slide 64: Extra References for This Section
Some recommended journal papers on frequency stability of oscillator:
Kurokawa K., “Some basic characteristics of broadband negative resistance oscillator circuits”, Bell System Technical Journal, pp. 1937-1955, 1969.
Nguyen N.M., Meyer R.G., “Start-up and frequency stability in high-frequency oscillators”,IEEE journal of Solid-State Circuits, vol 27, no. 5 pp.810-819, 1992.
Grebennikov A. V., “Stability of negative resistance oscillator circuits”, International journal of Electronic Engineering Education, Vol. 36, pp. 242-254, 1999.
<number>

## Slide 65: Reconciliation Between Feedback and Negative Resistance Oscillator Perspectives
It must be emphasized that the circuit we obtained using negative resistance approach can be cast into the familiar feedback form. For instance an oscillator circuit similar to Example 4.2 can be redrawn as:
<number>
Amplifier
Feedback
Network
Extra
Negative Resistance
Oscillator

## Slide 66: 5.0 Voltage Controlled Oscillator
<number>

## Slide 67: About the Voltage Controlled Oscillator (VCO) (1)
A simple transistor VCO using Clapp-Gouriet or CE configuration will be designed to illustrate the principles of VCO.
The transistor chosen for the job is BFR92A, a wide-band NPN transistor which comes in SOT-23 package.
Similar concepts as in the design of fixed-frequency oscillators are employed. Where we design the biasing of the transistor, destabilize the network and carefully choose a load so that from the input port (Port 1), the oscillator circuit has an impedance (assuming series representation is valid):
Of which R1 is negative, for a range of frequencies from 1 to 2.
<number>
Lower
Upper

## Slide 68: About the Voltage Controlled Oscillator (VCO) (2)
<number>
Clapp-Gouriet
Oscillator Circuit
with Load
Zs
Z1 = R1 + jX1
ZL

## Slide 69: About the Voltage Controlled Oscillator (VCO) (3)
If we can connect a source impedance Zs to the input port, such that within a range of frequencies from 1 to 2:
The circuit will oscillate within this range of frequencies. By changing the value of Xs, one can change the oscillation frequency.
For example, if X1 is positive, then Xs must be negative, and it can be generated by a series capacitor. By changing the capacitance, one can change the oscillation frequency of the circuit.
If X1 is negative, Xs must be positive. A variable capacitor in series with a suitable inductor will allow us to adjust the value of Xs.
<number>
The rationale is that only the initial spectral of the noise
signal fulfilling Xs = X1 will start the oscillation.

## Slide 70: Schematic of the VCO
<number>
2-port network
Variable
capacitance
tuning network
Initial noise
source to start
the oscillation

## Slide 71: More on the Schematic
L2 together with Cb3, Cb4 and the junction capacitance of D1 can produce a range of reactance value, from negative to positive. Together these components form the frequency determining network.
Cb4 is optional, it is used to introduce a capacitive offset to the junction capacitance of D1.
R1 is used to isolate the control voltage Vdc from the frequency determining network. It must be a high quality SMD resistor. The effectiveness of isolation can be improved by adding a RF choke in series with R1 and a shunt capacitor at the control voltage.
Notice that the frequency determining network has no actual resistance to counter the effect of |R1()|. This is provided by the loss resistance of L2 and the junction resistance of D1.
<number>

## Slide 72: Time Domain Result
<number>
Vout when Vdc = -1.5V

## Slide 73: Load-Pull Experiment
Peak-to-peak output voltage versus Rload for Vdc = -1.5V.
<number>
Vout(pp)
RLoad

## Slide 74: Controlling Harmonic Distortion (1)
Since the resistance in the frequency determining network is too small, large amount of non-linearity is needed to limit the output voltage waveform, as shown below there is a lot of distortion.
<number>
Vout

## Slide 75: Controlling Harmonic Distortion (2)
The distortion generates substantial amount of higher harmonics.
This can be reduced by decreasing the positive feedback, by adding a small capacitance across the collector and base of transistor Q1. This is shown in the next slide.
<number>

## Slide 76: Controlling Harmonic Distortion (3)
<number>
Capacitor to control positive feedback
The observant
person would
probably notice
that we can also
reduce the harmonic
distortion by introducing
a series resistance in
the tuning network.
However this is not
advisable as the phase
noise at the oscillator’s
output will increase (
more about this later).
Control voltage
Vcontrol

## Slide 77: Controlling Harmonic Distortion (4)
The output waveform Vout after this modification is shown below:
<number>
Vout

## Slide 78: Controlling Harmonic Distortion (5)
Finally, it should be noted that we should also add a low-pass filter (LPF) at the output of the oscillator to suppress the higher harmonic components. Such LPF is usually called Harmonic Filter.
Since the oscillator is operating in nonlinear mode, care must be taken in designing the LPF.
Another practical design example will illustrate this approach.
<number>

## Slide 79: The Tuning Range
Actual measurement is carried out, with the frequency measured using a high bandwidth digital storage oscilloscope.
<number>
MHz
Volts
D1 is BB149A,
a varactor
manufactured by
Phillips
Semiconductor (Now NXP).

## Slide 80: Phase Noise in Oscillator (1)
Since the oscillator output is periodic. In frequency domain we would expect a series of harmonics.
In a practical oscillation system, the instantaneous frequency and magnitude of oscillation are not constant. These will fluctuate as a function of time.
These random fluctuations are noise, and in frequency domain the effect of the spectra will ‘smear out’.
<number>
f
fo
2fo
3fo
Ideal oscillator output
f
fo
2fo
3fo
t
t
Real oscillator output
Smearing
Extra

## Slide 81: Phase Noise in Oscillator (2)
Mathematically, we can say that the instantaneous frequency and magnitude of oscillation are not constant. These will fluctuate as a function of time.
As a result, the output in the frequency domain is ‘smeared’ out.
<number>
t
v(t)
t
v(t)
f
fo
f
fo
Extra
T = 1/fo
Contains both phase
and amplitude modulation
of the sinusoidal waveform
at frequency fo
Leeson’s expression
Large phase noise
Small phase noise

## Slide 82: Phase Noise in Oscillator (3)
Typically the magnitude fluctuation is small (or can be minimized) due to the oscillator nonlinear limiting process under steady-state.
Thus the smearing is largely attributed to phase variation and is known as Phase Noise.
Phase noise is measured with respect to the signal level at various offset frequencies.
<number>
Extra
Phase noise is measured in dBc/Hz @ foffset.
dBc/Hz stands for dB down
from the carrier (the ‘c’) in 1 Hz bandwidth.
For example
-90dBc/Hz @ 100kHz offset from a CW sine wave at 2.4GHz.
- 90dBc/Hz
100kHz
f
fo
t
v(t)
Signal level
Assume amplitude limiting effect
Of the oscillator reduces amplitude fluctuation

## Slide 83: Reducing Phase Noise (1)
Requirement 1: The resonator network of an oscillator must have a high Q factor. This is an indication of low dissipation loss in the tuning network (See Chapter 3a – impedance transformation network on Q factor).
<number>
X1
Xtune
-X1
f
f
2|X1|
Tuning
Network with
High Q
X1
Xtune
-X1
f
f
2|X1|
Tuning
Network with
Low Q
Ztune = Rtune +jXtune
Extra
Variation in Xtune
due to environment
causes small change
in instantaneous
frequency.

## Slide 84: Reducing Phase Noise (2)
A Q factor in the tuning network of at least 20 is needed for medium performance oscillator circuits at UHF. For highly stable oscillator, Q factor of the tuning network must be in excess or 1000.
We have looked at LC tuning networks, which can give Q factor of up to 40. Ceramic resonator can provide Q factor greater than 500, while piezoelectric crystal can provide Q factor > 10000.
At microwave frequency, the LC tuning networks can be substituted with transmission line sections.
See R. W. Rhea, “Oscillator design & computer simulation”, 2nd edition 1995, McGraw-Hill, or the book by R.E. Collin for more discussions on Q factor.
Requirement 2: The power supply to the oscillator circuit should also be very stable to prevent unwanted amplitude modulation at the oscillator’s output.
<number>
Extra

## Slide 85: Reducing Phase Noise (3)
Requirement 3: The voltage level of Vcontrol should be stable.
Requirement 4: The circuit has to be properly shielded from electromagnetic interference from other modules.
Requirement 5: Use low noise components in the construction of the oscillator, e.g. small resistance values, low-loss capacitors and inductors, low-loss PCB dielectric, use discrete components instead of integrated circuits.
<number>
Extra

## Slide 86: Example of Phase Noise from VCOs
Comparison of two VCO outputs on a spectrum analyzer*.
<number>
Extra
*The spectrum
analyzer internal
oscillator must
of course has
a phase noise of
an order of magnitude
lower than our VCO
under test.
VCO output
with high
phase noise
VCO output
with low
phase noise

## Slide 87: More Materials
This short discussion cannot do justice to the material on phase noise.
For instance the mathematical model of phase noise in oscillator and the famous Leeson’s equation is not shown here. You can find further discussion in [4], and some material for further readings on this topic:
  D. Schere, “The art of phase noise measurement”, Hewlett Packard RF & Microwave Measurement Symposium, 1985.
  T. Lee, A. Hajimiri, “The design of low noise oscillators”, Kluwer, 1999.
<number>
Extra

## Slide 88: More on Varactor
The varactor diode is basically a PN junction optimized for its linear junction capacitance.
It is always operated in the reverse-biased mode to prevent nonlinearity, which generate harmonics.
<number>
As we increase the negative
biasing voltage Vj , Cj decreases,
hence the oscillation frequency increases.
The abrupt junction varactor has high
Q, but low sensitivity (e.g. Cj varies
little over large voltage change).
The hyperabrupt junction varactor
has low Q, but higher sensitivity.
Extra
Vj
Vj
0
Cj
Linear region
Reverse biased
Forward biased
Cjo

## Slide 89: A Better Variable Capacitor Network
The back-to-back varactors are commonly employed in a VCO circuit, so that at low Vcontrol, when one of the diode is being affected by the AC voltage, the other is still being reverse biased.
When a diode is forward biased, the PN junction capacitance becomes nonlinear.
The reverse biased diode has smaller junction capacitance, and this dominates the overall capacitance of the back-to-back varactor network.
This configuration helps to decrease the harmonic distortion.
<number>
At any one time, at least one of
the diode will be reverse biased.
The junction capacitance of the
reverse biased diode will dominate
the overall capacitance of the
network.
Extra
Vcontrol
Symbol
for Varactor
To suppress
RF signals
To negative
resistance
amplifier
Vcontrol
Vcontrol

## Slide 90: Example 5.1 – VCO Design for Frequency Synthesizer
To design a low power VCO that works from 810 MHz to 910 MHz.
Power supply = 3.0V.
Output power (into 50Ω load) minimum -3.0 dBm.
<number>

## Slide 91: Example 5.1 Cont…
Checking the d.c. biasing and AC simulation.
<number>
Z11

## Slide 92: Example 5.1 Cont…
Checking the results – real and imaginary portion of Z1 when output is terminated with ZL = 100Ω.
<number>

## Slide 93: Example 5.1 Cont…
The resonator design.
<number>

## Slide 94: Example 5.1 Cont…
The resonator reactance.
<number>
Resonator
reactance
as a function of
control voltage
The theoretical tuning
range
-X1 of the destabilized amplifier

## Slide 95: Example 5.1 Cont…
The complete schematic with the harmonic suppression filter.
<number>
Low-pass filter

## Slide 96: Example 5.1 Cont…
The prototype and the result captured from a spectrum analyzer (9 kHz to 3 GHz).
<number>
VCO
Harmonic
suppression filter
Fundamental
-1.5 dBm
- 30 dBm

## Slide 97: Example 5.1 Cont…
Examining the phase noise of the oscillator (of course the accuracy is limited by the stability of the spectrum analyzer used).
<number>
Span = 500 kHz
RBW = 300 Hz
VBW = 300 Hz
-0.42 dBm

## Slide 98: Example 5.1 Cont…
VCO gain (ko) measurement setup:
<number>
Spectrum
Analyzer
Variable
power
supply

## Slide 99: Example 5.1 Cont…
Measured results:
April 2012
 2006 by Fabian Kung Wai Lee
<number>
0.0
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
750
800
850
900
950
fVCO / MHz
Vcontrol/Volts

## Slide 100: References
[1]* D.M. Pozar, “Microwave Engineering”, 2nd Edition, 1998 John-Wiley & Sons
[2] R. Ludwig, P. Bretchko, “RF Circuit Design: Theory and Applications”, 2000 Prentice-Hall
[3] B. Razavi, “RF Microelectronics”, 1998 Prentice-Hall, TK6560
[4] J. R. Smith, “Modern Communication Circuits”,1998 McGraw-Hill
[5] P. H. Young, “Electronics Communication Techniques”, 5th edition, 2004 Prentice-Hall
[6] Gilmore R., Besser L., “Practical RF Circuit Design for Modern Wireless Systems”, Vol. 1 & 2, 2003, Artech House
Notes: <number>