## Slide 1: ME1000 RF CIRCUIT DESIGN
<number>
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 8A. Small-Signal Amplifier (SSA) Design — Maximum Power Gain and Fixed Transducer Power Gain
Notes: <number>

## Slide 3: Basic Single-Stage Small-Signal Amplifier Design Flow
Define
Center frequency, fo
Power gain, GT
Noise figure, F
Source/load impedance
Bandwidth
VSWR
Select
active component
Design DC
biasing circuit
Get S-parameters
Stability analysis and
stabilization
Design input and output
impedance transformation
networks with Smith Charts
Check GT, noise figure,
VSWR, bandwidth
Prototyping
Satisfied
Tuning and
optimization
Not
satisfied
Some graphical tools used:
Constant GP circles
Constant F circles
Constant GA circles
Constant VSWR/mismatch circles
Large-signal
analysis:
Gain compression
TOI
Efficiency
Various types of SSA:
Maximum power gain
Lowest noise
Maximum output power
Notes: <number>

## Slide 4: Linear/Quasi-Linear Amplifier Types
Amplifier Type | Require s | Require L | Graphical tools
Maximum Unilateral GT | s11* | s22* | None
Maximum GT(max) | sm | Lm | None
Fixed GT with user-defined F and input mismatch | Tunable | Tunable | Constant GP circle Constant F circle Constant VSWR/Mismatch circle Constant GA circle
Lowest noise | m | Tunable (typically = 2*) | Constant F circle
Maximum Output Power | sm | OL | Constant PL contour
Good for lower
frequency,
fo < 500 MHz.
Not discussed
Here.
Discussed
in High Power
Circuits
Notes: <number>

## Slide 5: 1.0 Maximum GT Amplifier: Simultaneous Conjugate Match
Notes: <number>

## Slide 6: Simultaneous Conjugate Match in an Amplifier
To maximize the power transfer in an amplifier, both input and output ports of the amplifier have to be conjugately matched
When both input and output impedances of the amplifier are conjugately matched to the source and load impedances, the amplifier is called Simultaneous Conjugately Match (SCM)
It is not easy to achieve SCM, as L affects 1, and s affects 2. Only under special conditions can SCM occur.
Under SCM, Gp= GA= GT, and the gain obtained from the amplifier is the maximum gain, GT(max)
Most of the time the condition for SCM is not fulfilled and we can only optimized the power gain of the amplifier while GT(max) is not attainable
Notes: <number>

## Slide 7: Simultaneous Conjugate Match in an Amplifier (cont’d)
Amplifier
(2-port)
Source
Load
s = 1*
2* = L
Amplifier
(2-port)
Source
Load
s  1*
2*  L
Non-SCM
SCM condition
Notes: <number>

## Slide 8: Load and Source Impedances for the Simultaneous Conjugate Match
The input and output reflection coefficients of an amplifier are given by:
When we want the input and output ports of the amplifier to be conjugately matched to the source and load impedances, s= 1* and L= 2*.
Thus, we need to solve the following simultaneous equations:
This can only happen for a particular set of source and load impedances (as s affects 2, and L affects 1).
Notes: <number>

## Slide 9: Load and Source Impedances for the Simultaneous Conjugate Match (cont’d)
Solving both equations simultaneously results in (1.1a) and (1.1b):
(1.1a)
(1.1b)
Notes: <number>

## Slide 10: Power Gain During the Simultaneous Conjugate Match
When we connect source and load impedances having Sm and Lm respectively to an amplifier, Pin = PAs, PL= PAo
As a result, GP = GT = GA
Also note that transducer power gain, GT under this condition is the maximum power gain! It is commonly denoted by GT(max)
PL
PAs
PRs = 0
Pin = PAs
PAo
PL = PAo
Pro = 0
ZL
Vs
Zs
Amplifier
S
L
Input
Transformation
Network
Output
Transformation
Network
Sm*
Lm*
Sm
Lm
K>1
Notes: <number>

## Slide 11: Power Gains During the Simultaneous Conjugate Match (cont’d)
Substituting (1.1a) and (1.1b) into the expression for GP will give us GT(max)
Gp = GT = GA = GT(max)
(1.2a)
(1.2b)
Roulette Stability Factor
Lm
GP(max)
K
1
GMS
Maximum
stable
gain
Notes: <number>

## Slide 12: Summary for an SCM Amplifier Design
SCM to obtain maximum power gain can only be applied when the amplifier is unconditionally stable with the input and output ports conjugately matched.
When this happens, the maximum power gain that can be obtained is:
The limit for GT(max) is GMS. It is the largest maximum stable power gain that can be achieved for an amplifier.
From the above relations for GT(max), it is only real if K  1. Thus, an amplifier can only be simultaneously conjugate matched when it is unconditionally stable (passes the K-factor test).
If the amplifier is only conditionally stable, then SCM or the maximum power gain cannot be achieved. The required values for Lm and Sm will fall outside the unit disc of the Smith chart. We can only optimize GT up to a certain point.
(1.3)
Notes: <number>

## Slide 13: Example 1.1: SCM Amplifier Design
A BJT with IC = 10 mA and VCE = 6 V is operated at 2.4 GHz. The corresponding S-parameters are s11 = 0.3 < 30°, s12 = 0.2 < –60°, s21 = 2.5 < –80°, and s22 = 0.2 < –15°. Determine whether the transistor is unconditionally stable and find the values for s and L that provide the maximum power gain. Sketch the schematics of the system (use a box to represent the amplifier).
Notes: <number>

## Slide 14: Solution to Example 1.1
Stability Test:
Since K > 1 and |D| < 1, the amplifier is unconditionally stable.
We can maximize the power gain Gp by carrying out the simultaneous conjugate match design.
Notes: <number>

## Slide 15: Solution to Example 1.1 (cont’d)
Use (1.1a) to find:
Use (1.1b) to find:
Convert to impedance:
Notes: <number>

## Slide 16: Solution to Example 1.1 (cont’d)
Finding the maximum power gain:
Amplifier
53.085 +
j12.508
86.889 –
j17.325
Notes: <number>

## Slide 17: Appendix 1: Derivation of the Source and Load Impedances for the Simultaneous Conjugate Match and Constant Power Gain Circle
Notes: <number>

## Slide 18: The Conditions for the Maximum GP
We start by looking at the expression for the power gain GP.
We call this the normalized power gain. Notice that it is dependent on L.
Even though the method presented here is much longer, it gives more insights into the characteristics of the power gain GP.
Notes: <number>

## Slide 19: The Conditions for the Maximum GP (cont’d)
If we could maximize |g2|, then GP can be maximized.
Using:
Using:
We can rewrite the above expression as:
Because |s21| is fixed, it is an important parameter in an amplifier design. It sets the limit of the power gain.
Notes: <number>

## Slide 20: The Conditions for the Maximum GP (cont’d)
This can be further expanded into a circle equation in the complex plane:
Where:
(A.1)
(A.2)
Coordinate for the center of a circle
The radius of a circle
Notes: <number>

## Slide 21: The Conditions for the Maximum GP (cont’d)
2c2 can be further simplified using the identity:
To:
Where:
(A.3)
(A.4)
Notes: <number>

## Slide 22: The Conditions for the Maximum GP (cont’d)
Expression (A.1) again represents a circle in the complex L = U2 + jV2 plane.
For each value of g2, a circle can be drawn. Thus each circle represents the contour of the constant power gain GP for a given load ZL. When 2c2 = 0, the power gain is maximum.
Take note that there is no minimum power gain! GP can only approach 0.
What happens if we set g2 > go?
Im( L )
Re( L )
g4
g3
g2
g1
g0
Notes: <number>

## Slide 23: The Conditions for the Maximum GP (cont’d)
From (A.3), when 2c2 = 0:
Since g2(max) only exists if K > 1, this implies the maximum gain only exists when the amplifier is unconditionally stable.
At K = 1,
This power gain is known as the Maximum Stable Gain, GMS. This is the maximum power gain that is achievable!!! It is often specified in the datasheet of an amplifier or amplification device and gives the theoretical maximum gain achievable.
GP(max)
K
1
GMS
Maximum of the
maximum !!!
Notes: <number>

## Slide 24: Corresponding Load Impedance for the Maximum Power Gain
(A.5a)
(A.5b)
From (A.1) and putting 2c2 = 0:
Notes: <number>

## Slide 25: Load Impedance for the Maximum Power Gain
By expanding (A.5a) and (A.5b) using g2(max), we can show that:
Or:
The proof is extremely tedious and will not be shown here. You can refer to the extra hand-written notes for the proof.
(A.6a)
Notes: <number>

## Slide 26: Source Impedance for the Maximum Power Gain
(A.6b)
Using:
We can obtain the corresponding 1.
And requiring S = 1 *, the source reflection coefficient can be obtained.
Notes: <number>

## Slide 27: 2.0 Design for the Fixed Transducer Power Gain GT: The Constant GP Circle Approach
Notes: <number>

## Slide 28: Constant Power Gain Circles
From the Dependency Diagram of the previous chapter, we see that GP only depends on L. It is indeed possible to determine the range of L which would give a fixed GP, and this range actually falls on the locus of a circle on the Smith Chart.
From the equation (A.1) of Appendix 1, the radius and center of the Constant Power Gain Circle are given by:
(2.1a)
(2.1b)
(2.1c)
(2.1d)
Center
of circle
Radius
of circle
Normalized GP
Notes: <number>

## Slide 29: Constant Power Gain Circles (cont’d)
Im
Re
TGp
RGp
L Plane
Constant Gp circle
ZL, which falls on this circle, will give a similar GP when connected to the amplifier output
0
Notes: <number>

## Slide 30: The Constant Gp Circle Approach
Use the constant Gp circles together with the LSC (if the amplifier is conditionally stable) to select the appropriate L.
From the selected L, determine 1.
Conjugate match the input port (make sure that s is in the stable region).
Thus GT = Gp.
PAo
PL
Pro
PAs
PRs = 0
Pin = PAs
PL
S
S*
2
L’
Vs
Zs
Amplifier
Output
Transformation
Network
ZL
Input
Transformation
Network
Notes: <number>

## Slide 31: Example 2.1: Constant GP Amplifier Design
A microwave BJT has s11 = 0.9 < 60°, s12 = 0.06 < 60°, s21 = 3 < 120°, s22 = 0.82 < –30° at 1.2 GHz. Design a single-stage amplifier having a 50  input and output transmission lines, with a required transducer power gain between 40 to 50.
Solution…
K = 0.902 and |D| = 0.898, so the amplifier is conditionally stable.
S-parameters at 1.2 GHz:
Notes: <number>

## Slide 32: Example 2.1: Constant GP Amplifier Design (cont’d)
Since |s11| = 0.9 < 1 and the LSC encloses the origin, the stable region is as indicated.
LSC
Stable region
Plane for L
Plot the Load Stability Circle…
Notes: <number>

## Slide 33: Example 2.1: Constant GP Amplifier Design (cont’d)
Constant GP circle for Gp = 36
Constant GP circle for Gp = 45
Notes: <number>

## Slide 34: Example 2.1: Constant GP Amplifier Design (cont’d)
L = 0.05 < –0.6177 rad
LSC
GP = 36
GP = 45
Constant GP circles on the L plane
This point is the farthest away from the LSC, it is less susceptible to the parameter changes.
Draw the constant power gain circles…
Notes: <number>

## Slide 35: Example 2.1: Constant GP Amplifier Design (cont’d)
Finding the corresponding load impedance:
Notes: <number>

## Slide 36: Example 2.1: Constant GP Amplifier Design (cont’d)
Finding the corresponding input impedance and taking its complex conjugate:
Notes: <number>

## Slide 37: Example 2.1: Constant GP Amplifier Design (cont’d)
The block diagram:
GT = PL/Pin = 45
Amplifier
54.154
–j3.144
PL
Pin
10.13
–j84.70
Notes: <number>

## Slide 38: Example 2.1: Constant GP Amplifier Design (cont’d)
Since the actual Zs and ZL are 50 , the impedance transformation network is needed to change the 50  load impedance into 54.154 – j3.144, and to 10.13 – j84.70 for the source impedance. We may use either two or three elements impedance transformation network. This is shown below for the load network.
jX
jB
50
54.154 – j3.144
RL=50, XL=0, Rs=54.154, Xs = –3.144
Notes: <number>

## Slide 39: Example 2.1: Constant GP Amplifier Design (cont’d)
The final network:
GT = PL/Pin = 45
Amplifier
1.95 nH
50
0.86 pF
1.26 pF
3.38 nH
50
ZL = 54.154 – j3.144
ZS = 10.13 – j84.70
Notes: <number>

## Slide 40: 3.0 Design for a Fixed Transducer Power Gain GT: The Constant GA Circle Approach
Notes: <number>

## Slide 41: Preliminary
This approach is just the dual of the Constant GP Approach
Instead of tuning L for a fixed GP, we tune s for a fixed GA. Therefore, the constant GA circles and s plane for the Smith chart are employed.
This approach is useful when we need to take into account the final transducer power gain GT and the noise figure of the amplifier.
Extra
Notes: <number>

## Slide 42: Constant Available Power Gain Circles
From the Dependency Diagram of the previous chapter, we see that GA only depends on s. Indeed it is possible to determine the range of s which would give a fixed GA, and this range actually falls on the locus of a circle on the Smith chart.
The derivation is similar to the procedures in Appendix 1.
(3.1a)
(3.1b)
(3.1c)
(3.1d)
Center
of circle
Radius
of circle
Normalized GA
Extra
Notes: <number>

## Slide 43: Constant Available Power Gain Circles (cont’d)
Im
Re
s Plane
TGA
RGA
Constant
GA circle
Zs which falls on this circle will give a similar GA when connected to the amplifier output
0
Extra
Notes: <number>

## Slide 44: The Constant GA Circle Approach
Use the constant GA circles together with the SSC (if the amplifier is conditionally stable) to select the appropriate s.
From the selected s, determine 2.
Conjugate match the output port (make sure that L is in the stable region).
GT = GA.
Extra
PAo
PL = PAo
Pro = 0
PAs
PRs
Pin
PL
Amplifier
S
1
2
2*
Vs
Zs
Output
Transformation
Network
ZL
Input
Transformation
Network
Notes: <number>

## Slide 45: References
[1]* D.M. Pozar, “Microwave Engineering”, 3rd Edition, 2005 John-Wiley & Sons.
[2] R.E. Collin, “Foundations for Microwave Engineering”, 2nd Edition, 1992 McGraw-Hill.
[3] R. Ludwig, P. Bretchko, “RF Circuit Design – Theory and Applications”, 2000 Prentice-Hall.
[4]* G. Gonzalez, “Microwave Transistor Amplifiers – Analysis and Design”, 2nd Edition 1997, Prentice-Hall.
[5] Gilmore R., Besser L., “Practical RF Circuit Design for Modern Wireless Systems”, Vol. 1 and 2, 2003, Artech House.
Notes: <number>