## Slide 1: ME1000 RF CIRCUIT DESIGN
<number>
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 8E. Multistage Small-Signal Amplifier (SSA) Design
Notes: <number>

## Slide 3: 1.0 Multistage Amplifier
Notes: <number>

## Slide 4: Introduction
The amplifiers discussed in the precedent parts are all single-stage amplifiers
This is because each amplifier only contains a single active amplification component
Typically, the number of stages of an amplifier corresponds to the number of amplification components connected in a cascaded order
An amplifier with multiple active devices connected in cascade is called a multistage amplifier
A multistage amplifier is usually used when a higher gain is needed and a single active device is insufficient to provide the necessary power gain
Notes: <number>

## Slide 5: Typical Block Diagram of a Multistage Amplifier System
An example of a two-stage amplifier is shown below:
Amplifier
1
Input
Matching
Network
Vs
Zs
ZL
Output
Matching
Network
Amplifier
2
Inter-stage
Matching
Network (IMN)
DC Supply
Z1L
Z2s
Z11
Z12
Z21
Z22
Z2L
Z1s
1s
11
12
1L
2s
21
22
2L
or
Notes: <number>

## Slide 6: 2.0 Multistage Amplifier Design Strategy
Notes: <number>

## Slide 7: Power Flow Diagram of Multistage Amplifier
Consider a two-stage amplifier with lossless inter-stage matching network (IMN):
Amplifier
1
Input
Matching
Network
Vs
Zs
ZL
Output
Matching
Network
Amplifier
2
Inter-stage
Matching
Network
Incident power or available power
Reflected power
Absorbed power
Lossless
=
PA1
Pin1
PAo1
PL1
PA2
PAo2
PL2
PL2
The total transducer power gain is:
(2.1)
PL1 = PA2
Notes: <number>

## Slide 8: Design Strategy
By introducing an intermediate impedance, say Zo, we can split the inter-stage matching network into two blocks
This effectively splits the multistage amplifier into several individual single-stage amplifiers
Amplifier
1
Amplifier
2
Inter-stage
Matching
Network
Output Matching Network for Stage 1
Zo
Input Matching Network for Stage 2
Zo
+
-
Notes: <number>

## Slide 9: Design Strategy (cont’d)
Thus based on (2.1) and the fact that the inter-stage matching network can be decomposed into individual blocks, the design of a multistage amplifier proceeds by designing individual single-stage amplifiers fulfilling certain performance specifications, then combining these single-stages amplifiers to form a multistage amplifier
Notes: <number>

## Slide 10: Design Strategy (cont’d)
In a two-stage amplifier design, we also design for high overall gain, low-noise, or high output power.
Amplifier Types | Required 1s | Required 1L | Required 2s | Required 2L | Graphical tools
Maximum GT(max) |  |  |  |  | None
Lowest noise |  |  |  |  | Constant F circle
Maximum Output Power |  |  |  |  | Constant PL contour
Discussed
in High Power
Circuits
Notes: <number>

## Slide 11: 3.0 Two-Stage Small-Signal Amplifier Design Example
Notes: <number>

## Slide 12: Example 3.1
Let us use an example to illustrate the strategy of a multistage small-signal amplifier design
Here we would design a two-stage transistor amplifier with the following specifications:
  Power supply voltage: 2.8 to 3.2 V
  DC current dissipation: 15 mA or less
  Operating frequency range: 870 MHz  30 MHz
  Overall transducer power gain: 20 – 30 dB
  Overall Noise Figure: 3 dB or smaller
  Source and load impedances: 50 Ω
  Active components: BFR92A, RF NPN transistor
Notes: <number>

## Slide 13: Example 3.1 (cont’d)
Based on our experience with using the BFR92A at 3.0 V, IC = 5.0 mA, we know that this particular RF NPN transistor can provide at least 10 dB GT with noise figure < 2 dB between 800 to 920 MHz
Thus, it is possible to divide this two-stage amplifier into two single-stage amplifiers, each fulfilling:
IC = 6.0 mA or less
GT = 10 dB or higher
F = 2.0 dB or less
Example:
We could use Gp1_dB = 11 dB, M1_dB = –1 dB;
or Gp1 = 12.6, M = 0.89.
1.6 or less
Notes: <number>

## Slide 14: Example 3.1 (cont’d)
Stage 1 design, centered at 870 MHz:
Vs
Zo
Amplifier
1
Input
Transformation
Network 1
Output
Transformation
Network 1
Zo
S
1
2
L
s is chosen such that M1 is close to 1 and F1 = 1.6 or less
L is chosen to provide the power gain GT of 10 dB or more
Notes: <number>

## Slide 15: Example 3.1 (cont’d)
Stage 2 design, centered at 870 MHz:
s is chosen such that M2 is also close to 1 and F2 = 1.6 or less.
L is chosen to provide the power gain GT of 10 dB or more
Vs
Zo
Amplifier
2
Input
Transformation
Network 2
Output
Transformation
Network 2
Zo
S
1
2
L
Notes: <number>

## Slide 16: Example 3.1 (cont’d)
When both Stage 1 and Stage 2 are combined together, the overall transducer power gain is:
The overall noise figure is:
or
Notes: <number>

## Slide 17: Example 3.1 Schematic Realization: Single-Stage DC Design
We begin by designing a single-stage RF amplifier
The transistor is BFR92A
Firstly, a simple DC biasing circuit is designed as follows; this would provide IC around 5.0 mA and VC around 2.0 V, with 1 V for the ac signal swing
Notes: <number>

## Slide 18: Example 3.1 Schematic Realization: Single-Stage AC Design
Next, we modify the DC circuit to include the RF chokes and coupling capacitors
We then perform an AC analysis and compute the S-parameters and related noise parameters
Notes: <number>

## Slide 19: Example 3.1 Schematic Realization: Single-Stage AC Design (cont’d)
We observe that this circuit becomes marginally stable below 550 MHz, otherwise it is unconditionally stable up to 1500 MHz
Furthermore, a power gain of up to 30 dB is achievable at 870 MHz
The noise figure at 870 MHz is around 1.1 dB, with the optimum source impedance shown Zsm = 31.25 + j12.80
Notes: <number>

## Slide 20: Example 3.1 Schematic Realization: Single-Stage AC Design (cont’d)
Now we fix the analysis at 870 MHz
We also add built-in functions to calculate the optimum source impedance for low-noise, and the source and load impedances for the simultaneous conjugate match
Notes: <number>

## Slide 21: Example 3.1 Schematic Realization: Single-Stage AC Design (cont’d)
In the Smith chart for Zs, we plot the three constant noise figure circles and Zsscm (the simultaneous conjugate match Zs)
We see that choosing Zsscm will give a noise figure of less than 1.4 dB (Nfmin + 0.4), which is reasonable
Thus, it is more sensible to design a single-stage unconditionally stable amplifier
Nfmin+0.1
Nfmin+0.2
Nfmin+0.4
Zsscm
s Plane
Notes: <number>

## Slide 22: Example 3.1 Schematic Realization: Single-Stage AC Design (cont’d)
Finally, we include the source and load impedance transformation networks
Note that the inductor and capacitor values are approximated to the nearest ‘standard’ values
Also note that Rm1 is included to improve the stability of the amplifier at a low frequency. From the result in the next slide, we observe that the amplifier is indeed stable down to 100 MHz. This will degrade the noise figure somewhat.
To increase loss
at low frequency
Notes: <number>

## Slide 23: Example 3.1 Schematic Realization: Single-Stage AC Design (cont’d)
From the AC simulation results, the noise figure (NF) do indeed degraded at 870 MHz; however it is around 1.7 dB, which is still acceptable for one stage
Converting NF in dB to F:
The transducer power gain GT is 12.0 dB or 15.85
Since the source and load impedances are now 50 , we can cascade two similar amplifier together to get a total GT of 24.0 dB
We will proceed in this manner and check if the noise figure and GT are fulfilled
Notes: <number>

## Slide 24: Example 3.1 Schematic Realization: Two-Stage AC Design
If we assume the mismatch factor for each intersection to be approximately 1 (since both stages are more or less simultaneously conjugate matched), the estimated overall noise figure is:
This will be verified in the next few slides
Notes: <number>

## Slide 25: Example 3.1 Schematic Realization: Two-Stage AC Design (cont’d)
The overall two-stage amplifier
Notes: <number>

## Slide 26: Example 3.1 Schematic Realization: Two-Stage AC Design (cont’d)
As can be seen from the S-parameters simulation, the GT, NF are 24.7 dB and 1.78 dB respectively
Also this two-stage amplifier is unconditionally stable from 100 MHz and beyond
Notes: <number>

## Slide 27: Example 3.1 Schematic Realization: Two-Stage AC Design (cont’d)
Finally we examine the input and output matchs of this two-stage amplifier
The |s11| and |s22| plots are reasonable enough in the vicinity of 870 MHz (less than –15 dB). In terms of VSWR, input VSWR is around 1.24 and output VSWR is around 1.39 at 870 MHz.
Notes: <number>

## Slide 28: End Note for Example 3.1
This is just a simple example, which we did not consider a large-signal effect like gain compression
In most cases, both stages in a two-stage amplifier are designed differently. Typically, the first stage has a smaller P1dB (output 1 dB compression power), while the second stage has a larger P1dB (this usually entails a higher supply voltage and larger DC collector current, IC).
In that way, in addition to higher overall power gain, we can also obtain larger output power
Notes: <number>