## Slide 1: ME1000 RF CIRCUIT DESIGN
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.
Notes: <number>

## Slide 2: 8C. Small-Signal Amplifier (SSA) Design — Constant Mismatch and Effective Power Gain
Notes: <number>

## Slide 3: 1.0 Impedance Mismatch Factor
Notes: <number>

## Slide 4: Impedance Mismatch Factor
The concept of the Available Power PA
From the theory of maximum power transfer, when R1 = Rs, X1 = –Xs (or Z1 = Zs*), maximum power is transferred from the source to the amplifier. This power is PA, the available power from the source.
(1.1)
(1.2)
Amplifier
ZL
Zs
I1
Vs
Pin
Z1
Notes: <number>

## Slide 5: Impedance Mismatch Factor (cont’d)
When Z1  Zs*, we have an impedance mismatch and Pin < PA. The input power can be written as:
M is known as the Impedance Mismatch Factor (IMF)
The input power to an amplifier (or any linear network) is the product of IMF and the available power
PA
(1.4)
(1.3)
Notes: <number>

## Slide 6: Invariant Property of Impedance Mismatch Factor
When a lossless network is inserted between the source and Port 1, the Thevenin equivalent network can be used to find M at both ends of the network
ZT
Vs
Z1
Amplifier
ZL
Zs
Z1’
Vs
Input
Matching
Network
Z1
ZT
Notes: <number>

## Slide 7: Invariant Property of Impedance Mismatch Factor (cont’d)
We can represent the lossless network using the Z-parameters. And using circuit analysis shows that M = M’.
Use to show that
Z11 – Z12
Z22 – Z12
Z12
Input
Matching
Network
Notes: <number>

## Slide 8: Impedance Mismatch Factor Summary
In general, when there are N lossless networks connected in cascade:
Zs
Vs
Network 1
Amplifier
ZL
Network 2
M1
M2
M3
Pin
Pin
Pin
PA
M1 = M2 = M3
(1.5)
Notes: <number>

## Slide 9: Relationship Between M and the Input VSWR
Usually, the matching between two networks is specified by the VSWR
ZL
Amplifier
Zo
Vs
Lossless
Impedance
Transformation
Network
Z1
Zs
Z1’
Zo
Tline
(1.6)
Notes: <number>

## Slide 10: Input Mismatch and Transducer Power Gain
A VSWR1 near unity ensures that most of the power from the source is absorbed by the amplifier. It is equivalent to requiring M1 = 1. A VSWR1 that is greater than unity (or M < 1) is termed the input mismatch.
As we have seen in Chapter 7, the actual power gain experienced by a system is PL/PA, which is the Transducer Power Gain, GT
From which we can conclude that:
Gp
(1.7a)
(1.7b)
Notes: <number>

## Slide 11: Input Mismatch and Transducer Power Gain (cont’d)
Zs
ZL
Amplifier
with large
GP
An amplifier with a high Gp but a bad input matching (VSWRin >> 1), low GT
Zs
ZL
Amplifier
with large
Gp
An amplifier with a high Gp and a good input matching (VSWRin  1), high GT
Bottom line: A proper small-signal amplifier design needs to have a high GP and a good input matching VSWRin close to 1
Notes: <number>

## Slide 12: Input Mismatch and Transducer Power Gain (cont’d)
In general, we could not set M1 = 1 due to conflicting requirements; for instance, factors such as stability, low-noise competes with a good matching requirement. A small amount of input mismatch must be tolerated.
To control the amount of input mismatch, Constant Input Mismatch Circles are plotted after the power gain is determined
To maintain a certain effective power gain, we usually specify the maximum VSWR1. This can be converted to M1.
An amplifier can have a high power gain GP, but if the input mismatch factor M1 is small, only a small amount of power from the source network is absorbed by the input (Pin). It is this power which is amplified and presented at the output of the amplifier.
Notes: <number>

## Slide 13: Constant Input Mismatch Circles
Complex plane for s
Fixed
Notes: <number>

## Slide 14: Constant Input Mismatch Circles (cont’d)
The radius and center of the input mismatch circle for a particular L and M1 is given by:
This circle is also known as the constant input VSWR circle in other literatures
(1.8a)
(1.8b)
(1.8c)
Notes: <number>

## Slide 15: 2.0 Design for a Fixed GT and Input Mismatch
Notes: <number>

## Slide 16: Design for a Specific Transducer Power Gain GT
Usually we start by plotting the constant power gain circles and fixing M1 (this would fix the GT). The constant GP circles determine the load impedance required.
Once L is determined, 1 is calculated and we could find the corresponding s that would give the required M1. These values of s would form a circle, known as the Constant Input Mismatch Circle on the Smith chart.
The approach shown here complements the constants GP and GA approaches in Chapter 8A
M1
s
L
1
GP
GT
We set the
effective gain
GT
Notes: <number>

## Slide 17: Example 2.1
A FET amplifier has the following parameters: s11 = 0.8 < –140°, s12 = 0.2 <30°, s21 = 2.8 < 60°, s22 = 0.2 < 150° at 1.5 GHz. We would like to use this FET amplifier with GP = 10.79 dB. Assuming we can tolerate an input mismatch of VSWRin = 1.6, find a suitable load and source reflection coefficients. Also work out the effective power gain of the amplifier.
Solution:
From the S-parameter, the maximum stable gain GMS = |s21/s12| = 14
Hence, GP = 10.79 dB or 12 is within this limit
K = 0.561 < 1, hence the amplifier is conditionally stable
Notes: <number>

## Slide 18: Example 2.1 (cont’d)
SSC
LSC
Stable region for s
Stable region for L
s Plane
L Plane
Notes: <number>

## Slide 19: Example 2.1 (cont’d)
From GP = 12, we plot the constant power gain circle and determine a suitable load reflection coefficient L
For L = 0.54 < –1.48 Rad:
L = 0.28 < –0.94rad
This point is chosen as it is sufficiently far away from the LSC and not too close to the border of the Smith chart
LSC
Gp = 12 Circle
L Plane
Notes: <number>

## Slide 20: Example 2.1 (cont’d)
For VSWR1 = 1.6
Notes: <number>

## Slide 21: Example 2.1 (cont’d)
s = 0.48 < 2.48 rad
s Plane
IMC
SSC
This point is chosen as it is farthest away from the SSC
Notes: <number>

## Slide 22: Example 2.1 (cont’d)
Computing the source and load impedances:
Notes: <number>

## Slide 23: Example 2.1 (cont’d)
The final block diagram:
GP = PL/Pin = 12
FET
Amplifier
61.71
–j30.79
Zs = 19.24 + j14.81
PL
Worst case GT or Effective power gain = M1GP = 12  0.947 = 11.364
What is the best
case GT ?
Zo
Pin
Lossless
ITN
Pin
VSWR1 = 1.6
Notes: <number>

## Slide 24: References
[1]* D.M. Pozar, “Microwave Engineering”, 3rd Edition, 2005 John-Wiley & Sons.
[2] R.E. Collin, “Foundations for Microwave Engineering”, 2nd Edition, 1992 McGraw-Hill.
[3] R. Ludwig, P. Bretchko, “RF Circuit Design: Theory and Applications”, 2000 Prentice-Hall.
[4]* G. Gonzalez, “Microwave Transistor Amplifiers: Analysis and Design”, 2nd Edition 1997, Prentice-Hall.
[5] Gilmore R., Besser L., “Practical RF Circuit Design for Modern Wireless Systems”, Vol. 1 & 2, 2003, Artech House.
Notes: <number>