## Slide 1: ME1000 RF CIRCUIT DESIGN
<number>
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.
http://dreamcatcher.asia/cw

## Slide 2: 3B. RF Microwave Filters

## Slide 3: 1.0 Basic Filter Theory

## Slide 4: Introduction
An ideal filter is a linear 2-port network that provides perfect transmission of signal for frequencies in a certain passband region, infinite attenuation for frequencies in the stopband region, and a linear phase response in the passband (to reduce signal distortion).
The goal of filter design is to approximate the ideal requirements within acceptable tolerance with circuits or systems consisting of real components.

## Slide 5: Categorization of Filters
Low pass filter (LPF), high pass filter (HPF), bandpass filter (BPF), bandstop filter (BSF), arbitrary type, etc.
In each category, the filter can be further divided into active and passive types.
In an active filter, there can be amplification of the signal power in the passband region; a passive filter do not provide power amplification in the passband.
Filters used in electronics can be constructed from resistors, inductors, capacitors, transmission line sections, and resonating structures (e.g., piezoelectric crystal, Surface Acoustic Wave (SAW) devices, mechanical resonators, etc.).
An active filter may contain a transistor, FET, and an op-amp.
Filter
LPF
BPF
HPF
Active
Passive
Active
Passive

## Slide 6: Filter Frequency Response
Frequency response implies the behavior of the filter with respect to steady-state sinusoidal excitation (e.g., energizing the filter with a sine voltage or current source and observing its output).
There are various approaches to displaying the frequency response:
  Transfer function H() (the traditional approach)
  Attenuation factor A()
  S-parameters, e.g., s21()
  Others, such as ABCD parameters, etc.

## Slide 7: Filter Frequency Response (cont’d)
Low pass filter (passive)
Filter
H()
V1()
V2()
ZL
c
A()/dB

0
c
3
10
20
30
40
50
(1.1b)
(1.1a)
c
|H()|

1
Transfer function
Arg(H())

Complex value
Real value

## Slide 8: Filter Frequency Response (cont’d)
Low pass filter (passive) continued...
For the impedance matched system, using s21 to observe the filter response is more convenient, as this can be easily measured using a vector network analyzer (VNA).
Zc
Zc
Zc
Transmission line
is optional
c
20log|s21()|

0 dB
Arg(s21())

Filter
Zc
Zc
Zc
Vs
a1
b2
Complex value

## Slide 9: Filter Frequency Response (cont’d)
Low pass filter (passive) continued...
A()/dB

0
c
3
10
20
30
40
50
Filter
H()
V1()
V2()
ZL
Passband
Stopband
Transition band
Cut-off frequency (3 dB)

## Slide 10: Filter Frequency Response (cont’d)
High pass filter (passive)
A()/dB

0
c
3
10
20
30
40
50
c
|H()|

1
Transfer function
Stopband
Passband

## Slide 11: Filter Frequency Response (cont’d)
Bandpass filter (passive) Bandstop filter

A()/dB
40
1
3
30
20
10
0
2
o
1
|H()|

1
Transfer function
2
o

A()/dB
40
1
3
30
20
10
0
2
o
1
|H()|

1
Transfer function
2
o

## Slide 12: Basic Filter Synthesis Approaches
Image Parameter Method.
Zo
Zo
Zo
Zo
Zo
Filter
Zo
H1()
H2()
Hn()
Zo
Zo
Consider a filter to be a
cascade of linear 2-port
networks.
Synthesize or realize each
2-port network, so that
the combine effect gives the
required frequency response.
The ‘image’ impedance seen
at the input and output of
each network is maintained.

The combined
response
Response of
a single
network


## Slide 13: Basic Filter Synthesis Approaches (cont’d)
Insertion Loss Method.
Filter
Zo
Zo
Use the RCLM circuit synthesis theorem to come up with a resistive terminated
LC network that can produce the
approximate response.
Zo

Ideal
Approximate with rational polynomial
function
|H()|
We can also use Attenuation Factor or |s21| for this.
Approximate ideal filter response
with polynomial function:

## Slide 14: Our Scope
Only concentrate on passive LC and stripline filters.
Filter synthesis using the Insertion Loss Method (ILM). The Image Parameter Method (IPM) is more efficient and suitable for simple filter designs, but has the disadvantage that arbitrary frequency response cannot be incorporated into the design.

## Slide 15: 2.0 Passive LC Filter Synthesis Using the Insertion Loss Method

## Slide 16: Insertion Loss Method (ILM)
The insertion loss method (ILM) enables a systematic way to design and synthesize a filter with various frequency responses.
The ILM method also enables a filter performance to be improved in a straightforward manner, at the expense of a ‘higher order’ filter.
A rational polynomial function is used to approximate the ideal |H()|, A(), or |s21()|.
Phase information is totally ignored.
Ignoring phase simplifies the actual synthesis method. An LC network is then derived which will produce this approximated response.
The attenuation A() can be cast into power attenuation ratio, called the Power Loss Ratio, PLR, which is related to A()2.

## Slide 17: More on ILM
There is a historical reason why phase information is ignored. Original filter synthesis methods are developed in the 1920s–60s, for voice communication. The human ear is insensitive to phase distortion, thus only the magnitude response (e.g., |H()|, A()) is considered.
Modern filter synthesis can optimize a circuit to meet both magnitude and phase requirements. This is usually done using computer optimization procedures with ‘goal functions’.
Extra

## Slide 18: Power Loss Ratio (PLR)
PLR large, high attenuation
PLR close to 1, low attenuation
For example, a low pass
filter response is shown
below:
ZL
Vs
Lossless
2-port network
1
Zs
PA
Pin
PL
PLR(f)
Low pass filter PLR
f
1
0
Low
attenuation
High
attenuation
fc
(2.1a)

## Slide 19: PLR and s21
In terms of incident and reflected waves, assuming ZL = Zs = ZC.
Zc
Vs
Lossless
2-port network
Zc
PA
Pin
PL
a1
b1
b2
(2.1b)

## Slide 20: PLR for the Low Pass Filter (LPF)
Since |1()|2 is an even function of , it can be written in terms of 2 as:
PLR can be expressed as:
Various types of polynomial function in  can be used for P(). The requirement is that P() must either be an odd or even function. Among the classical polynomial functions are:
  Maximally flat or Butterworth functions
  Equal ripple or Chebyshev functions
  Elliptic function
  Many, many more
(2.2)
(2.3a)
(2.3b)
This is also known
as Characteristic Polynomial
The characteristics we need
from [P()]2 for LPF:
[P()]2  0 for  < c
[P()]2 >> 1 for  >> c

## Slide 21: Characteristic Polynomial Functions
Maximally flat or Butterworth:
Equal ripple or Chebyshev:
Bessel or linear phase:
N = order of the
Characteristic
Polynomial P()
(2.4a)
(2.4b)
(2.4c)

## Slide 22: Examples of PLR for the Low Pass Filter
PLR of the low pass filter using 4th order polynomial functions (N = 4) – Butterworth, Chebyshev (ripple factor =1), and Bessel. Normalized to c = 1 rad/s, k = 1.
Butterworth
Chebyshev
Bessel
PLR
Ideal
If we convert into dB,
this ripple is equal to
3 dB
k=1

## Slide 23: Examples of PLR for the Low Pass Filter (cont’d)
PLR of the low pass filter using the Butterworth characteristic polynomial, normalized to c = 1 rad/s, k = 1.
N=2
N=6
N=4
N=5
N=3
N=7
Conclusion:
The type of
polynomial
function and
the order
determine the
attenuation rate
in the stopband.

## Slide 24: Characteristics of Low Pass Filters Using Various Polynomial Functions
Butterworth: Moderately linear phase response, slow cutoff, smooth attenuation in the passband.
Chebyshev: Bad phase response, rapid cutoff for a similar order, contains ripple in the passband. May have impedance mismatch for N even.
Bessel: Good phase response, linear. Very slow cutoff. Smooth amplitude response in the passband.

## Slide 25: Low Pass Prototype Design
A lossless linear, passive, reciprocal network that can produce the insertion loss profile for the low pass filter is the LC ladder network.
Many researchers have tabulated the values for the L and C for the low pass filter with cut-off frequency c = 1 rad/s, that works with the source and load impedance Zs = ZL = 1 .
This low pass filter is known as the Low Pass Prototype (LPP).
As the order N of the polynomial P increases, the required element also increases. The no. of elements = N.
L1=g2
L2=g4
C1=g1
C2=g3
RL= gN+1
1
L1=g1
L2=g3
C1=g2
C2=g4
RL= gN+1
g0= 1
Dual of each
other

## Slide 26: Low Pass Prototype Design (cont’d)
The LPP is the ‘building block’ from which real filters may be constructed.
Various transformations may be used to convert it into a high pass, bandpass, or other filter of arbitrary center frequency and bandwidth.
The following slides show some sample tables for designing LPP for Butterworth and Chebyshev amplitude response of PLR.

## Slide 27: Table for the Butterworth LPP Design
See Example 2.1 in the following slides on how the constant values g1, g2, g3, … etc., are obtained.

## Slide 28: Table for the Chebyshev LPP Design
Ripple factor 20log10 = 0.5 dB
Ripple factor 20log10 = 3.0 dB

## Slide 29: Table for the Maximally-Flat Time Delay LPP Design

## Slide 30: Example 2.1: Finding the Constants for the LPP Design
and
Thus
Therefore we can compute the power loss ratio as:
[P()]2
R
R
Vs
C
L
R
jL
R
Vs
1/jC
V1
Consider a simple case of a 2nd order low pass filter:
Extra

## Slide 31: Example 2.1: Finding the Constants for the LPP Design (cont’d)
Extra
PLR can be written in terms of polynomial of 2:
For Butterworth response with k = 1, c = 1:
(E1.1)
(E1.2)
Comparing equations (E1.1) and (E1.2):
Setting R = 1 for the Low Pass Prototype (LPP):
(E1.3)
(E1.4)
Thus from equation (E1.4):
Using (E1.3)
Compare this result with
N=2 in the table for the LPP Butterworth response.
This direct ‘brute force’
approach can be
extended to N=3, 4, 5…

## Slide 32: Example 2.1: Verification
Extra

## Slide 33: Example 2.1: Verification (cont’d)
Extra
–3 dB at 160 mHz (milliHertz!!),
which is equivalent to 1 rad/s
Power loss ratio
versus frequency

## Slide 34: Impedance Denormalization and Frequency Transformation of LPP
Once the LPP filter is designed, the cut-off frequency c can be transformed to other frequencies.
Furthermore the LPP can be mapped to other filter types such as high pass, bandpass, and bandstop.
This frequency scaling and transformation entails changing the value and configuration of the elements of the LPP.
Finally the impedance presented by the filter at the operating frequency can also be scaled, from unity to other values; this is called impedance denormalization.
Let Zo be the new system impedance value. The following slide summarizes the various transformation from the LPP filter.

## Slide 35: Impedance Denormalization and Frequency Transformation of LPP (cont’d)
LPP to
Low Pass
LPP to
High Pass
LPP to
Bandpass
LPP to
Bandstop
Note that the inductor always multiplies with Zo while the capacitor divides with Zo
(2.5a)
(2.5b)
L
C
Center frequency
Fractional bandwidth

## Slide 36: Summary of Passive LC Filter Design Flow Using the ILM Method
Step 1: From the requirements, determine the order and type of approximation functions to use.
  Insertion loss (dB) in the passband ?
  Attenuation (dB) in the stopband ?
  Cut-off rate (dB/decade) in the transition band ?
  Tolerable ripple?
  Linearity of phase?
Step 2: Design a normalized low pass prototype (LPP) using the L and C elements.
L1=g2
L2=g4
C1=g1
C2=g3
RL= gN+1
1
|H()|

0
1
1

## Slide 37: Summary of Passive Filter Design Flow Using the ILM Method (cont’d)
Step 3: Perform frequency scaling, and denormalize the impedance.
Step 4: Choose suitable lumped components, or transform the lumped circuit design into distributed realization.
|H()|

0
1
1
2
50
Vs
15.916pF
0.1414pF
79.58nH
0.7072nH
0.7072nH
15.916pF
50
RL
All uses the microstrip stripline circuit

## Slide 38: Filter vs. Impedance Transformation Network
If we ponder carefully, the sharp observer will notice that the filter can be considered as a class of impedance transformation network.
In the passband, the load is matched to the source network, much like a filter.
In the stopband, the load impedance is highly mismatched from the source impedance.
However, the procedure described here only applies to the case when both load and source impedance are equal and real.
Extra

## Slide 39: Example 2.2A: LPF Design – Butterworth Response
Design a 4th order Butterworth low pass filter, Rs = RL= 50 , fc = 1.5 GHz.
L1=0.7654H
L2=1.8478H
C1=1.8478F
C2=0.7654F
RL= 1 
g0= 1
L1=4.061 nH
L2=9.803 nH
C1=3.921 pF
C2=1.624 pF
RL= 50 
g0=1/50
Steps 1 & 2: LPP
Step 3: Frequency scaling
and impedance denormalization

## Slide 40: Example 2.2B: LPF Design – Chebyshev Response
Design a 4th order Chebyshev low pass filter, 0.5 dB ripple factor, Rs = 50 , fc = 1.5 GHz.
L1=1.6703H
L2=2.3661H
C1=1.1926F
C2=0.8419F
RL= 1.9841 
g0= 1
L1=8.861 nH
L2=12.55 nH
C1=2.531 pF
C2=1.787 pF
RL= 99.2 
g0=1/50
Steps 1 & 2: LPP
Step 3: Frequency scaling
and impedance denormalization

## Slide 41: Example 2.2 (cont’d)
Chebyshev
Butterworth
|s21|
Ripple is roughly
0.5 dB
Arg(s21)
Chebyshev
Butterworth
Better phase
linearity for Butterworth
LPF in the passband
Computer simulation result
using AC analysis (ADS2003C)
Note: Equation used in Data Display of ADS2003C
to obtain a continuous phase display with the built-in
function phase( ).

## Slide 42: Example 2.3: BPF Design
Design a bandpass filter with Butterworth (maximally flat) response.
N = 3
Center frequency fo = 1.5 GHz
3 dB Bandwidth = 200 MHz or f1 = 1.4 GHz, f2 = 1.6 GHz
Impedance = 50 Ω

## Slide 43: Example 2.3 (cont’d)
From table, design the low pass prototype (LPP) for 3rd order Butterworth response, c = 1.
Zo=1
g1
1.000F
g3
1.000F
g2
2.000H
g4
1
2<0o
Simulated result
using PSpice
Voltage across g4
Steps 1 & 2: LPP

## Slide 44: Example 2.3 (cont’d)
LPP to bandpass transformation
Impedance denormalization
50 
Vs
15.916 pF
0.1414 pF
79.58 nH
0.7072 nH
0.7072 nH
15.916 pF
50 
RL
Step 3: Frequency scaling
and impedance denormalization

## Slide 45: Example 2.3 (cont’d)
Simulated result using PSpice:
Voltage across RL

## Slide 46: All Pass Filter
There is also another class of filter known as the All Pass Filter (APF).
This type of filter does not produce any attenuation in the magnitude response, but provides phase response in the band of interest.
APF is often used in conjunction with LPF, BPF, HPF, etc., to compensate for phase distortion.
Extra
Zo
BPF
APF
f
0
|H(f)|
1
f
Arg(H(f))
Example of the APF response
f
|H(f)|
1
0
f
Arg(H(f))
f
0
|H(f)|
1
f
Arg(H(f))
Linear
phase in
passband
Nonlinear
phase in
passband

## Slide 47: Example 2.4: Practical RF BPF Design Using SMD Discrete Components

## Slide 48: Example 2.4 (cont’d)
BPF synthesis
using synthesis
tool E-syn
of ADS2003C

## Slide 49: Example 2.4 (cont’d)
|s21|/dB
Arg(s21)/degree
Measured
Simulated
Measurement is performed with the
Agilent 8753ES Vector Network
Analyzer, using Full OSL calibration

## Slide 50: 3.0 Microwave Filter Realization Using Stripline Structures

## Slide 51: 3.1 Basic Approach

## Slide 52: Filter Realization Using Distributed Circuit Elements
Lumped-element filter realization using surface mounted inductors and capacitors generally works well at lower frequencies (at UHF, say < 3 GHz).
At higher frequencies, the practical inductors and capacitors loses their intrinsic characteristics.
Also, a limited range of component values is available from the manufacturer.
Therefore, for microwave frequencies (> 3 GHz), the passive filter is usually realized using distributed circuit elements such as transmission line sections.
Here we will focus on stripline microwave circuits.

## Slide 53: Filter Realization Using Distributed Circuit Elements (cont’d)
Recall in the study of Terminated Transmission Line Circuit that a length of terminated Tline can be used to approximate an inductor and a capacitor.
This concept forms the basis of transforming the LC passive filter into distributed circuit elements.
Zo
Zo
Zc , 
l
L

Zc , 
l
C

Zc , 
Zc , 
Zc , 
Zo
Zo


## Slide 54: Filter Realization Using Distributed Circuit Elements (cont’d)
This approach is only an approximation. There will be deviation between the actual LC filter response and those implemented with terminated Tline.
Also, the frequency response of the distributed circuit filter is periodic.
Other issues are shown below.
Zc , 
Zc , 
Zc , 
Zo
Zo
How do we implement a series Tline
connection? (only practical for
certain Tline configuration)
Connection of physical
length cannot be
ignored at the
microwave region,
comparable to 
Thus some theorems are used to
facilitate the transformation of the LC
circuit into stripline microwave circuits.
Chief among these are the Kuroda’s
Identities (See Appendix 1)

## Slide 55: More on Approximating L and C with Terminated Tline: Richard’s Transformation
Zc , 
l
L

Zin
(3.1.1a)
Zc , 
l
C

Zin
(3.1.1b)
For LPP design, a further requirement is
that:
(3.1.1c)
Wavelength at
cut-off frequency
Here, instead of fixing Zc and tuning l to approach an L or C,
we allow Zc to be a variable too.

## Slide 56: Example 3.1: LPF Design Using Stripline
Design a 3rd order Butterworth low pass filter, Rs = RL= 50 , fc = 1.5 GHz.
Steps 1 & 2: LPP
Step 3: Convert to Tlines
Zc=0.500
Zc=1.000
1 
Zc=1.000
1 
Zo=1 
g1
1.000H
g3
1.000H
g2
2.000F
g4
1
Length = c/8
for all Tlines
at  = 1 rad/s

## Slide 57: Example 3.1 (cont’d)
Length = c/8
for all Tlines
at  = 1 rad/s
Step 4: Add an extra Tline on the series
connection and apply Kuroda’s
2nd Identity.
Zc=0.500
Zc=1.000
1 
Zc=1.000
1 
Zc=1.0
Zc=1.0
Extra Tline
Extra Tline
n2Z1=2
l

Z2=1

Similar operation is
performed here
Yc

## Slide 58: Example 3.1 (cont’d)
Zc=0.500
1 
1 
Zc=2.0
Zc=2.0
Zc=2.000
Zc=2.000
After applying Kuroda’s 2nd Identity
Length = c/8
for all Tlines
at  = 1 rad/s
Since all Tlines have similar physical
length, this approach to stripline filter
implementation is also known as
Commensurate Line Approach.

## Slide 59: Example 3.1 (cont’d)
Zc=25
50 
50 
Zc=100
Zc=100
Zc=100
Zc=100
Length = c/8
for all Tlines at
f = fc = 1.5 GHz
Zc/Ω /8 @ 1.5 GHz/mm W/mm
50 13.45 2.85
25 12.77 8.00
100 14.23 0.61
Microstrip line using double-sided FR4 PCB (r = 4.6, H=1.57 mm)
Step 5: Impedance and frequency denormalization
Here we multiply all
impedance with Zo = 50
We can work out the correct width W given the
impedance, dielectric constant, and thickness.
From W/H ratio, the effective dielectric constant
eff can be determined. Use this together with
frequency at 1.5 GHz to find the wavelength.

## Slide 60: Example 3.1 (cont’d)
Step 6: The layout (top view)

## Slide 61: Example 3.1 (cont’d)
Simulated results

## Slide 62: Conclusions for Section 3.1
Further tuning is needed to optimize the frequency response.
The method illustrated is good for the low pass and bandstop filter implementation.
For high pass and bandpass, other approaches are needed.

## Slide 63: 3.2 Further Implementations

## Slide 64: Realization of LPF Using the Step-Impedance Approach
A relatively easy way to implement LPF using stripline components.
Using alternating sections of high and low characteristic impedance Tlines to approximate the alternating L and C elements in an LPF.
Performance of this approach is marginal as it is an approximation, where a sharp cutoff is not required.
As usual, beware of parasitic passbands!!!

## Slide 65: Equivalent Circuit of a Transmission Line Section
Z11 – Z12
Z11 – Z12
Z12
l
Zc

(3.2.1a)
(3.2.1b)
(3.2.1c)
Ideal lossless Tline
T-network equivalent circuit
Positive reactance
Positive
susceptance

## Slide 66: Approximation for High and Low ZC
When l < /2, the series element can be thought of as an inductor and the shunt element can be considered a capacitor.
For l < /4 and Zc = ZH >> 1:
For l < /4 and Zc = ZL  1:
jX/2
jB
jX/2
X  ZH l
B  YLl
When Zc  1
l < /4
When Zc >> 1
l < /4
Z11 - Z12
Z11 - Z12
Z12

## Slide 67: Approximation for High and Low ZC (cont’d)
Note that l < /2 implies a physically short Tline. Thus a short Tline with high Zc (e.g., ZH) approximates an inductor.
A short Tline with low Zc (e.g., ZL) approximates a capacitor.
The ratio of ZH/ZL should be as high as possible. Typical values: ZH = 100 to 150 , ZL = 10 to 15 .
(3.2.2a)
(3.2.2b)

## Slide 68: Example 3.2: Mapping an LPF Circuit into a Step Impedance Tline Network
For instance, consider the LPF Design Example 2.2A (Butterworth).
Let us use the microstrip line. Since a microstrip Tline with low Zc is wide and a Tline with high Zc is narrow, the transformation from circuit to physical layout would be as follows:
L1=4.061 nH
L2=9.803 nH
C1=3.921 pF
C2=1.624 pF
RL= 50 
g0=1/50

## Slide 69: Example 3.2: Physical Realization of LPF
Using the microstrip line, with r = 4.2, d = 1.5 mm:
L1 = 4.061 nH, L2 = 9.083 nH, C1 = 3.921 pF, C2 = 1.624 pF

## Slide 70: Example 3.2: Physical Realization of LPF (cont’d)
l
2
l
1
50

line
50

line
l
4
l
3
0.6 mm
15.0 mm
3.0 mm
To 50

Load
Verification:
Nevertheless we still
proceed with the imple-
mentation. It will be seen
that this will affect the
accuracy of the –3 dB cut-off
point of the filter.

## Slide 71: Example 3.2: Step Impedance LPF Simulation with ADS Software
Transferring the microstrip line design to ADS:
Microstrip line model
Microstrip step junction
model
Microstrip line substrate model

## Slide 72: Example 3.2: Step Impedance LPF Simulation with ADS Software (cont’d)

## Slide 73: Example 3.2: Step Impedance LPF Simulation with ADS Software (cont’d)
However if we extent the stop frequency for the S-parameter simulation to 9 GHz...
Parasitic passbands,
artifacts due to using
transmission lines

## Slide 74: Example 3.2: Verification with Measurement
The –3 dB point is around 1.417 GHz!
The actual LPF constructed in year
2000. The Agilent 8720D Vector Network Analyzer is used to perform the S-parameter measurement.

## Slide 75: Example 3.3: Realization of BPF Using a Coupled Microstrip Line
Based on the BPF design of Example 2.3:
50 
Vs
15.916 pF
0.1414 pF
79.58 nH
0.7072 nH
0.7072 nH
15.916 pF
50 
RL
J1
–90o
J2
–90o
J3
–90o
J4
–90o
Tline
Admittance
inverter
To RL
To source
network
See appendix (using Richard’s transformation
and Kuroda’s identities)
An array of coupled
microstrip line
o = wavelength at o
Section 1
Section 2
Section 3
Section 4
An equivalent circuit
model for coupled Tlines
with open circuit at
two ends.
Extra

## Slide 76: Example 3.3: Realization of BPF Using the Coupled Microstrip Line (cont’d)
Each section of the coupled stripline contains three parameters: S, W, d. These parameters can be determined from the values of the odd and even mode impedances (Zoo & Zoe) of each coupled line.
Zoo and Zoe are in turn depend on the “gain” of the corresponding admittance inverter J.
And each Jn is given by:
S
W
W
d
Extra
From Example 2.3

## Slide 77: Example 3.3: Realization of BPF Using the Coupled Microstrip Line (cont’d)
Section 1:
Section 2:
Section 3:
Section 4:
Note:
g1=1.0000
g2=2.0000
g3=1.0000
g4=1.0000
Extra

## Slide 78: Example 3.3: Realization of BPF Using the Coupled Microstrip Line (cont’d)
In this example, an edge-coupled microstrip line is used to implement the coupled transmission line structures needed in the BPF. Stripline does not suffer from dispersion and its propagation mode is pure TEM mode, however it is more difficult to implement physically due to the fact that the trace is buried within the dielectric.
Design equations for coupled microstrip line implemented are widely tabulated.
Here we will use FR4 (r = 4.6, r = 1.0) substrate with 1.0mm dielectric thickness, and 1 ounce copper (about 36m thick) copper laminate. The conductivity of copper is around 5.8107 Siemens/meter.
Furthermore we will use the LineCal tool in Advanced Design System to work out the dimensions needed for the coupled microstrip line.
Extra

## Slide 79: Example 3.3: Realization of BPF Using the Coupled Microstrip Line (cont’d)
Using the LineCal tool to work out the dimensions for sections 1 and 3.
Electrical length (l ), 90o for quarter
wavelength.
Zoe
Zoo
Zo
Voltage coupling
factor in dB
Fix the frequency at
1.5GHz, the center
of passband
Strategy:
1) We ‘tune’ the W and
S for the specified
Zoo and Zoe.
2) Then we ‘tune’ the length L
to meet the electrical length of
/2 (quarter wavelength) at
1.5GHz.
Extra

## Slide 80: Example 3.3: Realization of BPF Using the Coupled Microstrip Line (cont’d)
Using the LineCal tool to work out the dimensions for sections 2 and 4.
Extra

## Slide 81: Example 3.3: Realization of BPF Using the Coupled Microstrip Line (cont’d)
Alternatively we can implement our own design tool, as shown below implemented on Microsoft Excel.
Based on design equations from Garg R., Bahl I. J.,”Characteristics of coupled microstriplines”, IEEE
Transaction on Microwave Theory and Techniques, MTT-27, No.7, pp. 700-705,July 1979.
Strategy:
1) We ‘tune’ the W and
S for the specified Zoo and Zoe.
2) Based on the width W of
a single trace, we work out
the effective permittivity, and
use this to calculate the phase
velocity.
3) From this we find the
wavelength at 1.5GHz and
work out the required quarter
wavelength.
Extra

## Slide 82: Example 3.3: Coupled-Line BPF Simulation with ADS Software
Using ideal transmission line elements:
Ideal open circuit
Ideal coupled tline
Extra

## Slide 83: Example 3.3: Coupled-Line BPF Simulation with ADS Software (cont’d)
Parasitic passbands. Artifacts due to using distributed
elements, these are not present if lumped components
are used.
2fo
Extra

## Slide 84: Example 3.3: Coupled-Line BPF Simulation With ADS Software (cont’d)
Using a practical stripline model:
Coupled stripline model
Open circuit
model
Stripline substrate model
Extra

## Slide 85: Example 3.3: Coupled-Line BPF Simulation with ADS Software (cont’d)
Attenuation due to losses in the conductor and dielectric
Extra

## Slide 86: Example 3.4: Lumped Band-Pass Filter Implementation on PCB
In this example we wish to implement a 3rd order lumped LC Chebyshev BPF with lower and upper cut-off frequencies around 860 and 1000 MHz respectively.
We wish to highlight the effect of the PCB traces and through holes on the performance of the filter.
Here we are using double-sided copper FR4 substrate for our PCB.
FR4 substrate properties:
Thickness = 59 mils
Dielectric constant = 4.5
Loss tangent at 1000MHz = 0.01
Copper thickness: 1.4 mils (1 ounce/square feet)

## Slide 87: Example 3.4: Lumped Band-Pass Filter Implementation on PCB (cont’d)
Here we show three versions of the BPF: (1) Ideal schematic using ideal LC components and ignoring PCB interconnections (2) Practical lumped LC components and ignoring PCB interconnections (3) Practical lumped LC components with PCB interconnections.
For case (1) and (2), standard linear circuit analysis is employed.
For case (3), we employ EM (electromagnetic) and circuit co-simulation. Essentially we use Method-of-Moment (MoM) to find out the effect of electric and magnetic field interaction in the actual physical structure of the BPF. The result of MoM analysis is an admittance matrix which links the solder pads of all the LC lumped components. A circuit simulation, combining the LC components and admittance matrix is then used to find the frequency response of the system. This approach is the most accurate for high-frequency circuits.

## Slide 88: Example 3.4: Lumped Band-Pass Filter Implementation on PCB (cont’d)
Case (1) and (2): Ignoring PCB interconnections, circuit simulation results (|s21|).
Note: Here we use Agilent’s Genesys EDA tool
Ideal components
Real components
Note: All the LC components used have
self-resonance frequency > 2 GHz

## Slide 89: Example 3.4: Lumped Band-Pass Filter Implementation on PCB (cont’d)
Case (3) Practical lumped LC components with PCB interconnections.
The PCB layout of the BPF is shown below.
Port 1
Port 2
Microstrip Line
Via (Through hole
to GND plane on the
bottom side)
Internal ports for
connection to SMD
components
After discretization, with the
positioning of components shown
0.47pF
0.47pF
2.2nH
2.2nH
15nH
1.00pF

## Slide 90: Example 3.4: Lumped Band-Pass Filter Implementation on PCB (cont’d)
The Circuit-EM schematic model and circuit simulation results (|s21|).
We note that the PCB interconnections greatly change the frequency response of the filter.
Ideal components
Real components
Circuit-EM

## Slide 91: Example 3.4: Lumped Band-Pass Filter Implementation on PCB (cont’d)
Measured results are obtained from ME1000 TX Unit’s RF-BPF V1.00 using VNA with simple frequency response and port match calibration.

## Slide 92: Example 3.4: Lumped Band-Pass Filter Implementation on PCB (cont’d)
Comparison between circuit-EM co-simulated and measurement results.

## Slide 93: Items for Self-Study
Network analysis and realizability theory
Synthesis of terminated RLCM 1-port circuits
Ideal impedance and admittance inverters and practical implementation
Periodic structures theory
Filter design by the Image Parameter Method (IPM).

## Slide 94: Other Types of Stripline Filter
LPF
HPF:
SMD capacitor
BPF:
Notes: For these delightfully simple approaches, see Chapter 43 of W. Chen (Editor), “The Circuits and Filters Handbook”, 1995, CRC Press.
<number>

## Slide 95: Other Types of Stripline Filter (cont’d)
More BPFs:
BSF:

## Slide 96: Appendix 1 – Kuroda’s Identities

## Slide 97: Kuroda’s Identities
As extracted from Ref. [2]
Z1
l
Z2/n2
l
Z2
l
n2Z1
l
Z2
l
Z2/n2
l
1: n2
Z1
l
n2Z1
l
n2: 1








Note: The inductor represents the
shorted Tline while the capacitor
represents the open-circuit Tline.
Note: The
length of all
transmission
lines is
l = /8