## Slide 1: ME1000 RF CIRCUIT DESIGN
http://dreamcatcher.asia/cw
This courseware product contains scholarly and technical information and is protected by copyright laws and international treaties. No part of this publication may be reproduced by any means, be it transmitted, transcribed, photocopied, stored in a retrieval system, or translated into any language in any form, without the prior written permission of Acehub Vista Sdn. Bhd. or their respective copyright owners.
The use of the courseware product and all other products developed and/or distributed by Acehub Vista Sdn. Bhd. are subject to the applicable License Agreement.
For further information, see the Courseware Product License Agreement.

## Slide 2: 7. Small-Signal Amplifier Theory

## Slide 3: Agenda
Basic amplifier concepts and small-signal amplifier
Amplifier characteristics
Basic amplifier block diagram and power gain expressions
Dependency of gain on amplifier parameters
Stability concepts and criteria
Stability circles and regions
Stability factors
Stabilization methods

## Slide 4: 1.0 Basic Amplifier Concepts

## Slide 5: General Amplifier Block Diagram
Input and output voltage relation of the amplifier
can be modeled simply as:
Vcc
PL
Pin
The active
component
vi(t)
vs(t)
vo(t)
DC supply
ZL
Vs
Zs
Amplifier
Input
Matching
Network
Output
Matching
Network
ii(t)
io(t)

## Slide 6: Amplifier Classification
Amplifiers can be categorized in two manners.
According to the signal level:
  Small-signal amplifier
  Power/Large-signal amplifier
According to the DC biasing scheme of the active component:
  Class A
  Class B
  Class AB
  Class C
There are also other classes, such as Class D (D stands for
digital), Class E, and Class F. These classes of amplifiers use the transistor/FET as a switch.
Our approach in this chapter

## Slide 7: Small-Signal vs Large-Signal Operation
ZL
Vs
Zs
Sinusoidal waveform
Usually a non-sinusoidal waveform
Large-signal:
Nonlinear
Small-signal:
Linear
vo(t)
vi(t)

## Slide 8: Small-Signal Amplifier (SSA)
All amplifiers are inherently nonlinear.
However, when the input signal is small, the input and output relationship of the amplifier is approximately linear.
This linear relationship also applies to current and power.
An amplifier that fulfills these conditions: (1) small-signal operation, (2) linear, is called a Small-Signal Amplifier (SSA). The SSA will be our focus.
If an SSA amplifier contains BJTs and FETs, these components can be replaced by their respective linear small-signal model. For instance, the hybrid-pi model for BJT.
When vi(t)0 (< 2.6 mV)
(1.1)
Linear relation

## Slide 9: Example 1.0: An RF Amplifier Schematic
ZL
Vs
Zs
Amplifier
Input
Matching
Network
Output
Matching
Network
DC supply
RF power flow

## Slide 10: Example 1.0 (cont’d)
Under AC and small-signal conditions, the BJT can be replaced with a linear hybrid-pi model:
Hybrid-pi equivalent circuit for the BJT

## Slide 11: Typical RF Amplifier Characteristics
To determine the performance of an amplifier, the following characteristics are typically observed.
  Power gain
  Bandwidth (operating frequency range)
  Noise figure
  Phase response
  Gain compression
  Dynamic range
  Harmonic distortion
  Intermodulation distortion
  Third-order intercept point (TOI)
Important to small-signal amplifiers
Important parameters of
large-signal amplifiers
(related to linearity)
Will elaborate in “High-Power Circuits”

## Slide 12: Power Gain
For amplifiers functioning at RF and microwave frequencies, usually of interest is the input and output power relation.
The ratio of output power over input power is called the Power Gain (G), usually expressed in dB.
There are a number of definitions for power gain as we will see shortly.
Furthermore, G is a function of frequency and the input signal level.
Power Gain
(1.2)

## Slide 13: Why Power Gain for RF and Microwave Circuits?
Power gain is preferred for high frequency amplifiers as the impedance encountered is usually low (due to the presence of parasitic capacitance).
For instance, if the amplifier is required to drive a 50 Ω load, the voltage across the load may be small, although the corresponding current may be large (there is current gain).
For amplifiers functioning at a lower frequency (such as the IF frequency), it is the voltage gain that is of interest, since the impedance encountered is usually higher (less parasitic).
For instance, if the output of an IF amplifier drives the demodulator circuits, which are usually digital systems, the impedance looking into the digital system is high and a large voltage can develop across it. Thus working with voltage gain is more convenient at IF frequencies.
Power = Voltage x Current

## Slide 14: Why Power Gain for RF and Microwave Circuits? (cont’d)
Instead of focusing on voltage or current gain, RF engineers focus on power gain.
By working with power gain, the RF designer is free from the constraints of system impedance. For instance in the simple receiver block diagram below, each block contributes some power gain. A large voltage signal can be obtained from the output of the final block by attaching a high impedance load to its output.
LO
IF Amp.
BPF
LNA
BPF
RF portion
(900 MHz)
IF portion
(45 MHz)
RF signal
power
1 W
15 W
IF signal
power
75 W
7.5 mW
400 Ω
t
v(t)
4.90 V
Band-pass
filter
Low-noise
amplifier
Local
oscillator

## Slide 15: Derivation of Input and Output Power Relationship for Small-Signal Operation
RL
Vs
Zs
Zin = R
= R
Assume that the input impedance
to the amplifier is transformed to
R at the operating frequency
For small-signal
operation
Po dBm
Pin dBm
10log(a12)
Slope of 1 Unit
Usually we express power in logarithmic scale, i.e., in dB or dBm scale.
Here the relation between the input and output power is in dB.
Extra
Power gain
in dB
Pin
Po
vo
vi

## Slide 16: Harmonic Distortion
ZL
Vs
Zs
When the input driving signal is
small, the amplifier is linear.
Harmonic components are
almost non-existent.
f
f1
harmonics
f
f1
2f1
3f1
4f1
0
Small-signal
operation
region
Pout dBm
Pin dBm

## Slide 17: Harmonic Distortion (cont’d)
ZL
Vs
Zs
When the input driving signal is
too large, the amplifier becomes
nonlinear. Significant harmonics
are introduced at the output.
Harmonics generation reduces the gain of the amplifier, as some of the output power at the fundamental frequency is shifted to higher harmonics. This results in gain compression.
f
f1
f
harmonics
f1
2f1
3f1
4f1
0
Pout dBm
Pin dBm

## Slide 18: Power Gain, Dynamic Range, and Gain Compression
Dynamic range (DR)
Input 1dB compression
Point (Pin_1dB)
Saturation
Device
burn
out
Ideal amplifier
1dB
Gain compression
occurs here
Noise Floor
–70
–60
–50
–40
–30
–20
–10
0
10
Pin
(dBm)
20
Pout
(dBm)
–20
–10
0
10
20
30
–30
–40
–50
–60
Power gain Gp = Pout(dBm) - Pin(dBm)
= -30–(–43) = 13 dB
Linear Region
Nonlinear
Region
Pin
Pout
Input and output at the same frequency

## Slide 19: Bandwidth
Power gain G versus frequency for small-signal amplifiers
f / Hz
0
G/dB
3 dB
Bandwidth
Extra
Po dBm
Pi dBm
Po dBm
Pi dBm
Can you explain
why the power gain
changes with frequency?
What are the physical
reasons for the positive
slope at the lower frequency and the negative slope at the higher frequency?

## Slide 20: Intermodulation Distortion (IMD)
ignored
f
f1
f2
|Vi|
These are unwanted components, caused by
the term 3vi3(t), which falls in the operating
bandwidth of the amplifier.
f
f1-f2
2f1-f2
2f2-f1
f2
f1
2f1
f1+f2
2f2
3f1
3f2
2f1+f2
2f2+f1
|Vo|
IMD
Operating bandwidth
of the amplifier
More will be said about this, later in the large-signal amplifier design.
Two signals, v1 and v2 with similar amplitude, frequencies f1 and f2 near each other
Usually specified in dB

## Slide 21: Noise Figure (F)
Vs
The amplifier also introduces noise into the output, in addition to the noise from the environment
Assume small-signal operation
Noise Figure (F)= SNRin/SNRout.
Since SNRin is always larger than SNRout, F > 1 for an amplifier which contributes noise.
More will be said about this, later in small-signal amplifier design.
SNR:
Signal to Noise
Ratio
Larger SNR
Smaller SNR
Zs
ZL
Noise

## Slide 22: Phase Response
Phase consideration is important for an amplifier working with wideband signals.
For a signal to be amplified with no distortion, two requirements are needed (from linear systems theory):
  The magnitude of the power gain transfer function must be a constant with respect to frequency f.
  The phase of the power gain transfer function must be a linear function of f.
A 2-Port
Network
H()
V1()
V2()
ZL
Transfer function

|H()|
Magnitude response
(related to power
gain)

()
Phase response
Extra
Bode
Plot

## Slide 23: Phase Response (cont’d)
A linear phase produces a constant time delay for all signal frequencies, and a nonlinear phase shift produces a different time delay for different frequencies.
Property (1.) means that all frequency components will be amplified by a similar amount; property (2.) implies that all frequency components will be delayed by similar amount.

()
Linear
phase response
ZL
A 2-Port
Network H()
V1(t)
V2(t)
t
V1(t)

()
Nonlinear
phase response
t
V2(t)
t
V2(t)
Extra

## Slide 24: 2.0 Small-Signal Amplifier Power Gain Expressions

## Slide 25: The Theory of Maximum Power Transfer
Zs
ZL
Vs
IL
VL
Time averaged power dissipated across the
load ZL:
Letting
We find that the value for RL and XL
that would maximize PL is
RL = Rs, XL = -Xs.
In other words: ZL = Zs*
To maximize the power transfer to the load impedance, ZL must be the complex conjugate of Zs, a notion known as Conjugate Matched.
where
Extra
Basic source-load network

## Slide 26: The Theory of Maximum Power Transfer (cont’d)
Extra
Zs
ZL = Zs*
Vs
PL = PA
Under conjugate match condition:
Zs
ZL  Zs*
Vs
PL
Under non-conjugate match condition:
PA
Preflect
We can consider the load power PL to
consist of the available power PA minus
the reflected power Preflect.
Available
Power
or
L

## Slide 27: Power Components in an Amplifier
ZL
Vs
Zs
Amplifier
Vs
Zs
ZL
Z1
Z2
VAmp
+
-
PAo
PL
PRo
PAs
PRs
Pin
Two basic source-
load networks
Approximate
linear circuit

## Slide 28: Power Gain Definition
From the power components, three types of power gain can be defined.
GP, GA, and GT can be expressed as the S-parameters of the amplifier and the reflection coefficients of the source and load networks. Refer to Appendix 1 for the derivation.
The effective power gain
(2.1a)
(2.1b)
(2.1c)

## Slide 29: Naming Convention
ZL
Vs
Zs
Amplifier
2-port
Network
1
2
Source
Network
Load
Network
s
L
In the spirit of high-frequency circuit design, where the frequency response of an amplifier is characterized by the S-parameters and the reflection coefficient is
used extensively instead of impedance, the power gain can be expressed in terms of these parameters.

## Slide 30: Summary of Important Power Gain Expressions and the Gain Dependency Diagram
Note:
All GT, GP, GA, 1, and 2
depend on the S-parameters.
(2.2a)
(2.2b)
(2.2c)
(2.2d)
(2.2e)
s
L
1
2
GA
GP
GT
The Gain Dependency Diagram

## Slide 31: Transducer Power Gain GT
GT is the relevant indicator of the amplifying capability of the amplifier.
Whenever we design an amplifier to a specific power gain, we refer to the transducer power gain GT.
GP and GA are usually used in the process of amplifier design or synthesis to meet a certain GT.
An amplifier can have a large GP or GA and yet a small GT, as illustrated in the next slide.

## Slide 32: Transducer Power Gain GT (cont’d)
Zs
ZL
Amplifier
with large
GP
PL
Pin
PAs
s 1  s*
GT =
Small
PL
PAs
Zs
ZL
Amplifier
with large
GP
Input
Matching
Network
Pin
Pin
1
s 1’ = s*
GT =
Large
Note that GP remains
unchanged in both
cases.

## Slide 33: Essence of Small-Signal Amplifier Design
In essence, designing (on a schematic level) a small-signal amplifier with transistor or monolithic microwave integrated circuit (MMIC) implies finding the suitable load and source impedance to be connected to the output and input port, so you get the required transducer power gain GT, bandwidth, and other characteristics.

## Slide 34: Unilateral Condition
In certain cases, when the operating frequency is low, |s12|  0, such a condition is known as a Unilateral condition.
Under the unilateral condition:
From (2.2d):
We see that the Transducer Power Gain GT consists of three parts that are independent of each other.
(2.3)
Gs
Go
GL
Extra

## Slide 35: Unilateral Condition (cont’d)
In a small-signal amplifier design for the unilateral condition, we can find the suitable source and load impedance for a required GT by optimizing Gs and GL independently, and this simplifies the design procedure.
However in most cases, s12 is typically not zero especially at frequencies above 1 GHz. Thus, we will not pursue design techniques for the unilateral condition.
Extra

## Slide 36: Example 2.0: Familiarization with the Gain Expressions
An RF amplifier has the following S-parameters at fo: s11=0.3 < –70o, s21=3.5 < 85o, s12=0.2 < –10o, s22=0.4 < –45o at 500 MHz. The system is shown below. Assuming the reference impedance (used for measuring the S-parameters) Zo=50 , find the following at 500 MHz:
  GT, GA, GP
  PL, PA, Pinc.
Amplifier
ZL=73 
40 
5 < 0o

## Slide 37: Example 2.0 (cont’d)
Step 1 – Find  s and L
Step 2 – Find 1 and 2
Step 3 – Find GT, GA, GP
Step 4 – Find PL, PA
Try to derive these two relations
Again, note that this is an analysis problem.

## Slide 38: 3.0 Stability Analysis of Small-Signal Amplifier

## Slide 39: Introduction
An amplifier is a circuit designed to enlarged electrical signals. For a certain input level (small-signal region), we would expect a certain output level, the ratio of which we call the gain of the amplifier.
An amplifier, or any two-ports circuits fulfilling the above condition is said to be stable, thus a stable system must fulfill the BIBO (Bounded input bounded output) condition.
On the contrary, an unstable circuit will produce an output that gradually increases over time. The output level will increase until the circuit saturates, with the output limited by non-linear effects within the circuit.
For most unstable circuits, the output will continue to increase even if the initial input is removed. In fact, an unstable amplifier can produce an output when there is no input. The amplifier becomes an oscillator instead!!!
Stability of an amplifier is affected by the load and source impedance connected to it’s two ports, and also by the frequency range.

## Slide 40: Introduction (cont’d)
An example of stable amplifier system.
Amp
In
Out
ZL
Zs
A pulse excitation
A sinusoidal excitation

## Slide 41: Introduction (cont’d)
An example of un-stable amplifier system, the input and output voltages as a function of time are shown.
Amp
In
Out
ZL
Zs
Initial input
A pulse excitation

## Slide 42: Introduction (cont’d)
Stability analysis can be carried out by many ways, for instance using what we learnt from Control Theory.
Stability analysis using Control Theory assumes the system can be simplified and modeled mathematically.
Usually under small-signal condition, the system is linear and Laplace Transformation can be applied. The system is thus cast into frequency domain.
A relationship between the input and output, called the Transfer Function can be obtained.
By analyzing the “poles” of the Transfer Function, the long-term behavior of the system can be predicted.

## Slide 43: Introduction (cont’d)
Stability analysis can also be performed empirically by considering a small-signal amplifier (since the initial signal that causes oscillation is always very small, for instance the noise in the circuit) with a set of source (Zs) and load (ZL) impedance. The amplifier circuit is then excited by a small ‘seed’ signal, and checked for oscillation. The source and load impedance are then varied, and the process is repeated.
An amplifier that do not oscillate for ALL passive Zs and ZL (even short and open circuit) is called an Unconditionally Stable circuit.
A Conditionally Stable amplifier will oscillate for certain passive Zs and ZL. While an Un-stable amplifier will oscillate for all impedances.
An unstable or marginally stable amplifier can be made more stable.

## Slide 44: Introduction (cont’d)
A third approach, since we are considering high frequency electrical systems with sinusoidal signals, is to consider the dynamics of voltage and current waves propagating at the ports of the amplifier system.
The amplifier is considered as connected to the Source and Load networks via transmission lines. As the system is powered up, the Source network launches an initial sinusoidal voltage/current wave into the input port of the amplifier.
A series of multiple reflections then follows, leading to steady-state condition. Here we will adopt this approach to show the criteria for AC stability in terms of reflection coefficients.
ZL
Zc
Zc
Zs
Vs
Output port (2)
Input port (1)

## Slide 45: Stability Concept: Perspective of Oscillation from Wave Propagation
An incident wave V+ propagating towards port 1 will suffer multiple reflections.
If |s1|>1, then the magnitude of the incident wave towards port 1 will increase indefinitely, leading to oscillation.
Z1 or 1
bs
bs1
bss 1
bss 12
bss 212
bss 213
Source
2-port
network
Zs or s
Port 1
Port 2
Only if
A geometric series
bss 313
bss 314
a1
b1

## Slide 46: Stability Concept (cont’d)
Thus oscillation will occur when | s1 | > 1.
The source network is usually passive, |s | < 1. Thus, for instability to occur, |1 | > 1 — this condition represents the potential for oscillation.
Similar arguments can be applied to port 2, and we see that the condition for oscillation is |2 | > 1.
Since the input and output power of a 2-port network are related, when either port is stable, the other will also be stable.
Port 1:
Port 2:

## Slide 47: Perspective of Oscillation from Circuit Theory
Source Network
Port 1
Rs
jXs
R1
jX1
Zs
Z1
V
(3.1)
Extra

## Slide 48: Perspective of Oscillation from Circuit Theory (cont’d)
Using Laplace transformation:
For a system to oscillate, the denominator of the equation must
have conjugate poles at the frequency o where oscillation occurs;
this means:
As will be shown, this requirement is similar to |s1|=1
This fact will be used in a
later chapter to create an
oscillating circuit.
(3.2a)
(3.2b)
(3.2c)
Extra

## Slide 49: Similarity Between Both Perspectives
From:
Extra

## Slide 50: Similarity Between Both Perspectives (cont’d)
We see that when R1+Rs|o= 0, X1+Xs|o=0 :
  |1s|o = 1
And when R1+Rs|o<0, X1+Xs|o= 0 we have |1s|o > 1
The above requirement also applies to port 2, in which case when R2+RL|o=0, X2+XL|o=0
  |2L|o = 1
And when R2+RL|o<0, X2+XL|o= 0 we have |2L|o > 1
Extra

## Slide 51: Important Summary on Oscillation
Assuming that |s | and |L | are always < 1 for passive components, we can conclude the following:
For a 2-port network to be stable, it is necessary that the load and source impedance are chosen in such a way that |1 | < 1and |2 | < 1.
To prevent oscillation:
The range of frequency of interest

## Slide 52: Stability Criteria for Amplifier
2-port
Network
1
2
Source
Network
Load
Network
s
L
As shown previously, for stability |1 | < 1 and |2 | < 1.
Using (2.2a), this can be expressed as:
(3.3a)
(3.3b)

## Slide 53: 3.1 Stability Circles

## Slide 54: Load Stability Circle (LSC)
Setting |1 | =1, we can determine all the corresponding values of L . The L happens to fall on the locus of a circle on the Smith chart.
Load stability circle
Center of circle
Radius of circle
(3.4)
Re L
Im L
RL
CL
0

## Slide 55: Source Stability Circle (SSC)
Setting |2 | =1, we can determine all the corresponding values of s . The s also happens to fall on the locus of a circle on the Smith chart.
Source stability circle
Center of circle
Radius of circle
(3.5)
Re s
Im s
Rs
Cs
0

## Slide 56: Stable Regions
The source and load stability circles only indicate the value of s and L where |2 | = 1 and |1 | = 1. We need more information to show the stable regions for the s and L plane on the Smith chart.
Example: for LSC, when L = 0, |1 | = |s11| (see (2.2a)).
Assume LSC does not encircle the s11= 0 point. If |s11| < 1 then L = 0 is a stable point; otherwise, if |s11| > 1 then L=0 is an unstable point.
LSC
|s11|<1
Stable
Region
LSC
|s11|>1
L plane

## Slide 57: Stable Region (cont’d)
Now let the LSC encircle the s11= 0 point. Similarly if |s11| < 1 then L = 0 is an stable point; otherwise, if |s11| > 1 then L= 0 is an unstable point.
This argument can also be applied for SSC, where we consider |s22| instead, and the Smith chart corresponds to the s plane.
LSC
|s11|<1
LSC
|s11|>1
Stable
Region
L plane

## Slide 58: Summary for Stability Regions
For both Source and Load reflection coefficients (s and L ) :
LSC or SSC
|s11| or |s22| <1
LSC or SSC
|s11| or |s22| >1
LSC or SSC
|s11| or |s22| <1
LSC or SSC
|s11| or |s22| >1
Stability circles do not
enclose the origin
Stability circles
enclose the origin
Stable
Region

## Slide 59: Unconditionally Stable Amplifier
There are times when the amplifier is stable for all passive source and load impedance.
In this case, the amplifier is said to be unconditionally stable.
Assuming |s11| < 1 and |s22| < 1, the stability region would look like this:
LSC
|s11|<1
L can occupy any point in the Smith chart
SSC
|s22|<1
s can occupy any point in the Smith chart

## Slide 60: Example 3.1
Use the S-parameters of the amplifier in example 2.1; draw the load and source stability circles and find the stability region.
SSC
LSC
Hint:
Apply equations
(3.4) and (3.5) to
find the center
and the radius of
the circles.

## Slide 61: Example 3.1 (cont’d)
Computation using the
MATHCAD® software

## Slide 62: Example 3.1 (cont’d)

## Slide 63: 3.2 Test for Unconditional Stability: The Stability Factor

## Slide 64: Stability Factor
Sometimes it is not convenient to plot the stability circles, or we just want a quick check whether an amplifier is unconditionally stable or not.
In such conditions we can compute the Stability Factor of the amplifier.
Rollette* has contributed a factor, the K-factor that tells us whether or not an amplifier (or any linear 2-port network) is unconditionally stable based on its S-parameters at a certain frequency.

## Slide 65: Stability Factor (cont’d)
The condition for a 2-port network to be unconditionally stable is shown below:
Otherwise the amplifier is conditional stable or unstable at all (it is an oscillator!).
K is also known as the Rollette Stability Factor.
(3.6)
Note that the K-factor only tells us if an amplifier (or any linear 2-port network) is unconditionally stable. It does not indicate the relative stability of the two amplifiers that fail the test. A newer test, called the  factor allows the comparison of two conditionally stable amplifiers (see Appendix 2).

## Slide 66: What if the Amplifier is Unstable, or the Stable Region is Too Small?
Use negative feedback to reduce the amplifier gain.
Redesign the DC biasing; find a new operating point (or Q point) that will result in a more stable amplifier.
Add some resistive loss to the circuit to improve stability.
Use a new component with better stability.

## Slide 67: 3.3 Stabilization of an Amplifier

## Slide 68: Introduction
The main reason why amplifiers become unstable is feedback (e.g. part of the output energy is put back into the input).
One possible feedback path is the parasitic capacitance Cb’c between the Base and Collector terminals of the transistor (the same can be said for FET). This is compounded by the Miller Effect ([4], [5]) if the transistor is used in CE configuration.
This usually results in elevated magnitude of s12 parameter as frequency increases (as seen in equation (3.6) the K value decreases if |s12| increases).
Classically the effect Cb’c can be cancelled by using a suitable inductor across B and C terminals, in a process called Neutralization*.
Another approach is to add dissipation loss at the input and output of the amplifier, this approach that will be elaborated in this section.
For instance see J.R. Smith, “Modern communication circuits”, 1998, McGraw-Hill, or P.H. Young, “Electronic
communication techniques”, 2004, Prentice Hall.

## Slide 69: Stabilization Methods
|1 | > 1 and |2 | > 1 can be written in terms of input and output impedances:
This implies that Re[Z1] < 0 or Re[Z2] < 0.
Therefore, one way to stabilize an amplifier is to add a series resistance or shunt conductance to the port. This should make the real part of the impedance become positive.
In other words, we deliberately add loss to the network.

## Slide 70: Stabilization Methods (cont’d)
2-port
Network
Z1
Source
Network
Load
Network
Z1+R1’
R1’
R2’
Z2
Z1+R1’
2-port
Network
Y1
Source
Network
Load
Network
Y1+G1’
G1’
G2’
Y2
Y2+G2’

## Slide 71: Effect of Adding Series Resistance on the Smith Chart
Suppose we have an impedance ZL and a load stability circle (LSC). Assume the LSC touches the R=10 circle. By inserting a series resistance of 10 Ω, we can limit ZL’ to the stable region on the Smith chart.
Z’ =
ZL+ 10
10 Ω
ZL
LSC
R = 10
circle
Stable
Region
Unstable
Region

## Slide 72: Effect of Adding Shunt Resistance on the Smith Chart
Suppose we have an admittance YL and a load stability circle (LSC). Assume the LSC touches the G=0.002 circle. By inserting a shunt resistance of 500 Ω, we can limit YL’ to the stable region on the Smith chart.
Y’ =
YL+ 1/500
500 Ω
YL
LSC
G = 0.002
circle
Unstable
Region
Stable
Region

## Slide 73: Summary for Stability Check of Single-Stage Amplifier
Set the frequency range
and design the DC biasing
Get the S-parameters within the frequency range
K-factor > 1
and |D| < 1 ?
Amplifier is unconditionally
stable
Yes
Draw the SSC and LSC
No
Find |s11| and |s22|
Circles intersect
the Smith chart?
Amplifier is conditionally stable; find the stable regions
Yes
No
Amplifier is
not stable
Start
End
Perform stabilization
Redesign the DC biasing
Choose a new transistor

## Slide 74: Chapter Summary
We have learnt the important concepts of small-signal amplifier and amplifier characteristics.
We have derived the three types of power gain expressions for an amplifier using S-parameters.
We also studied how the various gains depend on either s and L (the dependency diagram).
We have looked at the concept of oscillation and how it applies to stability analysis.
We have learnt about stability circles and how to find the stable region for source and load impedances.
We have learnt about the Rolette Stability Factor test (K) for unconditionally stable amplifiers.
We have learnt about elementary stabilization methods.

## Slide 75: Example 3.3: S-Parameters Measurement and Stability Analysis Using ADS Software

## Slide 76: Example 3.3: Stability Test
Plotting K and D versus frequency
(from 50 MHz to 1.0 GHz):
This is the frequency that
we are interested in
Amplifier is
conditionally
stable

## Slide 77: Example 3.3: Viewing S11 and S22 at f=600 MHz and Plotting Stability Circles
Since |s11| < 1 @ 600 MHz
Since |s22| < 1 @ 600 MHz

## Slide 78: Appendix 1: Derivation of Small-Signal Amplifier Power Gain Expressions

## Slide 79: Derivation of Amplifier Gain Expressions in Terms of S-Parameters
When the electrical signals in the amplifier are small, the active component (BJT) can be considered as linear.
Thus, the amplifier is a linear 2-port network. The S-parameters can be obtained and it is modeled by an S matrix.
The preceding gains GP , GA , GT can be expressed in terms of s , L , and s11, s12, s21, s22.
Input
Output
Vcc
Rb1
Rb2
Re
Cc1
Cc2
L1
L2
L3
Cd
L4

## Slide 80: Derivation of Gain Expression (1)
Source
2-port
Network
bs
b1
a1
bs
bs1
bss 1
bss 12
bss 212
bss 213
or

## Slide 81: Derivation of Gain Expression (2)
2-port
Network
1
2
Source
Network
Load
Network
s
L
b1
a1
b2
a2
From:
and
One obtains:
In a similar manner, we
can also obtain:

## Slide 82: Derivation of Gain Expression (3)
Finding the transducer power gain GT:
From slide DGE (1)
Only for
available gain

## Slide 83: Derivation of Gain Expression (4)
Finding the transducer power gain GT (continued):
Using
From slide DGE (2)
From slide
DGE (1)

## Slide 84: Derivation of Gain Expression (5)
The available power gain GA can be obtained from GT when  L = 2*, since
We have…

## Slide 85: Derivation of Gain Expression (6)
Finding the power gain GP :
From slide DGE (2)

## Slide 86: Appendix 2: The  Stability Test

## Slide 87: The  Stability Test
The Roulette Stability Test consists of two separate tests (the K and D values).
This makes it difficult to compare the relative stability of two conditionally stable amplifiers.
A later development combines the two tests into one, known as the  factor. A larger value indicates greater stability.
For an amplifier to be unconditionally stable, it is necessary that:
[Source: Edwards, M. L., and J. H. Sinsky, “A New Criterion for Linear Two-Port Stability Using a Single Geometrically Derived Parameter”, IEEE Trans. on Microwave Theory and Techniques, Dec 1992.]

## Slide 88: References
[1]* D.M. Pozar, “Microwave Engineering”, 3rd Edition, 2005 John-Wiley & Sons.
[2] R.E. Collin, “Foundations for Microwave Engineering”, 2nd Edition, 1992 McGraw-Hill.
[3] R. Ludwig, P. Bretchko, “RF Circuit Design: Theory and Applications”, 2000 Prentice-Hall.
[4]* G. Gonzalez, “Microwave Transistor Amplifiers: Analysis and Design”, 2nd Edition 1997, Prentice-Hall.
[5] G. D. Vendelin, A. M. Pavio, U. L. Rhode, “Microwave Circuit Design Using Linear and Nonlinear Techniques”, 1990 John-Wiley & Sons. A more updated version of this book, published in May 1992 is also available.
[6]* Gilmore R., Besser L., “Practical RF Circuit Design for Modern Wireless Systems”, Vol. 1 and 2, 2003, Artech House.
*Recommended