## Slide 1: Persistent memory
It’s finally here! What do I do with it?
Alexandra (Sasha) Fedorova
MongoDB and University of British Columbia

## Slide 2: Outline
What is persistent memory?
How much does it cost?
How do I use it?
How does it perform?
What are the implications for databases?

## Slide 3: Persistent memory
Memory that retains the data even after a power loss.
A.K.A.:
  NVRAM – non-volatile RAM
  NVDIMM – non-volatile dual inline memory modules
  PMM – persistent memory modules
Can be built using many different technologies
  PCM – phase change memory
  STT-RAM – spin-torque transfer RAM
  ReRAM – resistive memory
  3D XPoint technology

## Slide 5
This talk: Intel Optane™ DC Persistent memory
Developed together with Micron
Previously known as 3D XPoint

## Slide 6: Intel Optane™ DC Persistent memory
Released April 2, 2019
Optane™ (3D XPoint): new NVRAM technology
  Faster than NAND Flash

## Slide 7: Intel Optane™ DC Persistent memory
Cascade Lake
Memory controller
PCIe
controller
memory bus
PCI bus

## Slide 8: Intel Optane™ DC Persistent memory
Cascade Lake
Up to 6 PMMs
PMM: persistent memory module
128GB-512GB each
A single CPU can support up to
6 PMMs
Up to a total of:
6 x 512GB = 3TB persistent memory

## Slide 9: Outline
What is persistent memory?
How much does it cost?
How do I use it?
How does it perform?
What are the implications for databases?

## Slide 10: You can order it!
compsource.com
Anandtech.com
$15/GB
$13/GB
$31/GB
Comparing equivalently-sized DRAM modules
(smaller modules are much cheaper)

## Slide 11
I got persistent memory. Let’s figure out what to do with it!

## Slide 12: Memory mode
Optane memory is NOT persistent
DRAM acts as a cache (direct-mapped)
CPU memory controller manages the cache transparently
CPU/OS see a larger memory pool
non-persistent

## Slide 13: App-direct
Persistent mode
Sits side-by-side with DRAM
persistent

## Slide 14: What does ”persistent” mean?
If the data reaches the memory controller it will survive a power failure
Memory controller
memory bus
CPU cache
Survives power failure
Data gets lost
If the data sits in the CPU cache, it won’t.
  Need to explicitly flush it using special instructions.

## Slide 15: PM is exposed as a regular device
Persistent memory shows us as a PMEM device
  /dev/pmem0, dev/pmem1, etc…
You can mount a file system onto it

## Slide 16: You Can Emulate PM in the Linux Kernel
$ sudo emacs -nw /etc/default/grub
$ sudo grub-mkconfig -o /boot/grub/grub.cfg
GRUB_DEFAULT=0
GRUB_TIMEOUT_STYLE=hidden
GRUB_TIMEOUT=2
GRUB_DISTRIBUTOR=`lsb_release -i -s 2> /dev/null || echo Debian`
GRUB_CMDLINE_LINUX_DEFAULT=""
GRUB_CMDLINE_LINUX="memmap=16G!12G
Add this line to your GRUB file.

## Slide 17: File system support
ext4 and xfs have been modified to support PMEM
They use Direct-Access Mode (DAX), bypassing the buffer cache
Mount the file system on /dev/pmemX with the direct access (DAX) option
  # mkdir /mnt/pmem
  # mkfs.ext4 /dev/pmem0
  # mount -o dax /dev/pmem0 /mnt/pmem

## Slide 18: Support in Linux 4.3
PMEM – persistent memory device
DAX – file system support

## Slide 19: The interface to persistent memory
Management Path
  Configure / check persistent memory
Storage path
  File system manages the persistent memory
  Access using POSIX file interface
Memory path:
  Mmap interface
  Load/store instructions
    Intel’s PMDK (persistent memory development kit) provides malloc/free interface.

## Slide 20
Source: pmem.io PMDK introduction
pmem.io
Storage path
Memory path

## Slide 21: How to program?
EASY: Just use a file system interface
  PROS: No changes to the application
  CONS: Has overhead, must use file system interface (POSIX API)
HARD: Convert the application to use persistent memory
  PROS: Can persist all kind of state and recover faster
  CONS: Need to keep track of persistent memory allocations and use transactions / logging

## Slide 22: Intel PMDK
Persistent Memory Development Kit
For C/C++
Basic access to persistent memory
Persistent pointers
Transactions and Logging

## Slide 23: Examples:
Example 1: Use PM via a memory-mapped file
Example 2: Use a persistent object store
Example 3: Use transactions

## Slide 24: Example 1: Use PM via a memory-mapped file
Source: pmdk.io

## Slide 25: Example 1: Use PM via a memory-mapped file
Source: pmdk.io
Calling mmap() directly will work just fine – the main advantage of pmem_map() is that it tries to find an address where mapping is likely to use large page mappings, for better performance when using large ranges of pmem.

## Slide 26: Example 1: Use PM via a memory-mapped file
Source: pmdk.io
Just like regular memory!
Is the string persistent after strcpy on line 80?
We don’t know!
  Could be in the CPU cache (all or part of it), not on storage media
  Some parts could have been pushed to the media as part of cache eviction
  Instructions like ’SFENCE’ don’t work – they are for write visibility among threads.
MUST EXPLICITLY FLUSH MEMORY!

## Slide 27: Example 1: Use PM via a memory-mapped file
Flushing memory to persistence:
This is just a wrapper around msync() that ensures that the arguments are aligned.
OK to use msync()directly.
pmem_persist() will, if possible, perform the flush directly from user space, without calling into the OS. This is made possible on the Intel platform using instructions like CLWB and CLFLUSHOPT.
OK to use msync()instead.
OK to use CLWB and CLFLUSHOPT directly.
Source: pmdk.io

## Slide 28: Example 1: Use PM via a memory-mapped file
Copying persistent memory
Optimized for copying to pmem. On the Intel platform, this is done using the non-temporal store instructions which bypass the processor caches.
Using memcpy will also work.
Source: pmdk.io

## Slide 29: Examples:
Example 1: Use PM via a memory-mapped file
Example 2: Use a persistent object store
Example 3: Use transactions

## Slide 30: libpmemobj
persistent pointers and a way to atomically manipulate them

## Slide 31: Example 2: Use a persistent object store
Source: pmdk.io
Transactional objects live in persistent memory pool
It’s just a file that holds data structures
Here is how you create one
Just a file name
Permissions, same as for creat().
Application defined string. Identifies an expected file format, e.g., MY_LIST.
Can be null.
Creating a persistent memory pool

## Slide 32: Root Object
Entry point for all persistent objects allocated using the API.
There is exactly one root object per pool.
Create or resize the root object.
PMEM object ID (OID).
NOT A DIRECT POINTER!
OBTAIN A DIRECT POINTER!
Source: pmdk.io
Example 2: Use a persistent object store

## Slide 33: Writing an object
Source: pmdk.io
Read data into a regular memory buffer
Set and persist the object size
pmemobj_persist:
Write changes to media.
Not transactional. Some changes could have been flushed earlier.
Copy the data and persist to media.
pmemobj_memcpy_persist:
Copies and persists the changes.
Not transactional.
Your could crash here and end up with inconsistent state.
Example 2: Use a persistent object store

## Slide 34: Read the object from a different process
Open with the same name and LAYOUT_NAME as specified at creation time.
Get the root object and the direct pointer.
Read as you would a regular pointer.
Example 2: Use a persistent object store

## Slide 35: Examples:
Example 1: Use PM via a memory-mapped file
Example 2: Use a persistent object store
Example 3: Use transactions

## Slide 36: Example 3: Use transactions
Set and persist the object size
Copy the data and persist to media.
Your could crash here and end up with inconsistent state.
We will use transactions to solve this!

## Slide 37
Example 3: Use transactions
<REQUIRED>
[OPTIONAL]

## Slide 38
Example 3: Use transactions
Crash here and get into bad state
Problematic example:
Solve it with transactions:
“takes a “snapshot” of the memory block of given size, located at given offset off in the object specified by oid, and saves it to the undo log. The application is then free to directly modify the object in that memory range. In case of a failure or abort, all the changes within this range will be rolled back”

## Slide 39: Properties of transactions in PMDK
Crash consistency
  If you crash in the middle or abort, NONE of the changes are reflected in persistent memory.
Not atomic with respect to other threads (no isolation)
  Other threads immediately see the changes in memory.
A few questions:
  What happens if only some of the changes are persisted on commit?
  Is there a recovery procedure?
  Where is the log stored (in PM?)? If so, what’s the overhead of logging?
Example 3: Use transactions

## Slide 40
DON’T TRY THIS AT HOME!

## Slide 41: Outline
What is persistent memory?
How much does it cost?
How do I use it?
How does it perform?
What are the implications for databases?

## Slide 42: Read latency vs DRAM*
Local DRAM
Remote DRAM
Source: Basic Performance Measurements of the Intel Optane DC Persistent Memory Module arXiv:1903.05714v2
*Measured on individual reads, no caching, no prefetching
Same machine, different NUMA node
PM gives us sub-microsecond latencies.
PM is ~2-3x slower than DRAM
The difference between sequential and random is ~2x
Take-away #1:
169 ns
305 ns

## Slide 43: Write latency vs DRAM
PM-Optane: 94ns
DRAM: 86ns
How it was measured:
  Issue a write followed by a cache flush instruction and a fence
  Not guaranteed to reach the media, but reaches the processor’s ADR (Asynchronous DRAM refresh domain).
Source: Basic Performance Measurements of the Intel Optane DC Persistent Memory Module arXiv:1903.05714v2
Individual writes comparable to DRAM.
Because the write returns after we reach the memory controller
Take-away #2:

## Slide 44: Sequential Read/Write Bandwidth vs DRAM
Local DRAM
Remote DRAM
~40 GB/s for reads, ~14 GB/s for writes.
Source: Basic Performance Measurements of the Intel Optane DC Persistent Memory Module arXiv:1903.05714v2
* On six interleaved Optane DIMMs
Reading PM is as fast as reading DRAM on a remote NUMA node!

## Slide 45: Random Read/Write Bandwidth (One Thread)
Source: Basic Performance Measurements of the Intel Optane DC Persistent Memory Module arXiv:1903.05714v2
Non-interleaved region on a single DIMM
One thread
2-3x difference between sequential and random bandwidth with a single thread for both reads and writes
2.8 GB/s
1.5 GB/s
(Sequential: 5 GB/s)
(Sequential: 5.5 GB/s)

## Slide 46: Sequential vs Random BW with 16 Threads
Reads:
  Sequential bw: 40 GB/s
  Random bw: 11 GB/s
Writes:
  Sequential bw: 10 GB/s
  Random bw: 5 GB/s
For SSDs: ~10x difference between sequential and random bandwidth
Source: Lies, Damn Lies And SSD Benchmark Test Result, Seagate.
Source: Basic Performance Measurements of the Intel Optane DC Persistent Memory Module arXiv:1903.05714v2
4x difference
2x difference
On Optane PM the performance difference between sequential and random accesses is 2-4x
Take-away #3:

## Slide 47: Latency of file operations
No clear advantage of using Optane PM for individual file operations with small data transfers
Software overhead and/or caching effects dominate
Take-away #4:
Source: Basic Performance Measurements of the Intel Optane DC Persistent Memory Module arXiv:1903.05714v2
Chart: microseconds
| Read-4K | Write-4K | Append-4K | Write-512B | Create
Ext4 | 0.852 | 3.907 | 4.746 | 1.378 | 16.554
Ext4-DAX | 1.632 | 1.97 | 8.604 | 1.039 | 15.301
NOVA | 1.396 | 4.506 | 3.146 | 5.191 | 10.831
Ext4-SSD-Optane | 0.853 | 4.313 | 5.326 | 1.368 | 15.257
Unmodified
Direct access to media. No buffer cache.
NVM-optimized file system from academia.
SSD with Optane technology

## Slide 48: Throughput of file operations: Reads
Raw bandwidth (16 threads) was:
~39 GB/s for sequential reads
~11 GB/s for random reads
Source: Basic Performance Measurements of the Intel Optane DC Persistent Memory Module arXiv:1903.05714v2
Chart: Bandwidth (GB/s)
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0
PM-Optane-Ext4 | 1.1553 | 1.959 | 3.9102 | 6.4248 | 9.1465
PM-Optane-Ext4-DAX | 1.625 | 2.8828 | 5.4873 | 9.3379 | 11.2
PM-Optane-NOVA | 1.5947 | 3.1084 | 5.4971 | 9.91 | 16.8
SSD-Optane-Ext4 | 0.28809 | 0.56152 | 1.0264 | 1.7686 | 2.252
Random 4K reads (1-16 threads)
Chart: Bandwidth (GB/s)
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0
PM-Optane-Ext4 | 1.3252 | 2.499 | 4.623 | 7.5078 | 9.1592
PM-Optane-Ext4-DAX | 1.8984 | 3.3672 | 6.6533 | 10.8 | 11.2
PM-Optane-NOVA | 2.0586 | 4.4541 | 8.6162 | 15.9 | 28.2
SSD-Optane-Ext4 | 2.0381 | 2.2656 | 2.3516 | 2.4443 | 2.5059
Sequential 4K reads (1-16 threads)
5x

## Slide 49: Throughput of file operations: Writes
Chart: Bandwidth (GB/s)
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0
PM-Optane-Ext4 | 0.36816 | 0.64453 | 1.085 | 1.5605 | 1.5938
PM-Optane-Ext4-DAX | 0.82715 | 1.4336 | 2.0156 | 2.501 | 2.04
PM-Optane-NOVA | 0.7373 | 1.416 | 2.5674 | 4.4355 | 6.127
SSD-Optane-Ext4 | 0.15918 | 0.24414 | 0.44727 | 0.66016 | 0.61914
Random 4K writes (1-16 threads)
Chart: Bandwidth (GB/s)
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0
PM-Optane-Ext4 | 0.2998 | 0.53809 | 0.86426 | 0.99219 | 0.24121
PM-Optane-Ext4-DAX | 0.76953 | 1.3145 | 1.7324 | 1.6113 | 0.25488
PM-Optane-NOVA | 0.74512 | 1.5195 | 2.7842 | 5.2451 | 8.8457
SSD-Optane-Ext4 | 0.11914 | 0.21387 | 0.33984 | 0.37598 | 0.2168
Sequential 4K writes (1-16 threads)
Raw bandwidth (16 threads) was:
~10 GB/s for sequential writes
~5 GB/s for random writes

## Slide 50: Take-away #4
Using PM-Optane as storage gives up to ~5x more throughput when equivalent technology is sitting in an SSD.
Software bottlenecks become pronounced.

## Slide 51: Outline
What is persistent memory?
How much does it cost?
How do I use it?
How does it perform?
What are the implications for databases?

## Slide 52: Implications (overview)
PM is faster than SSD, so software overheads are more noticeable
  Implication: may have to retune performance
Difference between random and sequential is not that big
  Hint: you don’t need to organize your data structures for sequential access
Bandwidth is much larger than that of a disk (65K I/O queues)
  Question: how do you feed that bandwidth?
Atomicity unit is much smaller than disk (e.g., 256 bytes)
  Implication: Might affect software correctness

## Slide 53: Do we care about being sequential?
* hypothetical application
total execution time
Random Sequential
SSD
Random Sequential
PM-Optane
I/O overhead
Software overhead
2-4x difference
Persistent memory:
I/O time becomes much smaller
Software overhead remains
10x difference
Difference between sequential and random may become much less important
I/O much faster
Much larger software overheads

## Slide 54: Don’t organize your data for sequential writes
Many systems sort their data for writing to achieve sequential writes
This generates CPU overhead!
Cut this out!
Jian Xu and Steven Swanson, University of California, San Diego, NOVA: A Log-structured File System for Hybrid Volatile/Non-volatile Main Memories, USENIX FAST 2016
B. Leper, O. Balmau, K. Gupta, W. Zwaenepoel, KVell: the Design and Implementation of a Fast Persistent Key-Value Store, SOSP 2019

## Slide 55: Use multiple logs
Historically: single log, because
  You want sequential writes
  Mechanical disks have only one head
  Don’t care about or want concurrency
Persistent memory:
  Very large bandwidth and many I/O queues
  Sequential performance is still better than random, but
  Software overhead becomes more noticeable
Benefits of multiple logs
  Utilize the bandwidth (need to feed multiple queues)
  Achieve high concurrency (remove software overhead)
Jian Xu and Steven Swanson, University of California, San Diego, NOVA: A Log-structured File System for Hybrid Volatile/Non-volatile Main Memories, USENIX FAST 2016

## Slide 56: Implement log as a linked list
Bad idea for disks:
  We lose sequential access property
Better for persistent memory
  Easier to allocate space
  Easier to clean the log -- can do one page at a time
  Easier to reclaim stale log pages
Jian Xu and Steven Swanson, University of California, San Diego, NOVA: A Log-structured File System for Hybrid Volatile/Non-volatile Main Memories, USENIX FAST 2016

## Slide 57: Get rid of block interface?
Databases use block interface
  Read from and write to disk in units of entire pages (e.g., 8KB)
  For NVRAM: huge write amplification
Ideas from research community
  Re-write the storage engine to use byte interface
Caveats (Keith Bostic, co-creator of WiredTiger):
  Huge engineering effort
  Staying away from block interface is not easy: compression/encryption.

## Slide 58: Best practices of NVRAM adoption
Redesigning data structures for persistent memory is very hard
Fast path for adoption: use PM as a fast storage device
Avoid kernel overhead of file system access:
  Use memory mapped files with DAX.
  Flush with user-level instructions: pmem_persist, not msync.
  Pre-allocate files to avoid journaling overhead when files grow piecemeal.
  Use large pages (ext4 does this).
Jian Xu et al., Finding and Fixing Performance Pathologies in Persistent Memory Software Stacks , ASPLOS 2019

## Slide 59: Summary
Persistent memory is here
It is about 2x cheaper than DRAM*
It is only 2-3x slower than DRAM
It is up to 5x faster than SSD for throughput-oriented workloads
The difference in performance between sequential and random accesses is a lot smaller than SSD
Software overheads are more pronounced than on SSD
Interesting implications for storage systems

## Slide 60: Backup slides

## Slide 61: Example 1: Use PM via a memory-mapped file
Flushing persistent memory
pmem_flush() = pmemp_persist() + pmem_drain()
Send data to hardware
Wait for hardware buffers to drain until data reaches the media.
Does nothing (empty function) on Intel platforms!
Source: pmdk.io

## Slide 62: Example 1: Use PM via a memory-mapped file
Separating flush and drain steps
Source: pmdk.io

## Slide 63: NOVA
Log structured, but only the metadata is written into the log
  An alternative is journaling, but journaling writes the data twice
  Hence, less write amplification than journaling.
  Data is written directly into the media, and shadow paging is used for atomicity
Each inode has its own log
  Concurrency, better bandwidth utilization
Log is implemented as a linked list
  Easier and faster to clean
Jian Xu and Steven Swanson, University of California, San Diego, NOVA: A Log-structured File System for Hybrid Volatile/Non-volatile Main Memories, USENIX FAST 2016

## Slide 64: Wear leveling
Like SSDs performs wear-leveling
  Internal address translation
Bad block management