## Slide 1: Scheduling: How could such a simple thing could possibly be so complicated?
CPEN 331, UBC
Alexandra Fedorova

## Slide 2
System software and hardware
time
Core 0
Core 1
Core 2
Core 3
HARDWARE
SOFTWARE
Scheduling runqueue
Tasks (threads)
timeslice
timeslice

## Slide 3
System software and hardware
time
Core 0
Core 1
Core 2
Core 3
HARDWARE
SOFTWARE
Scheduling runqueue
Tasks (threads)
timeslice
timeslice
context switch time
Time to switch from one thread to another
=
Can context switch take a long time?
How to determine the “right” length for the timeslice?
How do we pick the next thread from the scheduling queue?

## Slide 4
Linus Torvalds
“The scheduler simply isn’t that important.” Linus Torvalds, 2001
“And you have to realize that there are not very many things that have aged as well as the scheduler. Which is just another proof that scheduling is easy.”
Linus Torvalds, 2001

## Slide 5: By year 2000, scheduling was a solved problem…
We figured out what the timeslice should be
  Multi-Level Feedback Queues (MLFQ) algorithm
  Give a larger timeslice to non-iteractive programs, but let them run less often
  Give a smaller timeslice to interactive programs, but let them run more often
We also figure out how to set thread priorities
… and then came year 2000

## Slide 6: What happened in year 2000?
The dot-com boom
Everyone is using the Internet
Unix runs on servers, desktops and cell phones
Very different applications
  Servers vs video streaming vs data analysis
Machine are increasingly shared by multiple applications
A single scheduling algorithm does not fit different application styles…
… but wait, then came 2004

## Slide 7
Gordon Moore
Robert Dennard
Transistor density doubles every 18 months: we can put more and more transistors on the chip
Power density remains constant as we put more and more transistors on the chip

## Slide 8: End of Dennard scaling
We can still put more cores on the chip
But we can’t run them faster
And we don’t get better performance with more transistors

## Slide 9: All hail the multicore era!

## Slide 10
System software and hardware
time
Core 0
Core 1
Core 2
Core 3
HARDWARE
SOFTWARE
Scheduling runqueue
timeslice
timeslice
ALL CORES ACCESS A SINGLE RUNQUEUE
Can you think of any problems with that?
Multiple runqueues
Can you think of any problems with that?

## Slide 11
System software and hardware
time
Core 0
Core 1
Core 2
Core 3
HARDWARE
SOFTWARE
Scheduling runqueue
Tasks (threads)
timeslice
timeslice
context switch time
Does it matter on which core to run a thread?
cache
cache
cache
cache
shared cache
shared cache
Threads running on cores that share a cache may compete for the cache and various hardware queues.
Or they may share data in caches!
A thread processing network packets is better off running close to the network card

## Slide 12: Contention for shared resources
Core 0
Core 1
Core 2
Core 3
cache
cache
cache
cache
shared cache
shared cache
Threads
soplex
sphinx
namd
gamess
Experiment 1: run each application alone on the machine
measure the running time
measure the running time
measure the running time
measure the running time
solo running time
Run #2
Run #1
Run #3
Run #4

## Slide 13: Contention for shared resources
Core 0
Core 1
Core 2
Core 3
cache
cache
cache
cache
shared cache
shared cache
Threads
soplex
sphinx
namd
gamess
Experiment 2: run threads together, co-scheduled in different ways
Run #2
Run #1
Run #3
measure the running time for each application
measure the running time for each application
measure the running time for each application
Contended running time
BEST co-schedule: lowest average runtime for all apps.
WORST co-schedule: highest average runtime for all apps.

## Slide 14: How much slowdown in co-scheduled runs?
BEST co-schedule: lowest average runtime for all apps.
WORST co-schedule: highest average runtime for all apps.
How much slower the app runs when contending compared to running alone

## Slide 15: Which cores run your threads really matters!

## Slide 16: In the meantime… the rebirth of NUMA
Non-Uniform Memory Access architecture
Was invented in 1990s
Rebirth in the multicore world around 2007

## Slide 17: A NUMA System
node
A CPU core
(caches not shown)
main memory
NUMA: Non-Uniform Memory Access latency
Multiple nodes connected via an interconnect
interconnect

## Slide 18: How do NUMA systems make scheduling more complicated?

## Slide 19
threads
data
~300 cycles
no delays
~200 cycles
no delays
Thread placement on NUMA systems

## Slide 20: Does remote latency hurt performance? Let’s run an experiment!
Experiment 1: all data is local
Experiment 2: all data is remote

## Slide 21: How much worse do we run when all data is remote?
<20% performance impact
How much worse we run when all data is remote
The scheduler must place threads close to their data!

## Slide 22
But wait, it gets even worse!

## Slide 23
threads
data
Memory latency gets to ~1000 cycles
under bad congestion!
Interconnect congestion
popular data
ALL THREADS ACCESS THIS DATA!
MEMORY CONTROLLER CONGESTION
INTERCONNECT CONGESTION

## Slide 24: Congestion kills performance
How much slower we run when there is congestion relative to when there is none
The scheduler must place threads and data to avoid congestion!

## Slide 25: What I told you so far…
Scheduling is conceptually simple
It was simple to implement prior to 2000
Internet boom forced systems a wider variety of applications and made multi-program and multiuser servers more common
Multicore revolution placed new challenges on software performance
The rebirth of NUMA hardware added even more challenges
A scheduler can do a lot to avoid these problems
So, naturally, people started hacking the scheduler
Let’s see what happened and what we learned…